## Slide 1: ECC CEPT PT1 Upper 6 GHz Issue for IEEE 802.11
Date: 31 July 2025
Authors:
Name | Company | Address | Phone | Email
Rich Kennedy | self |  |  | rkennedy1000@gmail.com

## Slide 2: The Issue: Adjacent Band Coexistence between MFCN Base Station in U6 and WAS/RLAN in L6
ECC PT1 deals with IMT matters
  “ECC Project Team 1 (ECC PT1) is responsible for mobile (IMT) issues, including compatibility studies, development of band plans, and development and review of ECC deliverables”
Correspondence Group MFCN in U6GHz vs incumbents meeting to resolve sharing issues
  The ECC is studying the Upper 6 GHz band as a shared band
The addition of IMT to the upper 6 GHz band can also create issues in the adjacent band
  Base stations operating at the low end of the upper 6 GHz band could render the high end of the lower 6 GHz band unusable - would eliminate one of only three 160 MHz channels
Qualcomm study suggests a guard band is not necessary
  Document number: CG-MFCN6GHz(25)INFO006 (see the Input document folder for the June 10-11, 2025 meeting)
  Is this opinion shared by the Wi-Fi industry?
IEEE 802.18 should take the lead on this matter
  Many other regulatory domains could adopt this EU position
Notes: 2

## Slide 3: The Shrinking Lower 6 GHz Band
The bottom 20 MHz not available in the EU to protect the Communication Based Train Control (CBTC) systems in the adjacent band (below 5935 MHz)
  Lower 6 GHz band limited to 480 MHz (5945 MHz to 6425 MHz)
Channels in the next 160 MHz must be de-prioritized to minimize OOBE into CBTC
  Limited access in 5945 MHz to 6105 MHz
Potential interference at the top end from MFCN base stations in the upper 6 GHz band
  ECC PT1 CG MFCN U6GHz discussing the need for a guard band
Notes: 3

## Slide 4: Upcoming Meetings
ECC PT1 CG#6 MFCN U6GHz vs incumbents - 26-28 August, Milan, Italy
ECC PT1 – 15-19 September 2025, Vilnius, Lithuania