## Slide 1: P802.19.1 Assumptions and Architecture
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2009-01-28
Authors:
Name | Company | Address | Phone | email
Chen Sun | NICT | 3-4, Hikarino-oka, Yokosuka, Kanagawa, Japan, 239-0847 |  | sun@nict.go.jp
Ha Nguyen Tran |  |  |  | 
M. Aziz Rahman |  |  |  | 
Stanislav Filin |  |  |  | 
Yohannes D. Alemseged |  |  |  | 
Gabriel Villardi |  |  |  | 
Hiroshi Harada |  |  |  | 

## Slide 2: Abstract
Reference
  This contribution is based on contributions IEEE 802.19-10/4r0 and IEEE 802.19-10/7r1
Assumptions
  To define the operation environment of 802.19.1
Architecture
  Logical entities
  Interfaces
Summary

## Slide 3: Assumptions
1 If TVBD network or device is aware of its location, it could be also aware of its operational environment, for example, its service coverage area, interference coverage area, and sensing coverage area.

## Slide 4: Assumptions
2 If TVBD network or device has spectrum sensing capability, at least two levels of spectrum sensing are considered:
  TVBD network can detect presence of a signal in a channel, but cannot distinguish whether this signal is from a primary or secondary user
  TVBD network can detect presence of a signal in a channel and in some cases can distinguish whether this signal is from a primary or secondary user.
3 Not all TVBD networks or devices will use P802.19.1 coexistence methods
  Explanatory note: In other words, there will be some TVBD networks that will operate autonomously without caring for any other TVBD networks. This can happen even if P802.19.1 provides considerable advantages to the TVBD networks following its coexistence protocol.
4 If TVBD network detects a signal in a TV channel and does not identify it as a primary signal, then the TVBD network assumes that this TV channel is allowed for secondary usage.
  Explanatory note: If there is a non-802.19.1 compliant secondary user in a TV channel, those 802.19.1-compliant users can use this TV channel.

## Slide 5: Assumptions
5 If the interfaces between TWBD network or device and TVWS database is available, 802.19.1 logical entity can obtain information through this interface. Otherwise, 802.19.1 can use its own interface (defined by 802.19.1 or provided by TVWS database provider) to access TVWS database.

## Slide 6: Assumptions
6 TVBD networks that require coexistence do not always have capability to communicate directly with each other by using MAC and PHY protocols of their air interfaces.
7 If TVBD network or device has backhaul connection (e.g., IP-based wired connection), then this connection can be used to provide transport means for TVWS coexistence.

## Slide 7: Assumptions
8 The implementation of 802.19.1 does not assume modifications on the PHY and MAC of existing and upcoming standards of TVBD networks or devices.

## Slide 8
The architecture defines three groups of interfaces and three logical entities
  Interface between 802.19.1 entities (A)
  Interface between an 802.19.1 entity and TVWS network or device (B)
  Interface between an 802.19.1 entity and the TVWS database (C)
  Coexistence enabler (CE)
  Coexistence database (CDB)
  Coexistence management server (CMS)
IEEE 802.19.1 Architecture
Coexistence
Enabler A
Coexistence
Enabler B
TVBD
Network/Device
TVWS
Database
Coexistence
Database
TVBD
Network/Device
IEEE 802.19.1 interface
IEEE 802.19.1 logical entity
A4
B
B
A1
A2
C1
A3
Coexistence
Management
Server
C2

## Slide 9: Logical entities
802.19.1 logical entity
  An IEEE 802.19.1 logical entity is defined by its functional role(s) and interfaces with other IEEE 802.19.1 logical entities. It doesn’t need to be of material existence. The three types of logical entities defined are coexistence enabler (CE), coexistence management server (CMS) and coexistence database (CDB).
Coexistence enabler
  Interact with TVDB networks or devices
    Acquire information from TVBD network or device
    Send commands and messages to TVBD network or device
  Coexistence decision making
    Within the coexistence policy, suggestions and guidelines received from Coexistence Management Server (if any)
    Mainly used for autonomous decision making (decentralized deployment option)
  Provides information to Coexistence Database, for example, information obtained from TVBD network or device
  Exchanges information with other Coexistence Enablers

## Slide 10: Logical entities
Coexistence management server
  Coexistence decision making
    Mainly used for centralized deployment option
  Coexistence policy making, which provides coexistence policy , suggestions and guidelines to Coexistence Enablers
  Interact with TVWS database
    Acquire information from the TVWS database for coexistence purpose
Coexistence database
  Store information required for TVWS coexistence, e.g., registration information of TVBD networks and devices, spectrum usage information, sensing related information etc.
  Preliminary data processing function such as information sorting, indexing, acquiring, etc.
  Provide information to Coexistence Management Server
  Provide information to Coexistence Enablers
  Interact with TVWS database
    Acquire information from the TVWS database for coexistence purpose

## Slide 11: Interfaces
802.19.1 defines three groups of interfaces. Different interfaces in each group are distinguished by their usage, types of information exchanged, and underlying protocols.
  Interface between 802.19.1 entities (A)
  Interface between an 802.19.1 entity and TVWS network/devices (B)
  Interface between an 802.19.1 entity and the TVWS database (C)
Interface between 802.19.1 entities (A)
  (A1) CMS-CDB-interface
    This interface is used by CMS to obtain information required for coexistence decision making and coexistence policy making from CDB
  (A2) CE-CMS-interface
    This interface is used by the CE to obtain coexistence policy and regulation, as well as information from the TVWS database that has been obtained by the CMS.
  (A3) CE-CDB-interface
    This interface is used by CEs to register their TVBD networks or devices for coexistence and to obtain information of other registered TVBD networks or devices. Also, this interface is used by CEs to provide information obtained from their TVBD networks or devices to CDB. Also, this interface is used by the CE to obtain information inside the TVWS database that has been obtained by the CDB.
  (A4) CE-CE-interface
    This interface is used to exchange information between two CEs for making coexistence decision.

## Slide 12: Interfaces
Interface between an 802.19.1 entity and TVWS network or device (B)
  This interface is used for the flow of information between an 802.19.1 logical entity and TVWS network or device. This information includes information from TVWS network or device and commands for reconfiguration to TVWS network or device.
Interface between an 802.19.1 entity and the TVWS database (C)
  (C1) CMS-TVWS database
    This interface is used by CMS to obtain information from the TVWS database
  (C2) CDB-TVWS database
    This interface is used by CDB to obtain information from the TVWS database

## Slide 13: Summary
The assumptions given (based on contribution IEEE 802.19-10/4r0) describe the foreseeable operation environment where 802.19.1 is expected to be deployed.
The proposed architecture (based on contribution IEEE 802.19-10/7r1) is comprised of three logical entities and three groups of interfaces
We believe that proposed architecture is consistent with architectures proposed in contributions IEEE 802.19-10/13r0 presented by Mika Kasslin and IEEE 802.19-10/16r0 by Joe Kwak.