IEEE P802.19
TV Whitespace Coexistence Methods

| Comment Resolutions regarding to final index of 25 |
| --- |
| Date: 2012-05-15 |
| Author(s): |
| Name | Company | Address | Phone | Email |
| Donghun Lee | ETRI | 138 Gajeong-Ro, Yuseong-Gu, Daejeon, 305-700, South Korea | +82-42-860-0865 | mmdang@etri.re.kr |
| Hyunduk Kang | ETRI | 138 Gajeong-Ro, Yuseong-Gu, Daejeon, 305-700, South Korea | +82-42-860-1074 | henry@etri.re.kr |
| Byung-Jang Jeong | ETRI | 138 Gajeong-Ro, Yuseong-Gu, Daejeon, 305-700, South Korea | +82-42-860-6765 | bjjeong@etri.re.kr |

| Final index | Clause | Subclause | Page | Line | Type | Comment | Proposed change |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 25 | 4 | 4.2.2.3 | 22 | 4 | T | The confirmation primitive for registration is necessary to confirm the registration of corresponding WSO. The current draft, howerver, missed the primitive between CE and WSO | Add the confirmation primitive |

Discussion:

Final index 25 pointed out that the confirmation primitive for registration is necessary. Then, we propose adding confirmation primitive in 4.2.2.3.4

Proposal (Revision part is marked by blue color)

4.2.2.3.4 GetRegInfo.confirm

This primitve is used by a CE to confirm the registration to the WSO.

The sematics of the primitive are:

GetRegInfo.confirm ( )

This primitve is generated by the CE to confirm the registration to the WSO.

# Text boxes

Abstract

This document provides proposed resolutions for comment 25 received in the 802.19.1 LB.