IEEE P802.19
TV Whitespace Coexistence Methods

| Comment Resolutions regarding to final index of 41 |
| --- |
| Date: 2012-05-15 |
| Author(s): |
| Name | Company | Address | Phone | Email |
| Donghun Lee | ETRI | 138 Gajeong-Ro, Yuseong-Gu, Daejeon, 305-700, South Korea | +82-42-860-0865 | mmdang@etri.re.kr |
| Hyunduk Kang | ETRI | 138 Gajeong-Ro, Yuseong-Gu, Daejeon, 305-700, South Korea | +82-42-860-1074 | henry@etri.re.kr |
| Byung-Jang Jeong | ETRI | 138 Gajeong-Ro, Yuseong-Gu, Daejeon, 305-700, South Korea | +82-42-860-6765 | bjjeong@etri.re.kr |

| Final index | Clause | Subclause | Page | Line | Type | Comment | Proposed change |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 41 | 4 | 4.2.2.4.5 | 26,27 | 15,3 | T | The data type of listOfAllowedTVWSChNumber is sequence. However, the data types of availableStartTime and availableDuration is not sequence | Revise the data types with Sequence of GeneralizedTime and Sequence of REAL, respectively |

Discussion:

Final index 41 pointed out that the data types of availableStartTime and availableDuration are wrong. Then, our proposal is given as follows

Proposal (Revision part is marked by blue color)

4.2.2.4.5 AvailableChannelList.response

Table 18 –AvailableChannelList.response primitive parameters

| Name | Data type | Description |
| --- | --- | --- |
| AvalableChannelList | AvailableChannelList | Available channel list to operate in TVWS |
| listOfAvailableStartTime | Sequence of GeneralizedTime optional | Start time of availablitity of a channel |
| listOfAvailableDuration | Sequence of REAL optional | Duration of availablity |
| listOfAllowedTVWSChNumber | ListOfAllowedTVWSChNumber optional | Allowed TVWS channel number list |
| listOfConstOfChUses | Sequence of ConstOfChUses optional | Channel user constraint |

# Text boxes

Abstract

This document provides proposed resolutions for comment 41 received in the 802.19.1 LB.