IEEE P802.19
TV Whitespace Coexistence Methods

| Comment Resolutions regarding to final index of 121 |
| --- |
| Date: 2012-05-15 |
| Author(s): |
| Name | Company | Address | Phone | Email |
| Donghun Lee | ETRI | 138 Gajeong-Ro, Yuseong-Gu, Daejeon, 305-700, South Korea | +82-42-860-0865 | mmdang@etri.re.kr |
| Hyunduk Kang | ETRI | 138 Gajeong-Ro, Yuseong-Gu, Daejeon, 305-700, South Korea | +82-42-860-1074 | henry@etri.re.kr |
| Byung-Jang Jeong | ETRI | 138 Gajeong-Ro, Yuseong-Gu, Daejeon, 305-700, South Korea | +82-42-860-6765 | bjjeong@etri.re.kr |

| Final index | Clause | Subclause | Page | Line | Type | Comment | Proposed change |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 121 | 5 | 5.3 | 63 | 19,38 |  | The data type of listOfAllowedTVWSChNumber is sequence. However, the data types of availableStartTime and availableDuration is not sequence | Revise the data types with Sequence of GeneralizedTime and Sequence of REAL, respectively |

Discussion:

Final index 121 pointed out that the data types of availableStartTime and availableDuration are wrong. Then, our proposal is given as follows

Proposal (Revision is marked by blue color)

5.3 Messages

AvailableChannelResponse::=SEQUENCE{

--Allowed TVWS channel number list

listOfAllowedTVWSChNumber	 ListOfAllowedTVWSChNumber OPTIONAL,

listOfAvailableStartTime		Sequence of GeneralizedTime  OPTIONAL,

listOfAvailableDuration		Sequence of REAL OPTIONAL,

--Channel user constraint

listOfconstOfChUses		Sequence of ConstOfChUses OPTIONAL,

…

}

# Text boxes

Abstract

This document provides proposed resolutions for comment 121 received in the 802.19.1 LB.