IEEE P802.19
Wireless Coexistence

| Proposal on adding new procedures for requesting and obtaining measurement procedures |
| --- |
| Date: 2012-07-18 |
| Author(s): |
| Name | Company | Address | Phone | Email |
| Hyunduk Kang | ETRI | 138 Gajeong-Ro, Yuseong-Gu, Daejeon, 305-700, South Korea |  | henry@etri.re.kr |
| Donghun Lee | ETRI | 138 Gajeong-Ro, Yuseong-Gu, Daejeon, 305-700, South Korea |  | mmdang@etri.re.kr |
| Byung-Jang Jeong | ETRI | 138 Gajeong-Ro, Yuseong-Gu, Daejeon, 305-700, South Korea |  | bjjeong@etri.re.kr |

Discussion

The current draft DF2.08 defines requesting and obtaining measurement by the CM to obtain measurement results from the WSO. The CM may collect measurement results from WSOs to manage coexistence among WSOs.

Measurement results from WSOs are important information to both WSOs and the coexistence system because through measurement results it is possible to estimate channel status including blind WSOs that are not registered to the coexistence system.

WSOs might have various measurement capabilities such as energy detection, feature detection, and so on. We expect that information service case, one WSO may take advantage of measurement capability of its coexistence set element. For example, if the WSO is only capable of energy detection but it requires more detailed measurement result, the WSO may use measurement result obtained from its coexistence set element which is capable of feature detection.

Considering the above, it is necessary that the WSO issues request for measurement result from other WSO to the coexistence system.

Propose

1. Add the following sub-clauses after 5.2.8.3 Obtaining scheduled measurement procedure in DF2.08:

      - Requesting measurement results to the CM

The WSO shall perform this procedure, illustrated in Figure 1, when it needs to obtain measurement result from one or multiple coexistence set elements of the WSO via the CM. The WSO shall take advantage of measurement capability of its coexistence set elements.

If the CM receives PerformMeasurement_Request message from the CE it may perform the procedure defined in clause 5.2.8.1 to request measurement results from the corresponding one or multiple coexistence set elements of the WSOs.

PerformMeasurement.request primitive and its data type are defined in clause 4.2.2.5 Measurement service and 4.3.2 COEX_MEDIA_SAP. PerformMeasurementRequest and PerformMeasurementConfirm messages and its data type are defined in clause 5.3 Messages and 5.4 Data types.

Figure 1・Requesting measurement results to the CM

      - Obtaining measurement results from the CM

Given that the CM receives PerformMeasurement_Request message from the CE defined in clause 5.2.8.4, the CM shall perform this procedure, illustrated in Figure 2, when it ready to send measurement result obtained from one or multiple coexistence set elements of the WSO.

PerformMeasurement.response primitive and its data type are defined in clause 4.2.2.5 Measurement service and 4.3.2 COEX_MEDIA_SAP. PerformMeasurementResponse and PerformMeasurementConfirm messages and its data type are defined in clause 5.3 Messages and 5.4 Data types.

Figure 2・Obtaining measurement results from the CM

2. Add the following primitives and messages marked by red color in DF2.08

        - GetRegInfo.response

GetRegInfo.response 	(

…

measurementCapability

)

Table 14— GetRegInfo.response primitive parameters

| Name | Data type | Description |
| --- | --- | --- |
| … | … | … |
| measurementCapability | MeasurementCapability | Measurement capability of this WSO |

        - NewRegInfo.indication

NewRegInfo.indication 	(

…

measurementCapability

)

Table 15— NewRegInfo.indication primitive parameters

| Name | Data type | Description |
| --- | --- | --- |
| … | … | … |
| measurementCapability | MeasurementCapability | Measurement capability of this WSO |

        - PerformMeasurement.request

This primitive is used by a WSO to request measurements.

The semantics of this primitive are:

PerformMeasurement.request 	(

listOfChNumber,

measDef	i,

…

)

The primitive parameter is defined in Table 27.

Table 27— PerformMeasurement.request primitive parameter

| Name | Data type | Description |
| --- | --- | --- |
| listOfChNum | ListOfChNum | List of channel number |
| measDefi | MeasDefi | Measurement definition |

This primitive is generated by a WSO to request measurements.

        - PerformMeasurement.response

This primitive is used by a CE to provide measurement results to the WSO.

The semantics of this primitive are:

PerformMeasurement.response	(

measurementReport

)

The primitive parameter is defined in Table 28.

Table 28— PerofrmMeasurement.response primitive parameter

| Name | Data type | Description |
| --- | --- | --- |
| measurementReport | MeasurementReport | Measurement report |

When the WSO receives this primitive, it examines the received measurement results.

    - COEX_MEDIA_SAP

MeasurementCapability :: =	ENUMERATED	{

energyDetection,

featureDetection,

…

}

MeasDescr ::= ENUMERATED {

…

interferenceLevel

}

ReqInfoValue ::= CHOICE {

…

InterferenceLevelValue		REAL

}

ListOfChNumber ::= SEQUENCE OF INTEGER

MeasDefi ::= SEQUENCE OF MeasDefiElement

MeasDefiElement := ENUMERATED {

interferenceLevel

primaryDetection,

wsoDetection,

…

}

MeasValue :: = SEQUENCE OF MeasValueElement

MeasValueElement :: =  CHOICE {

interferenceLevelValue			REAL,

primaryDetection			BOOLEAN,

wsoDetection				BOOLEAN,

…

}

MeasurementReport ::= SEQUENCE {

listOfChNumber	ListOfChNumber,

measDefi		MeasDefi,

measValue 		MeasValue

}

  - Messages

CE_Registration_Request ::= SEQUENCE {

…

measurementCapability		MeasurementCapability

}

CM_Registration_Request ::= SEQUENCE {

…

measurementCapability		MeasurementCapability

}

PerformMeasurement_Request ::= SEQUENCE {

listOfChNumber		ListOfChNumber,

measDefi		MeasDefi

}

PerformMeasurement_Response ::= SEQUENCE {

measurementReport	MeasurementReport

}

PerformMeasurement_Confirm ::= SEQUENCE {

}

  - Data types

MeasurementCapability :: =	ENUMERATED	{

energyDetection,

featureDetection,

…

}

MeasurementDescription ::= SEQUENCE OF SEQUENCE {

measDescr 	ENUMERATED { …

interferenceLevel},

measFreq 	MeasFreq

}

MeasurementResult ::= SEQUENCE OF SEQUENCE {

reqInfoDescr ReqInfoDescr,

reqInfoValue 	CHOICE {…

interferenceLevelValue REAL}

}

ListOfChNumber ::= SEQUENCE OF INTEGER

MeasDefi ::= SEQUENCE OF MeasDefiElement

MeasDefiElement := ENUMERATED {

interferenceLevel

primaryDetection,

wsoDetection,

…

}

MeasValue :: = SEQUENCE OF MeasValueElement

MeasValueElement :: =  CHOICE {

interferenceLevelValue		REAL,

primaryDetection		BOOLEAN,

wsoDetection			BOOLEAN,

…

}

MeasurementReport ::= SEQUENCE {

listOfChNumber	ListOfChNumber,

measDefi		MeasDefi,

measValue 		MeasValue

}