## Slide 1: Coexistence Discovery
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2012-11-13
Authors:

## Slide 2: Abstract
This presentation contains a proposal of coexistence discovery mechanism which is somewhat different from the current one in the DF3.02 draft

## Slide 3: Introduction
This presentation illustrates the steps to be taken in the 802.19.1 coexistence system to determine which WSOs may interfere with each other
  As the result there will be a coexistence set for each CE registered to the system
The proposal is to modify the scheme currently specified in the 802.19.1 draft to
  Keep WSO geo-location information within CM which serves the CE representing the WSO
  Allow implementation of different type and level of propagation models as part of the discovery scheme

## Slide 4: The approach in nutshell
A CE provides information about a WSO to a CM
The CM determines at least one area for the WSO which is represented by the CE and provides the area(s) to a CDIS
  The CDIS stores for each CE the WSO area(s), CE identifier and CM contact information
The CDIS finds out with which areas of other WSOs the area(s) of the new WSO overlap and provides information about those other WSOs to the CM
  The CM receives a list of CEs and contact information of CMs which serve those CEs
The CM contacts the other CMs to find out whether their CEs represent WSOs which really may interfere with each other
At the end the CM has the coexistence set for the CE from which it received information in step 1

## Slide 5: MSC view of the approach
CM1
CM2
CE
CDIS
I represent this WSO
Determine WSO area(s)
I serve this CE which
has this WSO area(s)
These CEs have overlapping
WSO area(s) and they are
served by these CMs
Determine WSO related locations for which you ask info from another CM
Estimate signal level in the indicated locations
What is estimated signal level in these locations from WSO represented by this CE you serve?
These are signal level estimates
Decide whether the CE for which you received signal level estimates belongs to the coexistence set
Area overlap analysis

## Slide 6: Step 1: Parameters given by a CE to a CM
No changes to this communication needed with respect to the latest draft

## Slide 7: Step 2: CM determines WSO area(s)
CM1
CM2
CE
CDIS
I represent this WSO
Determine WSO area(s)
I serve this CE which
has this WSO area(s)
These CEs have overlapping
WSO area(s) and they are
served by these CMs
Determine WSO related locations for which you ask info from another CM
Estimate signal level in the indicated locations
What is estimated signal level in these locations from WSO represented by this CE you serve?
These are signal level estimates
Decide whether the CE for which you received signal level estimates belongs to the coexistence set
Area overlap analysis

## Slide 8: Step 2: CM determines WSO area(s) (cont.)
The CM determines simple approximation (a rectangle) of communication and (one or more) interference areas of the WSO
The rectangle(s) shall include the whole estimated communication/ interference areas and informed as 2 points; the south-west and north-east corners
The CM shall provide the areas to the CDIS
  Other information provded includes tolerable interference level and supported frequencies
North
East

## Slide 9: Step 3: CDIS analysis WSO areas
CM1
CM2
CE
CDIS
I represent this WSO
Determine WSO area(s)
I serve this CE which
has this WSO area(s)
These CEs have overlapping
WSO area(s) and they are
served by these CMs
Determine WSO related locations for which you ask info from another CM
Estimate signal level in the indicated locations
What is estimated signal level in these locations from WSO represented by this CE you serve?
These are signal level estimates
Decide whether the CE for which you received signal level estimates belongs to the coexistence set
Area overlap analysis

## Slide 10: Step 3: CDIS analysis WSO areas (cont.)
The CDIS finds out which WSO areas which it has available overlap with the newly registered one(s)
  Some conditions may be set to the overlap analysis
The CDIS provides to the CM a list of CEs have overlapping WSO area(s) and information about CMs which serve these CEs
  The CDIS may provide also information about the highest interference level in the border of communication area or the overlap percentage of interference area on the communication area

## Slide 11: Step 4a: Reality check with another CM
CM1
CM2
CE
CDIS
I represent this WSO
Determine WSO area(s)
I serve this CE which
has this WSO area(s)
These CEs have overlapping
WSO area(s) and they are
served by these CMs
Determine WSO related locations for which you ask info from another CM
Estimate signal level in the indicated locations
What is estimated signal level in these locations from WSO represented by this CE you serve?
These are signal level estimates
Decide whether the CE for which you received signal level estimates belongs to the coexistence set
Area overlap analysis

## Slide 12: Step 4a: Reality check with another CM (cont.)
The CM determines at least one location related to the WSO represented by the CE for which it is determining coexistence set
  More on the locations in the next slide
The CM shall issue the following question to the other CM
  What is the field strength/power level in these locations caused by a WSO represented by this CE you serve?

## Slide 13: Step 4a: Reality check with another CM (cont.)
Case in which the WSO is a single transceiver
The CM needs to find out whether the WSO (green triangle) can be interfered by another WSO which has been identified as a potential coexistence set element by CDIS. The CM determines one or more locations (red dots) which represent the WSO. One location (i.e. WSO’s actual location) is given if one can release actual loation of the WSO to another CM. Multiple locations are given if the CM is not willing to release actual location of the WSO to another CM. The locations should be selected so that the requesting CM can determine from the response which contains transmission signal level estimates to the locations whether there is interference to the WSO which is in this case a single transcevier.
Case in which the WSO is a network operated by a master (green triangle) to which variable number of slave devices in unknown locations are connected with coverage area of the network (blue oval)
The CM determines multiple locations which represent the master device and possible slave devices of the network. The CM needs to estimate coverage area of the network from which it can estimate possible and probable locations of slave devices. In general, the location should be again selected so that the requesting CM can determine from the response which contains transmission signal level estimates to the locations whether there is interference to the WSO which is in this case a master device and a set of slave devices.

## Slide 14: Step 4b: Reality check with another CM
CM1
CM2
CE
CDIS
I represent this WSO
Determine WSO area(s)
I serve this CE which
has this WSO area(s)
These CEs have overlapping
WSO area(s) and they are
served by these CMs
Determine WSO related locations for which you ask info from another CM
Estimate signal level in the indicated locations
What is estimated signal level in these locations from WSO represented by this CE you serve?
These are signal level estimates
Decide whether the CE for which you received signal level estimates belongs to the coexistence set
Area overlap analysis

## Slide 15: Step 4b: Reality check with another CM (cont.)
The responding CM estimates maximum signal strength from a WSO which is represented by the CE indicated in the request in a set of locations
  More on the estimation in the next slide
Once the responding CM has the answers available it shall issue the following answer to the requesting CM
  Maximum field strength/power level in these locations caused by a WSO represented by this CE I serve is as follows

## Slide 16: Step 4b: Reality check with another CM (cont.)
Case in which the WSO is a single transceiver
The responding CM needs to estimate maximum transmission signal level from the WSO (green triangle) it serves and for which it has received a signal level estimation request from another CM. Since the WSO in this case is a single transceiver with known location, the CM needs to just estimate maximum signal level of transmission from the WSO in a set of locations indicated in the request. The CM can use any type and kind of propagation model it has to estimate the signal levels. The more realistic model it has available the more accurate the estimation.
Case in which the WSO is a network
The responding CM needs to estimate transmission signal levels from the WSO it serves and for which it has received a signal level estimation request from another CM. Since the WSO in this case is a network operated by a master device with known location and a variable number of slave devices, the CM needs to estimate what is the maximum signal level of transmission from any potential location of slave devices within coverage area of the WSO in the locations indicated in the request and indicates the highest level for each indicated location.
The CM can use any type and kind of propagation model it has to estimate the signal levels. The more realistic model it has available the more accurate the estimation.
Propagation loss
Max Tx power
Max signal level per location
Propagation loss
Max Tx power
Max signal level per location

## Slide 17: Step 5: Decision on inclusion to coexistence set
CM1
CM2
CE
CDIS
I represent this WSO
Determine WSO area(s)
I serve this CE which
has this WSO area(s)
These CEs have overlapping
WSO area(s) and they are
served by these CMs
Determine WSO related locations for which you ask info from another CM
Estimate signal level in the indicated locations
What is estimated signal level in these locations from WSO represented by this CE you serve?
These are signal level estimates
Decide whether the CE for which you received signal level estimates belongs to the coexistence set
Area overlap analysis

## Slide 18: Step 5: Decision on coexistence set element (cont.)
Once the requesting CM has received a response from the responding CM it shall decide on whether the CE for which it received signal level estimate response belongs to the coexistence set or not
  The decision logic could be left open
  This should be very straightforward decision based on interference tolerance and estimated signal level

## Slide 19: Summary
We have presented a coexistence discovery scheme which doesn’t force a CM to release geo-location of a WSO to CDIS or to any other entity
The proposed scheme comprises of five steps which involve mainly CM and CDIS in the discovery
The proposed scheme provides means for a CM to use different type of signal propagation models to determine whether two WSO transceivers are interfers or not
  The standard should facilitate and encourage use of advanced, realistic and accurate propagation models