## Slide 1: Overview of IEEE 802.19.1
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2013-01-14
Authors:

## Slide 2: Introduction
This presentation contains a high level introduction to IEEE 802.19.1 coexistence system as per the latest draft
The presentation has been prepared for a joint meeting between IEEE 802.19 WG and IEEE 802.15 TG4m

## Slide 3: IEEE 802.19.1 system overview
Coexistence enabler (CE)
  Interface element that represents a white space object in the coexistence system
Coexistence manager (CM)
  Provides coexistence information and management services
Coexistence Discovery and Information Server (CDIS)
  Provides coexistence discovery service for CMs
External entities
  TVWS DB – channel availability for secondary use
  White Space Object (WSO) – a TV band device or network of TV band devices
Coexistence system facilitates coexistence of secondary users in TVWS

## Slide 4: Service view
Coexistence system provides management and information services to WSOs
  A WSO is represented by a CE that is connected to the WSO
  These services are provided by a CM to which the CE is connected, registered and authenticated
  A CE/WSO subscribed to the management service is managed by the coex system and it receives reconfiguration commands from the CM
  A CE/WSO subscribed to the information service receives information for its own decision making on resources; information includes data about WSOs which may interfere with or may be interfered by the WSO
CDIS provides coexistence discovery service to CMs
  CM becomes aware of those WSOs which may interfere with or may be interfered by the WSO that is represented by a CE registered to the CM

## Slide 5: Interfaces
All three B-interfaces (B1, B2, B3) shall use TCP/IP
The entities (CE, CM, CDIS) shall support both the SSH and TLS in all three B-interfaces
In the interface C to the TWVS DB the IETF PAWS protocols are used
The interface A (WSO-CE) is specified as a logical interface

## Slide 6: Summary
IEEE 802.19 TG1 is in the process of developing a standard that specifies radio technology independent methods for coexistence among dissimilar TV Band Devices (TVBDs) and dissimilar or independently operated networks of TVBDs
The IEEE 802.19.1 system comprises of three types of logical entities and three interfaces to interconnect the entities
  TCP/IP shall be used in all three inter-entity interfaces
The IEEE 802.19.1 system allows for a WSO (device or a network) to make its own decisions and get information for the decision making. This is called information service.
The IEEE 802.19.1 system also allows for a WSO (device or a network) to use the system to make coexistence decisions for the WSO. This is called management service.