## Slide 1: Coexistence Lessons Learned
November 2014
Paul Nikolich, IEEE 802
Slide <number>
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.19.
Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard." Early disclosure to the TAG of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication. Please notify the Chair <shellhammer@ieee.org> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.19 TAG. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.
Date: 2014-11-01
Authors:
Notes:         Steve Shellhammer, Qualcomm
Page <number>

## Slide 2: Abstract
This document is intended to be presented to 3GPP, in response to a request from 3GPP to IEEE 802 on the Coexistence Lessons Learned within IEEE 802
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 3: IEEE 802 Documents
References are made to both IEEE 802 standards and 802 working documents
IEEE 802 standards are available for free, 6 months after publication, under the IEEE Get program at:
  http://standards.ieee.org/about/get/
IEEE 802 working documents (except draft standards) are available on the IEEE 802 Mentor web site
  https://mentor.ieee.org/802/bp/StartPage
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 4: Presentation Outline
Part 1 – Feedback on 3GPP Document RP-141664
Part 2 – IEEE 802 Coexistence Lessons Learned
  IEEE 802.11 Coexistence Lessons Learned
  IEEE 802.15.2 Coexistence Lessons Learned
  IEEE 802.16h Coexistence Lessons Learned
  IEEE 802.22 Coexistence Lessons Learned
  New IEEE 802.19.1 standard for TVWS coexistence
Part 3 – Backup
  Coexistence History in IEEE 802
  Coexistence Scenarios and Metrics
  Examples of Coexistence Assurance Documents
  Coexistence Mechanisms: IEEE 802.11, 802.15.2, 802.16h, and 802.22
  Overview of 802.19.1 Standard for TVWS Coexistence
  IEEE 802 Coexistence Process
  References
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 5
Part 1 – Feedback on 3GPP Document
RP-141664
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 6: Feedback on 3GPP Document RP-141664
3GPP has identified fairness as the key challenge for successful spectrum sharing between LAA and Wi-Fi
3GPP has identified a useful initial definition of fairness
Fairness is important to IEEE 802 and 3GPP
LBT provides a useful starting point for fair sharing between LAA and Wi-Fi
IEEE 802 wants to work with 3GPP to achieve consensus on Wi-Fi/LAA sharing
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 7: 3GPP has identified fairness as the key challenge for successful spectrum sharing between LAA and Wi-Fi
3GPP doc. RP-141664 has identified the importance of fairness and defined fairness in the context of LAA LTE and Wi-Fi as follows:
  “Identify and define design targets for coexistence with other unlicensed spectrum deployments, including fairness with respect to Wi-Fi and other LAA services.”
IEEE 802 agrees that fairness is vital for successful sharing of unlicensed spectrum between LAA LTE and Wi-Fi
Fairness is in “the eye of the beholder” and so the challenge for 3GPP and IEEE 802 is to agree on a definition of fairness
The IEEE 802 notes this challenge could also be applied to sharing between LAA LTE and other systems
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 8: 3GPP has identified a useful initial definition of fairness
3GPP doc. RP-141664 has highlighted a potential definition of fairness for spectrum sharing between LAA LTE and Wi-Fi
  “This should be captured in terms of relevant fair sharing metrics, e.g., that LAA should not impact Wi-Fi services (data, video and voice services) more than an additional Wi-Fi network on the same carrier; these metrics could include throughput, latency, jitter etc.”
IEEE 802 supports this conceptual definition of fairness as the basis for further discussion between 3GPP and IEEE 802
This definition effectively treats LAA LTE and Wi-Fi as having equal standing in access to the spectrum, which is aligned with the intent of the regulatory authorities in most countries
Detailed system-level simulation scenarios will need to be specified that incorporate the throughput, latency and jitter metrics
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 9: Fairness is important to IEEE 802
The success of unlicensed spectrum (2.4 and 5 GHz) has been underpinned by the use of fair sharing mechanisms
There are billions of IEEE 802.11 devices that make use of these mechanisms
New IEEE 802.11 devices are increasingly being deployed in 5 GHz spectrum to satisfy a wide variety of important use cases
These IEEE 802.11 devices will be adversely affected by another system that does not support fair sharing mechanisms
Equally, other systems would be adversely affected if IEEE 802.11 devices stopped using fair sharing mechanisms
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 10: Fairness is important to 3GPP
Many 3GPP operators today currently leverage the benefits of Wi-Fi and want to continue to do so in the future
The market and regulators have an expectation of fair sharing between LAA and Wi-Fi, and will expect that LAA will not diminish the ongoing and expanded use of Wi-Fi in the 5 GHz band
Indeed, the doc. RP-141664 recognizes that, … it is not enough to minimize interference simply for regulatory aspects. It is also essential to insure that a deployed system will operate as a “good neighbor”
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 11: LBT provides a useful starting point for fair sharing between LAA and Wi-Fi
3GPP doc. RP-141664 highlights the use of LBT as a coexistence mechanism that is often used to achieve fairness
  “In some regions in the world, unlicensed technologies need to abide to certain regulations, e.g. Listen-Before-Talk (LBT). Fair coexistence between LTE and other technologies such as Wi-Fi as well as between LTE operators is seen necessary.”
IEEE 802 notes that LBT has a long history of success in promoting sharing between non-coordinated systems in unlicensed spectrum and has wide acceptance as a coexistence mechanism from regulators
IEEE 802 supports using the LBT coexistence mechanism as a useful starting point for sharing between LAA and Wi-Fi, particularly as it is required by regulations in Europe
IEEE 802 acknowledges that there may be other coexistence mechanisms for sharing between LAA and Wi-Fi, and is willing to discuss them as they are proposed
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 12: IEEE 802 wants to work with 3GPP to achieve consensus on Wi-Fi/LAA sharing
IEEE would like the opportunity to review the 3GPP coexistence simulation studies and provide feedback
IEEE 802 would also like to review a range of documents throughout the period of the study item
Examples of information 802 is interested in reviewing include,
  The SI schedule as it develops
  Details of the fairness criteria
  The simulation scenarios
  The LBT related parameters
  The simulation methodology
Our goal is for IEEE 802 and 3GPP to build towards a consensus on the best way for LAA to fairly share the same spectrum with 802.11 systems
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 13
Part 2 – IEEE 802 Coexistence Lessons Learned
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 14: IEEE 802.11 Coexistence Lessons Learned
CSMA/CA works in ISM bands (such as 2.4 and 5.8 GHz band) where there is uncontrolled energy in the band
IEEE 802.11 attempted to use TDMA-type systems (PCF and HCCA), and they have failed in the marketplace for a variety of reasons
  It is impractical to coordinate access between low-cost independent systems, particularly for mobile devices moving across networks
  The performance provided by CSMA/CA has proven to be good enough for the vast majority of use cases
Licensed-exempt wireless systems cannot rely on the guaranteed reception of radio management and control traffic
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 15: IEEE 802.15.2 Coexistence Lessons Learned
IEEE 802.15.2 [2] standardizes coexistence methods for IEEE 802.15.1 (Bluetooth) with other wireless systems in the 2.4 GHz frequency band
Multiple coexistence techniques are included in IEEE 802.15.2 to enable 802.15.1 to coexist with 802.11
  Several tables are provides in the Backup slides giving a brief overview of these mechanisms
One of the most powerful coexistence mechanisms included is adaptive frequency hopping (AFH) in which 802.15.1 “hops over” a nearby 802.11 WLAN
AFH has shown to be very effective
AFH was subsequently integrated into the Bluetooth specification
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 16: IEEE 802.16h Coexistence Lessons Learned
IEEE 802.16 is time-division duplex (TDD) system based on Orthogonal Frequency Division Multiple Access (OFDMA)
IEEE 802.16h [4] is an amendment to the 802.16 standard on “Improved Coexistence Mechanisms for Licensed-Exempt Operation”
One band considered for 802.16h operation is the 3650-3700 MHz band, also considered for 802.11y operation
During the development of 802.16h a coexistence assurance document [5] was developed which studied the coexistence of 802.16h and 802.11y
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 17: IEEE 802.16h Coexistence Lessons Learned
Note: Of all the 802 systems, 802.16h is the closest analog to LTE in unlicensed bands
The time-synchronization requirements of 802.16h systems are incompatible with deployed 802.11 systems
Coordination access requires a high-cost high-speed control channel between 802.16h and 802.11 systems, which is impractical
Coordination of policy between 802.16h and multiple 802.11 systems does not work since each 802.11 system is independent
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 18: IEEE 802.22 Coexistence Lessons Learned
IEEE 802.22 is a wireless regional area network (WRAN) standard for operation in the TVWS
Two or more WRAN networks may be running in the same area and be managed by different operators
Two coexistence mechanisms are included in the standard
  Spectrum etiquette is used to select orthogonal primary and secondary channels when sufficient channels are available
  Frame-based on-demand spectrum contention is used when a single TVWS channel must be shared
Additional detail is provides in the backup slides
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 19: IEEE 802.22 Coexistence Lessons Learned
In the TVWS there are special requirements for geo-location and database access in a master device within the network
In the TVWS these capabilities can be combined with an external database to enable coexistence, however, there has not yet been sufficient deployment in the TVWS to require any coexistence solutions beyond the spectrum etiquette
A definition of fairness is necessary in order to design a fair coexistence mechanism
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 20: New IEEE 802.19.1 Standard for TVWS Coexistence
With the FCC and other regulatory agencies opening up unused TV white space spectrum for unlicensed use multiple protocols may be standardized for TVWS operation
The IEEE took a proactive step to address TVWS coexistence by developing a standard
The standard utilizes two unique capabilities of TVWS networks
  Location awareness
  Access to Geo-location database
An overview of the 802.19.1 standard is given in the backup
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 21: Conclusions
NOTE: NEED TO FILL OUT CONCLUSIONS SLIDE
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 22: Part 3 – Backup
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 23: Coexistence History in IEEE 802
The issue of coexistence between IEEE 802 standard began with the standardization of IEEE 802.15.1 (i.e. Bluetooth)
  Appendix F in 802.11-1997 standard addressed coexistence of frequency hopping and direct sequence in the 2.4 GHz band
  The 802.15 working group was established in July 1999
  Both 802.11b and 802.15.1 operate in the 2.4 GHz ISM band
  Formed Task Group 2 on Coexistence of 802.11 and 802.15.1 in March 2000
  IEEE 802.15.2 was published in 2003
  Adaptive Frequency Hopping was later incorporated in to Bluetooth Specification
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 24: Coexistence History in IEEE 802
IEEE 802.19 Coexistence Technical Advisory Group
  IEEE 802 decided that it needed a technical advisory group (TAG) on wireless coexistence, that was not within any one of the individual WGs, but would operate at the 802 level. Formed TAG in 2002
  IEEE 802 developed rules on coexistence for new projects in 2004
    When a new project is proposed to the IEEE 802 Executive Committee the working group is required to state if the working group will develop a Coexistence Assurance (CA) document along with the draft standard
    If the WG commits to developing a CA document, then the WG is required to produce a CA document which is to be reviewed by the WG and 802.19 during WG letter ballot
  A number of CA documents have been produced since 2006
  Details of the process provided in subsequent slides
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 25: Coexistence History in IEEE 802
IEEE 802.19.1
  In 2009 a new project was initiated focusing on coexistence in the TV white space (TVWS)
  This standard leverages the inherent cognitive capabilities of TVWS devices including location awareness and ability to access on-line databases
  The 802.19.1 standard was published in 2014
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 26: Coexistence History in IEEE 802
Slide <number>
Years | Coexistence Work
1997 | IEEE 802.11 Appendix F addressing coexistence of frequency hopping and direct sequence systems in 2.4 GHz band
2002 | Formation of IEEE 802.19
2003 | IEEE 802.15.2 Recommended Practice on Coexistence of WPAN devices with other devices in Unlicensed Frequency Bands
2006 – Present | Coexistence Assurance (CA) Documents IEEE 802.11 – Six CA documents IEEE 802.15 – Twelve CA documents IEEE 802.16 – One CA document
To Present | General coexistence methods and self coexistence methods in MAC/PHY standards 802.11, 802.15 802.16h and 802.22
2014 | IEEE 802.19.1 Standard on TVWS Coexistence Methods
November 2014
Paul Nikolich, IEEE 802

## Slide 27: Coexistence Scenarios
In the evaluation of coexistence between wireless networks of different standards one must consider various coexistence scenarios and coexistence metrics
Coexistence Scenarios - Specify Network Parameters of the two (or more) networks
  Number of network devices
  Location of each of the network devices
    Deterministic Geometry or Stochastic Geometry
  Transmit power of the network devices
  Bandwidth and center frequency of network devices
  Statistics of channel occupancy of each of the networks
  Statistics of data traffic on each of the networks
  Protocol parameters
    Some are specified in standard, like carrier sense threshold
    Some are implementation specific, like rate adaptation algorithm
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 28: Simple Geometric Example
In an unlicensed band the user may not be able to control the physical separation of devices of the two different networks
Specify geometry as a function of the separation (d)
Evaluate coexistence metrics as a function of the separation (d)
Primary interference is between WLAN STA and WPAN Node 1
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 29: Stochastic Example
Randomly place devices from each network in a given region with a specified density
Placement of Base Stations or Access Points depend on how those devices are deployed (by operator or consumer)
Evaluate coexistence metrics as function of the density of the two networks, which may have different densities
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 30: Coexistence Metrics
There are a number of coexistence metrics that can be studied when evaluating the coexistence of two networks. Typically these are network performance metrics. Examples include,
  Network Throughput (e.g. median and 10th percentile)
  Network Latency (e.g. median and 90th percentile)
  Packet Error Rate
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 31: Examples from Coexistence Assurance Documents
A number of coexistence assurance documents have been developed in IEEE 802 to show how well new standards coexist with current standards
These documents are available on the web at,
  http://grouper.ieee.org/groups/802/19/pub/ca.htm
One nice example is the CA document for 802.15.4k which specifies several PHY for Low Energy, Critical Infrastructure Monitoring Networks (LECIM)
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 32: Example CA Document: 802.15.4k CA Doc
IEEE 802.15.4k supports multiple frequency bands
CA document summarizes which other systems operate in these bands
CA document specifies a fixed geometry of the victim network and varies the interference level, based on distance between interferer and victim node and path loss model
Simulations of co-channel interference are performed
  Plotted bit error rate (BER) and Frame error rate (FER) versus distance between interferer and victim
Considered both 802.15.4k interference on other systems and interference of other systems on 802.15.4k
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 33: IEEE 802.11 Coexistence Mechanisms
The IEEE 802.11 MAC is based on a carrier sense multiple access (CSMA) technology
IEEE 802.11 CSMA include two sensing techniques:
  Carrier sense for 802.11 Frames
  Energy Detection for other systems
The threshold for energy detection is typically set at a higher power level than 802.11 Frame detection since energy detection at very low power levels is typically unreliable
Clause 18 of the 802.11 standard [1] specifies the energy detection threshold limits for the OFDM PHY
Slide <number>
Channel Bandwidth | ED Threshold Limit
20 MHz | ED_Thresh ≤ -62 dBm
10 MHz | ED_Thresh ≤ -65 dBm
5 MHz | ED_Thresh ≤ -68 dBm
November 2014
Paul Nikolich, IEEE 802

## Slide 34: IEEE 802.15.2 Coexistence Mechanisms
IEEE 802.15.2 was developed to address the coexistence of IEEE 802.11 and 802.15.1 (Bluetooth)
A number of coexistence mechanism are included in the standard. A table is provides on the next few slides
One of the primary mechanisms, adaptive frequency hopping (AFH), was later adopted in the Bluetooth specification
Additional information about coexistence mechanisms including simulation results available in [2]
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 35: IEEE 802.15.2 Coexistence Mechanisms
Coexistence Mechanism | Description
Alternative Wireless Medium Access (AWMA) | A time division multiplexing scheme to be used when 802.15.1 master is collocated in the same devices as one of the 802.11 STAs. Since 802.15.1 slaves transmissions are set by 802.15.1 master no changes are required in the 802.15.1 slaves.
Packet Traffic Arbitration (PTA) | Specifies a packet traffic arbitration unit in a device that contains both a 802.11 STA and an 802.15.1 node. Based on priorities when there is a potential TX scheduling overlap 802.11 or 802.15.1 packets are transmitted, under the control of the PTA unit
Deterministic interference suppression | Through a collocated 802.11 STA and 802.15.1 node, the 802.11 STA can know the frequency hopping sequence. The 802.11 STA receiver introduces a dynamic notch filter to suppress the interfering 802.15.1 transmission
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 36: IEEE 802.15.2 Coexistence Mechanisms
Slide <number>
Coexistence Mechanism | Description
Adaptive interference suppression | Unlike deterministic interference suppression, this approach does not require knowledge of the frequency hopping sequence. This technique estimates the narrowband interference and subtracts the interferer. This technique requires some delay to estimate and subtract the narrowband interferer
Adaptive Packet Selection | Intelligent scheduling of 802.15.1 SCO and ACL packet transmissions to optimize network throughput and as a result minimize channel occupancy, hence improving coexistence
Packet scheduling for ACL links | Scheduling of ACL packets to occur on channel frequencies which do not cause interference to 802.11 STA
Adaptive Frequency Hopping (AFH) | Modify the frequency hopping sequence by eliminating channels which cause interference to 802.11 STA
November 2014
Paul Nikolich, IEEE 802

## Slide 37: IEEE 802.16h Coexistence Mechanisms
The 802.16h base station collects information about interference from the subscriber stations
Candidate Channel and Master Frame Assessment (CCMFA) is used to evaluate candidate channels, based on passive scanning, which has low interference
A coexistence frame (CX-Frame) is introduced which is based on two time intervals
  Coordinated Coexistence Schedule Based Interval (CXXBI)
  Coordinated Coexistence Contention Based Interval (CXCBI)
Slide <number>
November 2014
Paul Nikolich, IEEE 802
For a simulation coexistence analysis see document [5]

## Slide 38: IEEE 802.22 Self-Coexistence Mechanisms
Slide <number>
Slides on 802.22 from [7]
Orthogonal channel selection for operating channel and first backup channel
Frame allocation signalled by the super-frame control header (SCH)
MAC self-coexistence schemes
PHY coexistence mechanisms
Enough channels available
Two or more cells need to coexist on the same channel
November 2014
Paul Nikolich, IEEE 802

## Slide 39: IEEE 802.22 Self-Coexistence Mechanisms
Slide <number>
Spectrum Etiquette
  Orthogonal channel assignment scheme between adjacent cells
    different operating channel for overlapping or adjacent cells
    different first backup channel
Requires that information on operating, backup and candidate channels
of each cell is shared amongst WRAN cells: exchanged by CBP packets [5]
November 2014
Paul Nikolich, IEEE 802

## Slide 40: IEEE 802.22 Self-Coexistence Mechanisms
Slide <number>
On-demand Frame Contention
  Two or more cells need to co-exist on the same channel
November 2014
Paul Nikolich, IEEE 802

## Slide 41: Overview of IEEE 802.19.1 Background
Slide <number>
Radio regulations in some countries allow secondary radio systems to operate in TV white spaces
White spaces are not exclusively assigned to a particular radio system, any system that fulfils the requirements of the radio regulation can operate
Correspondingly, there is a need for coexistence mechanisms between different white space radio systems
IEEE 802.19.1 [6] has addressed this need by developing standard for TV white space coexistence methods
November 2014
Paul Nikolich, IEEE 802

## Slide 42: Overview of IEEE 802.19.1 System architecture
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 43: Overview of IEEE 802.19.1 Coexistence discovery
Coexistence Discovery and Information Server (CDIS) supports discovery of the neighboring white space radio systems
  Two white space radio systems are neighbors if they are likely to cause one-way or mutual harmful interference to one another if they operate on the same frequency channel
Coexistence discovery information serves as an input to coexistence decisions making
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 44: Overview of IEEE 802.19.1 Coexistence decision making
The IEEE standard 802.19.1 provides two ways to select parameters of a radio system
  Information service – coexistence system provides neighbor discovery information to a white space radio system and the white space radio system autonomously updates its operating parameters
  Management service – coexistence system manages the operating parameters of a white space radio system using Coexistence Manager (CM)
These services are provided by the IEEE 802.19.1 coexistence system to subscribed white space radio systems
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 45: Overview of IEEE 802.19.1
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 46: Overview of IEEE 802.19.1 Performance improvement
Slide <number>
Gain in throughput is 17% for 3 TV channels
Gain in throughput is 21% for 5 TV channels
November 2014
Paul Nikolich, IEEE 802

## Slide 47: Overview of IEEE 802.19.1 Summary
IEEE 802.19.1 is standard that defines coexistence system for radio systems operating in TV whitespace
IEEE 802.19.1 coexistence system can provide different level of services to the users based on their subscription
Different profiles are defined to support various deployment scenarios and use cases
Simulation shows performance improvement from using IEEE 802.19.1 coexistence system
Implementation of the IEEE 802.19.1 coexistence system was done for feasibility study of the developed protocol (see IEEE 802.19-12/138r0 for more details)
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 48: IEEE 802 Coexistence Process (1 of 2)
The IEEE 802 Operations Manual includes a procedure on Coexistence Assurance
  http://www.ieee802.org/PNP/approved/IEEE_802_OM_v15.pdf
13. Procedure for coexistence assurance
If indicated in the five criteria, the wireless WG shall produce a coexistence assurance (CA) document in the process of preparing for WG letter ballot and Sponsor ballot. The CA document shall accompany the draft on all wireless WG letter ballots.
The CA document shall address coexistence with all relevant approved IEEE 802 LMSC wireless standards specifying devices for unlicensed operation. The WG should consider other specifications in their identified target band(s) in the CA document.
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 49: IEEE 802 Coexistence Process (2 of 2)
13. Procedure for coexistence assurance (cont.)
The IEEE 802.19 WG shall have one vote in WG letter ballots that include CA documents. As part of its ballot comments, the IEEE 802.19 WG will verify the CA methodology was applied appropriately and reported correctly.
The ballot group makes the determination on whether the coexistence necessary for the standard or amendment has been met.
A representative of the IEEE 802.19 WG should vote in all wireless Sponsor ballots that are in the scope of the IEEE 802.19 coexistence WG.
Slide <number>
November 2014
Paul Nikolich, IEEE 802

## Slide 50: References
IEEE Std 802.11-2012, “Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications,” March 29, 2012
IEEE Std 802.15.2-2003, “Coexistence of Wireless Personal Area Networks with Other Wireless Devices Operating in Unlicensed Frequency Bands,” August 28, 2003
Nada Golmie, “Coexistence in Wireless Networks: Challenges and System-Level Solutions in the Unlicensed Bands,” Cambridge University Press, 2006
IEEE Std 802.16h, “Air Interface for Broadband Wireless Access: Amendment 2 Improved Coexistence Mechanisms for Licensed-Exempt Operation,” July 30, 2010
Shahar Hauzner and Mariana Goldhamer, “Coexistence Assurance Document for 802.16h CX-CBP,” IEEE 802.19-09/7r0, March 9, 2009
IEEE Std 802.19.1-2014, “TV White Space Coexistence Methods,” May 16, 2014
Apurva Mody, et. al., “Introduction to IEEE Std. 802.22-2011 and its Amendment PAR for P802.22b: Broadband Extension and Monitoring,” IEEE 802.22-11/132r3, November 2011
Slide <number>
November 2014
Paul Nikolich, IEEE 802