## Slide 1: Proposal for IEEE 802 submission to 3GPP
14 July 2015
Authors:
Name | Company | Phone | email
Andrew Myles | Cisco | +61 2 84461010 +61 418 656587 | amyles@cisco.com

## Slide 2: IEEE 802 welcomes the opportunity to collaborate with 3GPP today and into the future
Wi-Fi has been a massive economic success in the US, in Europe and globally
This benefit of “anyone, anytime, any place” must not be threatened by new access mechanisms
New access mechanisms such as LAA need compelling evidence – and there is not much time to gather it!
Evidence from 15 years of Wi-Fi suggests LBT with exponential back off is a suitable solution, as does recent work by 3GPP
IEEE 802 recommends 3GPP consider a variety of principles for LAA to promote fair sharing, based on Wi-Fi like access
Aside: IEEE 802 request 3GPP develop processes for all stakeholders to have a real say in LAA coexistence mechanisms

## Slide 3: Wi-Fi has been a massive socio-economic success in the US, in Europe and globally …
TELECOM ADVISORY SERVICES
FCC Commissioner Jessica Rosenworcel stated at the 2015 State of the Net Conference:
  Wi-Fi is a boon to the economy. The economic impact of unlicensed spectrum (in the US) has been estimated at more than $140 billion annually and it's only going to grow
Katz in a report in 2014, combining four previous studies, calculated an economic impact of $140 billion p.a. (US only), noting that this was probably an underestimate
Plum Consulting in a report in 2013 for GSMA estimated in 2013 that the economic value of Wi-Fi in Europe will increase from €23 billion p.a. in 2013 to €95 billion p.a. in 2023
Notes: Andrew

## Slide 4: … and this benefit of “anyone, anytime, any place” must not be threatened
Anyone
Anytime
Anyplace
…. with no SP required!
… and Wi-Fi just works well enough for data, voice, video and much more
Wi-Fi trades efficiency in favour of good enough performance and fair sharing between Wi-Fi networks and other technologies
It is also low cost!

## Slide 5: New access mechanisms such as LAA need compelling evidence – and there is not much time to gather it!
  At the recent ETSI BRAN meeting, an Ericsson representative made a presentation in which he emphasized the importance of making decisions based on “evidence”
  This is a very important principle that should be adopted by both 3GPP and IEEE 802
  This means, the use of an alternative sharing mechanism requires compelling evidence that the alternative mechanism shares fairly with systems used by billions of existing Wi-Fi users
  Of course, innovative new approaches to share the use of unlicensed spectrum must always be considered but should only be adopted after a long period of detailed study and consensus by all stakeholders
  The problem is that we do not have much time, in both the development of LAA in 3GPP and development of regulations in ETSI BRAN

## Slide 6: The evidence from Wi-Fi suggests LBT with exponential back off is a suitable solution …
  Wi-Fi provides 15 years of evidence that an access mechanism using LBT with truncated exponential back off provides fair coexistence between independent systems …
  … while also providing “good enough” (not perfect) performance
  This access mechanism trades off the optimal use of the channel vs fair sharing of a community resource with reduced complexity/cost
  This has shown to be true for many combinations of
    Traffic load
    Device density
    Hidden stations
    Traffic types
    Up and down link traffic
    …

## Slide 7: … and the evidence from TR 36.889 suggests LBT with exponential back off is suitable for DL access
  3GPP TR 36.889 concludes that a Category 4 LBT scheme is the best way to ensure fair coexistence (particularly with Wi-Fi) for DL access
  The TR (7.2.1.6) leaves some parameters open for further study but the evidence currently suggests Wi-Fi like parameters work well
    The TR specifies the back off as “dynamic variable” or “semi-static”, but notes the most of the Cat 4 evaluations in the TR are based on exponential back off
    The TR specifies CWmin and CWmax as configurable parameters, but almost all the Cat 4 evaluations used CWmin = 16 and CWmax = 1024
    The TR specifies either ACK/NACK or sensing based feedback, but all the variations of feedback described in 8.3.2.2 for Cat 4 use ACK/NACK
    The TR specifies a variable defer period, but the vast majority of Cat 4 simulations were based on defer periods of 34-43us
    The TR recommends a slot length less than 20us, with almost all such simulations using a slot length of 9us

## Slide 8: IEEE 802 LS’s highlight 3GPP’s simulations are insufficient to draw conclusions on many issues
  IEEE 802 and 3GPP have interacted on LAA/Wi-Fi coexistence issues between March & May 2015 via a series of liaisons
  IEEE 802 noted that 3GPP’s simulations need to consider a wider range of typical scenarios before they can be used to draw conclusions about alternative mechanisms, including:
    Up and down link traffic
    Voice and video (real time and streaming)
    High density and load
    Hidden stations
  3GPP has responded to IEEE 802 that they either have undertaken simulations or have plans to undertake simulations of some many, but not all, of these scenarios
  Not all of IEEE 802’s suggests have been accepted, and so it is impossible to conclude that any alternate mechanism is satisfactory

## Slide 9: Aside: IEEE 802 request 3GPP develop processes for all stakeholders to have a say in LAA coexistence
  3GPP are discussing the use of LAA in a 5GHz spectrum, which is a “community resource” that must be shared fairly
  However, it appears that 3GPP are planning to make decisions about LAA and how it uses 5GHz without giving other stakeholders a real voice
    3GPP has no review processes accessible to other stakeholders, unlike IEEE
    3GPP has not acted on many comments received from IEEE 802 via LS’s
  One option is for regulators to impose rules on behalf of other stakeholders that constrain 3GPP’s choices for LAA
    eg this is what is happening in ETSI BRAN
  A better choice is to set up mechanism that allow other stakeholders to have a real say in how LAA shares with Wi-Fi via a collaborative process
  The IEEE 802 requests that 3GPP propose an effective collaboration mechanism that allows other stakeholders to review and influence LAA, particularly in the context of coexistence
  to

## Slide 10: IEEE 802 recommends 3GPP consider a variety of principles for LAA to promote fair sharing
  The following slides contain a set of principles that IEEE 802 recommends considered from adoption as access mechanisms for LAA
  They are not intended to represent detailed specifications because that is the responsibility of 3GPP and not IEEE 802
  The goal of the recommendations are to enable LAA and Wi-Fi to share unlicensed spectrum fairly …
  … and ultimately to allow unlicensed spectrum to continue to be a community resource available for all
  In summary principles are proposed that LAA:
    Adopt Wi-Fi like parameters to maximise probability of coexistence
    Use access rules similar to those used by Wi-Fi
    Adopt a variety of other principles and proposals to promote sharing

## Slide 11: It is proposed that LAA adopt Wi-Fi like parameters to maximise probability of coexistence
Summary | Principle | Adopt Wi-Fi like parameters to maximise probability of coexistence
Definitions based on Wi-Fi | Proposal | Define “busy” & “free” states based on received energy & channel reservations
 | Proposal | Divide the “free” period into slots
 | Proposal | Define a “defer” period
 | Proposal | Define Energy Detect (ED) & Preamble Detect (PD) thresholds

## Slide 12: Principle: adopt Wi-Fi like parameters to maximise probability of coexistence
  The reality is that billions of Wi-Fi devices do exist and the 802.11 standard has defined various timing parameters
    eg slot times, CCA mechanism, AIFS mechanism
  Allowing LAA to use different parameters is likely to make fair sharing much harder ...
  … and forcing LAA to use similar parameters is unlikely to make it any less functional
  Therefore IEEE 802 recommends 3GPP adopt a limited number of parameters taken directly from the Wi-Fi access mechanism
  This approach is aligned with the Ericsson proposal in 3GPP in relation to “defer” and “slot” times … and much of the simulation work undertaken during the Study Item

## Slide 13: Proposal: define “busy” & “free” periods based on received energy & channel reservations, similar to Wi-Fi
  It is proposed by IEEE 802 that LAA adopt concepts of a “busy” and “free” medium similar to those used in Wi-Fi
    Note there is no need for 3GPP to adopt exactly the same terms as used in the IEEE 802.11 standard
  The wireless medium is deemed to be “busy” for the period a device:
    Receives energy above an energy threshold, and an additional “defer” period
    Transmits energy on the medium, and an additional “defer” period
    The device is aware another device has “reserved” the channel, and an additional “defer” period
      Note: reservation occurs by the use of NAV in Wi-Fi; other technologies may use different mechanisms
    The device is aware another device is probably transmitting on a channel, and an additional “defer” period
      This idea encapsulates the EIFS concept in Wi-Fi
  In all other circumstances the medium is deemed to be “free”

## Slide 14: Proposal: divide the “free” period into slots, similar to Wi-Fi
  It is proposed by IEEE 802 that LAA adopt concepts of a “slot” similar to that used in Wi-Fi
  The period the medium is “free” is divided into slots
  Energy detection shall occur during each slot
  Each slot has a period of at least 9us, similar to Wi-Fi
    A device must be capable of detecting energy (with 90% probability) and executing any other necessary actions, such as processing and turnaround, within this slot period
    Note: Wi-Fi systems must detect energy on the medium in each slot within 4us, leaving 5us for propagation delay, processing time and turnaround time; other technologies may use different timing
    Ideally LAA will define a slot time as exactly 9us, but great slot times are possible too – this was requested by ETSI BRAN participants

## Slide 15: Proposal: define a “defer period”, similar to Wi-Fi
  It is proposed by IEEE 802 that LAA adopt concepts of a “defer period” similar to that used in Wi-Fi
    PIFS, DIFS in the DCF version of Wi-Fi
    AIFS in the EDCA version of Wi-Fi
  The “defer period” is defined to be of length (16us + n * slot times), n >= 1, and consists of
    16us that is analogous to SIFS in Wi-Fi followed by …
    … one or more slot periods
  Energy detection are assumed to occur at least during the slots of the “defer period”
  The value of “n” depends on the priority level
    See later in this deck for details

## Slide 16: Proposal: define Energy Detect (ED) & Preamble Detect (PD) thresholds, similar to Wi-Fi
  Simulations with 20MHz channels from 3GPP indicate a need for LAA to have either:
    Wi-Fi preamble detection (PD) at -82dBm & energy detection (ED) at -62dBm (same as Wi-Fi)
    ED at least less than -77dBm
  It is proposed that ETSI BRAN adopt, similar to Wi-Fi, for a 20MHz channel, either:
    ED threshold as less than -77dBm
      Note: a lower ED threshold assists LAA mitigate hidden station issues
    ED threshold as less than -62dBm if the device also undertakes Wi-Fi PD at less than -82dBm
  Note: PD is not strictly technology neutral but it does pragmatically recognize there is a huge base of legacy Wi-Fi equipment

## Slide 17: It is proposed that LAA use access rules similar to those used by Wi-Fi
Access based on Wi-Fi | Principle | Define LBT rules in terms that allow flexibility and innovation, within limits
 | Proposal | Execute LBT and exponential back-off mechanisms before any transmission
 | Proposal | Allow a limited number of control frames to be transmitted without any LBT
 | Proposal | Count a random number of slots within a contention window as a back-off procedure
 | Proposal | Adjust contention window based on successful & unsuccessful transmission of frames
 | Principle | Enable QoS using multiple access engines in a device
 | Proposal | Set parameters for QoS
 | Proposal | Devices must undertake LBT before accessing secondary channels

## Slide 18: Principle: define LBT rules in terms that allow flexibility and innovation, within limits
  It is proposed that an LAA device must use a LBT plus “truncated, exponential back-off” mechanism before it can access the medium
    This proposal is aligned with the Cat 4 LAA proposal in 3GPP and Wi-Fi
  The mechanism is defined in terms that allow systems a degree of flexibility in implementation details
    This approach enables innovative solutions, while also achieving the goal of fair sharing of unlicensed spectrum (article 3.2 of the RE-D in Europe)
  It is proposed that multiple priority levels are defined by the use of multiple virtual “access engines” within a device
    A priority level is defined by tuple of CWmin, CWmax and the defer period
    Note: there has been no consideration of priority in 3GPP simulations

## Slide 19: Proposal: execute LBT and exponential back-off mechanisms before and after any transmission
  An “access engine” within a device may transmit consecutive multiple frames (in a TxOP) starting on a slot boundary if:
    The medium is “free” AND
    Any back-off procedure has completed AND
    No higher priority “access engine” in the same device is eligible to transmit
  An “access engine” within a device must execute a back-off procedure
    When the medium is “busy” at the time it queues the first frame in the TxOP for transmission OR
    After transmission of a complete TxOP OR
    When an “access engine” in the same device at a higher priority level causes a tx deferral

## Slide 20: Proposal: allow a limited number of control frames to be transmitted without any LBT
  Normally the access mechanism must operate before any transmission
  Exception: a short control frame may be transmitted immediately after a reception of a frame from another access engine without checking for a “free” medium
    Note: this is to provide for ACKs, CTSs, etc in Wi-Fi and similar frames in LAA
  It is assumed the “other” access engine can continue the TxOP immediately after the control frame
    eg allows data, ack, data, etc

## Slide 21: Proposal: count a random number of slots within a contention window as a back-off procedure
  The back-off procedure in each “access engine” in a device is driven by a parameter called CW (contention window), which may take values between
    CWmin: minimum value of CW
    CWmax: maximum value of CW
  A back-off procedure in each “access engine” operates as follows
    Choose a random number q between 0 and CW
    Count q slots
  Note that a back-off procedure will implicitly countdown only while the medium is “free” because slots are defined to be “free”

## Slide 22: Proposal: adjust contention window based on successful & unsuccessful transmission of frames
  Each “access engine” in a device adjusts CW independently
  CW is initially set to CWmin, with a maximum value of CWmax
  CW is reset to CWmin when evidence is received that the first frame in a past TxOP has been successfully received
    eg an immediate ACK in Wi-Fi, a delayed ACK in LAA
  CW may also be reset after a system defined number of consecutive transmission failures
    Note: this is analogous to the retry counts in Wi-Fi
  CW is doubled (plus one) each time evidence is received that the first frame in a past TxOP has not been successfully received
    eg evidence could be from missing ACK in 802.11, a delayed NACK in LAA
    Note: CW remains the same when transmission by a higher priority “access engine” causes the transmission of a TxOP to be deferred

## Slide 23: Principle: enable QoS using multiple “access engines” in a device, similar to Wi-Fi
  QoS is enabled in a LBT plus back-off environment in Wi-Fi using four “access engines” operating in parallel within a device
    The priority levels are voice, video, best effort (typical) and background
  3GPP do not appear to have considered QoS (either for Wi-Fi or LAA) in their simulations to date
  It is proposed that 3GPP adopt a similar QoS mechanism, if QoS is required, because it is proven and mature
  Note: the way the “access engine” is described in this proposal means it is more aligned with DCF in Wi-Fi than EDCA in Wi-Fi; this means EDCA is more conservative than this proposal
  While this proposal does not limit the use of high priority access, it is expected that devices would use high priority responsibly

## Slide 24: Proposal: set minimum parameters for QoS, similar to Wi-Fi
Note: an “access engine” may use higher values
Note: we will probably want to define different values for APs, like Wi-Fi
Note: these values are based on a DCF interpretation of EDCA – we could make it straight EDCA!
Level | Priority | n | CWmin | Cwmax
Highest | Voice | 1 | 3 | 7
Next highest | Video | 1 | 7 | 15
Typical | Best effort | 2 | 15 | 1023
Lowest | Background | 6 | 15 | 1023

## Slide 25: Proposal: devices must undertake LBT before accessing secondary channels
  The access mechanisms described in this document are based on access to a 20MHz channel
  However, Wi-Fi accesses 40MHz, 80MHz, 160Mhz too, and presumably LAA will want the same flexibility
  It is proposed that LAA use a similar mechanism to Wi-Fi to access secondary channels
  This means that at least a short LBT is undertaken in secondary channels after execution of a full access procedure in the primary channel

## Slide 26: Summary: “Access engine” operation is defined by a flow diagram
Wait for frame
State is “Busy”?
Set q = rand[0, CW]
Wait until state is “Free”
q = 0?
Set q = q -1
State “Free” at end of slot?
State “Free” at end of slot?
Frame ready to tx?
Tx frame
Start
Is higher priority tx ready?
Y
N
Y
N
N
Y
N
Y
N
Y
Y
N
Note: This diagram is not intended as a detailed specification – but rather a statement of principles

## Slide 27: It is proposed that LAA adopt a variety of other principles to promote sharing
Other | Proposal | Define the maximum transmission time of 5ms for each access
 | Principle | Do not require LAA to respect NAV from Wi-Fi
 | Proposal | Devices shall have mutual respect for reservations made by others using same mechanisms
 | Proposal | TxOPs may be continued by another device after completion of a “defer” period
 | Proposal | Devices using or reserving channel shall use it necessary transmission purposes

## Slide 28: Proposal: define the maximum transmission time of about 5ms for each TxOP, similar to Wi-Fi
  Define a TxOP as the contiguous transmissions after an “access engine” gains access to the medium (both DL and UL)
  Most 3GPP Cat 4 simulations were undertaken using maximum TxOP times of about 4ms, and showed reasonable fairness and performance with exponential back-off
  Some simulations (R1-153421) showed that a maximum TxOP time of 10ms was probably too long
  Measurements in the field (eg in a stadium) show that the vast majority of Wi-Fi TxOPs are less than 3ms – the maximum is 5.5ms
  It is proposed that a reasonable upper bound for the maximum length of a TxOP is about 5ms
    5ms provides a little more efficiency and a little less fairness than 4ms

## Slide 29: Principle: do not require LAA to respect NAV from Wi-Fi
  LBT is a compromise in that it listens for energy at the tx’er, whereas energy at the rx’er is more relevant to successful reception of the transmitted frames
  LBT is also a compromise in that there are configurations where LBT cannot be used avoid interfering with transmissions between other devices it can’t hear
  These issues represent various forms of what are known as hidden station problems
  Wi-Fi partially resolves hidden station problems by its use of the NAV in frames, and particularly its use of RTS/CTS control frames
    NAV in data frames actually protects ACK in Wi-Fi
  …

## Slide 30: Proposal: do not require LAA to respect NAV from Wi-Fi
  …
  These hidden station mitigation techniques may be less effective if LAA does not respect the NAV in frames transmitted by Wi-Fi devices
  Given it does not seem reasonable to adversely affect billions of existing Wi-Fi devices, it could be argued that we should require LAA devices to at least respect the NAV transmitted by all Wi-Fi devices
  However, this approach is not very technology neutral and unreasonably forces every LAA device to implement a Wi-Fi rx function
  Respecting the NAV might also be unnecessary if the LAA devices use an ED of, say, -77dBm as an alternative form of hidden station mitigation

## Slide 31: Proposal : devices shall have respect for reservations made by others using common mechanisms
  It is generally unacceptable to require LAA to respect a Wi-Fi NAV
  However, there have been some indications that LAA systems may transmit Wi-Fi CTS2Self control frames
  It is only fair that if a LAA system expects Wi-Fi systems to respect a NAV it transmits then the same LAA system should respect any NAV received from Wi-Fi systems
  This principle can be generalised by requiring any system using a particular mechanism to reserve the medium shall respect reservations made by other systems using the same mechanism

## Slide 32: Proposal: TxOPs may be continued by another device after completion of a “defer” period
  Most of the 3GPP simulations focused in LAA DL only scenarios
  However, there are plans for LAA to support UL traffic too in the future
  A potential problem with this is that the LAA UE is scheduled by the eNB, suggesting it may not undertake LBT sensing or any back-off
  This is an acceptable approach in an environment with no hidden stations
  However, any possibility of hidden stations suggests that UEs also need to execute at least some sort of LBT to ensure fair sharing of the channel
  It is proposed that a device may continue a TxOP obtained by another device immediately after a “defer” period of 25us
    Note: this allows access at PIFS

## Slide 33: Proposal: devices using or reserving a channel shall only use it for necessary tx purposes
  Some of the 3GPP simulations allow the LAA system to reserve the channel (using CTS2Self) before it is needed so that it is available when it is needed
  This could result in the LAA system reserving but not using the channel, effectively representing interference for Wi-Fi
  This is contrary to the principle in unlicensed to accept interference but to avoid causing interference
  Similarly it has been suggested that LAA could fill the medium with legitimate but unnecessary energy to maintain control of the medium until it is ready to use it
  It is proposed that any system reserving or using a channel must only make use of it for necessary and legitimate data and management transmission purposes

## Slide 34: IEEE 802 welcomes the opportunity to collaborate with 3GPP today and into the future
Wi-Fi has been a massive economic success in the US, in Europe and globally
This benefit of “anyone, anytime, any place” must not be threatened by new access mechanisms
New access mechanisms such as LAA need compelling evidence – and there is not much time to gather it!
Evidence from 15 years of Wi-Fi suggests LBT with exponential back off is a suitable solution, as does recent work by 3GPP
IEEE 802 recommends 3GPP consider a variety of principles for LAA to promote fair sharing, based on Wi-Fi like access
Aside: IEEE 802 request 3GPP develop processes for all stakeholders to have a real say in LAA coexistence mechanisms