## Slide 1: A discussion of ED & PD for 802.11 & LAA in unlicensed spectrum
18 July 2016
Authors:
Name | Company | Phone | email
Andrew Myles | Cisco | +61 2 84461010 +61 418 656587 | amyles@cisco.com

## Slide 2: IEEE 802 should explain & promote the need for 802.11 PD detection … because it is important!
3GPP RAN1 is requesting that future multi-technology coexistence be driven purely by a fixed ED threshold
3GPP RAN1’s request should challenge 802.11 WG to revaluate its assumptions & current solutions
IEEE 802 must be driven by unlicensed band’s Guiding Principle that transmitters should not harm receivers
Unfortunately, neither 802.11 or LAA satisfy the Guiding Principle in mixed environments very well
The underlying issue is that neither 802.11 or LAA can detect the other system in some cases
Lesson: both ED & PD matter for multi-technology coexistence environments
The existence of billions of 802.11 systems today means that an 802.11 based PD must be used
The situation
The problem
The answer
IEEE 802 should consider a range of “next steps” to explain and promote the need for 802.11 PD detection
Possible next steps

## Slide 3: 3GPP RAN1 is requesting that future multi-technology coexistence be driven purely by a fixed ED threshold
  The IEEE 802 review of LAA Rel. 13 resulted in IEEE 802 requesting 3GPP RAN1 to make LAA more sensitive to 802.11 transmissions:
    This request was based on the observations that the proposed LAA mechanism (based on ED of -72dBm only) does not ensure fair coexistence
    See Comment 3 in 19-16-0037-09 for details
  RAN1 rejected IEEE 802’s request on the basis that RAN1 has had considerable debate and has agreed there is not a problem, but without responding to the particular issues raised by IEEE 802
    See Response 3 in R1-166040
  RAN1 further suggested that 802.11 also use ED of -72dBm in the future
    RAN1 respectfully requests future IEEE 802.11 technologies to align the energy detection threshold used with other technologies operating in the same unlicensed band, e.g., -72 dBm.
    An energy detection threshold of -72 dBm has been chosen by 3GPP for Rel-13 LAA also with an interest in aligning with other technologies in the future.

## Slide 4: 3GPP RAN1’s request should challenge 802.11 WG to revaluate its assumptions & current solutions
  802.11 has been successfully operating and enabling coexistence for many years using both an ED (energy detection) of -62dBm and a PD (preamble detection) of -82dBm
  Success in this case has been the property of 802.11 that allows anyone, anytime, anyplace to operate a network that works well enough!
  However, the success has been made easier because most of the time 802.11 systems only have to share with other 802.11 systems
  That may no longer be the case, with the potential introduction of new technologies like LAA, LTE-U and MulteFire
  In the future, 802.11 systems may want to coexist with each other differently, with an increased focus on frequency reuse in 802.11ax
  3GPP RAN1’s suggestion to drive coexistence based only on ED of -72dBM should challenge the 802.11 WG to revaluate our assumptions & solutions

## Slide 5: IEEE 802 must be driven by unlicensed band’s Guiding Principle that transmitters should not harm receivers
  The rules for unlicensed spectrum in various regulatory domains are usually some variant of:
    Recognised services have absolute priority over unlicensed devices
    Unlicensed devices should avoid interfering with other unlicensed devices … and accept interference from other unlicensed devices!
  This leads to a Guiding Principle that has been an underlying driving assumption in almost all 802.11 WG activities over 25 years
    An 802.11 device (or any unlicensed device) should not transmit in an unlicensed channel if it is reasonably likely to cause harm to an ongoing reception by another unlicensed device in the channel
  This Guiding Principle should be something for which there should be no disagreement
    Note: it is not claimed that the Guiding Principle is a specific law or regulation anywhere, just that it represents best practice everywhere

## Slide 6: Harm in the Guiding Principle must refer to damage to any ongoing reception … not a long term average
  The Guiding Principle refers to harm to an ongoing reception by another unlicensed device
  Harm has been interpreted by various stakeholders in two main ways
    In 802.11 WG, harm is generally focused on the potential damage caused to any ongoing current reception
    In 3GPP RAN1, harm is often evaluated by simulation of average performance in various environments, rather than harm to the ongoing current reception
  Unfortunately, averaging over time and environments hides too many sins and cannot be used to protect receptions by individual devices
    3GPP RAN1’s simulation do not evaluate many important environments
    Even for the environments simulated, averages (or even 90% percentiles) will not reveal cases where some devices are unfairly “locked out”
  Every device has a right to operate, and so any evaluation of harm must be focused on any ongoing current reception … not a long term average

## Slide 7: Unfortunately, neither 802.11 or LAA satisfy the Guiding Principle in mixed environments very well
Transmitting device | Does transmitting device satisfy the Guiding Principle in a … | 
 | … 802.11 or LAA only environment? | … mixed 802.11/LAA environment?
802.11 |  | 
LAA | A issue for 3GPP RAN , not 802.11 WG | 

## Slide 8: This presentation is based on common definitions of Energy Detection (ED) & Preamble Detection (PD)
Definitions:
  Energy detection (ED)
    Refers to the ability of the receiver to detect energy level in the channel based on the noise floor, ambient energy, interference sources, and any unidentifiable 802.11 transmissions that can’t be decoded
  Preamble detection (PD)
    Refers to the ability of the receiver to detect and decode an 802.11 preamble
    In addition, Clear Channel Assessment (CCA) must be reported as BUSY when an 802.11 preamble is detected, and must be held as BUSY for the length of the received frame as indicated in the frame's PLCP Length field

## Slide 9: 802.11 generally satisfies the Guiding Principle in an 802.11-only environment
802.11 tx’s …
… low risk of adversely affecting other 802.11 systems given they are so far away
802.11 doesn’t tx …
… avoids significant risk of damaging ongoing tx’s by other 802.11 systems
Probably collision (otherwise would PD trigger), 802.11 tx’s …
… low risk of tx causing adverse effect to ongoing tx’s by other 802.11 systems given they probably in a collision already, and there is some possibility of successful tx
Probably collision (otherwise PD would trigger), but 802.11 doesn’t tx …
… there is not much pointtx’ing given the energy is so loud
< -82dBm
> -82dBm
< -62dBm
> -62dBm
ED
PD
802.11




1st
2nd
Assumption:
802.11 in 802.11 only environment

## Slide 10: 802.11 doesn’t satisfy the Guiding Principle very well in all cases in a mixed LAA/802.11 environment
802.11 tx’s …
… low risk of adversely affecting other 802.11 systems given they are so far away (note: PD not relevant to LAA)
802.11 doesn’t tx …
… avoids significant risk of damaging ongoing tx’s by other 802.11 systems (note: PD not relevant to LAA)
802.11 tx’s …
… but will tx over top of LAA tx’s down to -82dBm & below (but typically will not adversely affect other 802.11 tx’s)
… but mitigated noting LAA claims to handle interference well
802.11 doesn’t tx …
… there is not much point tx’ing given the energy is so loud
< -82dBm
> -82dBm
< -62dBm
> -62dBm
ED
PD
802.11




1st
2nd
Assumption:
802.11 in mixed LAA/802.11 environment

## Slide 11: LAA doesn’t satisfy the Guiding Principle in a mixed LAA/802.11 environment very well – and it matters!
LAA tx’s …
… but will tx over top of ongoing 802.11 tx’s down to -82dBm, where 802.11 would not in the same circumstances
LAA doesn’t tx …
… which means that LAA respects ongoing 802.11 tx’s from -72dBm to -62dBm better than 802.11 protects LAA tx’s
< -72dBm
> -72dBm
ED
LAA


3GPP RAN’s own studies indicate that LAA not satisfying the Guiding Principle actually matters
The issue above is not just a “thought experiment” with no practical effect
As noted in the IEEE 802 LS to 3GPP RAN1, 3GPP RAN1’s own simulation studies (despite their flaws) have shown that if LAA only uses an ED of -72dBm, fair coexistence with IEEE 802.11 cannot always be achieved
Also as noted in the LS, unfair coexistence with 802.11 is particularly acute in scenarios where the full coverage of each 802.11 AP is utilized (which are under-represented in 3GPP RAN1 studies), since devices with weaker link strengths are especially sensitive to interference.
PD
Assumption:
LAA in mixed LAA/802.11 environment
Only
Not done

## Slide 12: The underlying issue is that neither 802.11 or LAA can detect the other system in some cases
  A review of what causes 802.11 & LAA to not satisfy the Guiding Principle very well in all cases reveals a common factor…
    802.11 does not do as well when it can’t distinguish between a collision and an LAA transmission between -82dBm and -62dBm
    LAA does not do as well when it can’t distinguish between a collision and an 802.11 transmission between -82dBm and -72dBm
  The underlying issue is that both systems can’t decode the transmissions of the other technology in any circumstances, and thus can’t differentiate between a collision and a transmission
  The problem is not currently equal between the technologies because 802.11 has a 20dBm “gap”, whereas LAA only has a 10dBm “gap”
  Adoption of a common ED = -72dBm (as suggested by 3GPP RAN1) makes the problem equally bad … but does not solve it!

## Slide 13: Lesson: both Energy & Preamble Detection matter for multi-technology coexistence environments
  The underlying issue described on the previous page has a lesson as a corollary
  Both ED and PD are important because:
    ED can be used to detect collisions
    PD can be used to differentiate transmissions from collisions
  This is a lesson that was known as far back as 1998/99
    In 1998/99 the IEEE 802.11 WG and ETSI BRAN recognised the important of a common PD mechanism when they agreed on a common PHY for 802.11 and HIPERLAN II
    Of course, this agreement was ultimately irrelevant because HIPERLAN II failed in the market place, meaning coexistence with 802.11 was moot
Lesson
Both Energy Detection (ED) and Preamble Detection (PD) matter for multi-technology coexistence!

## Slide 14: Preamble Detection is likely to become increasingly important to enable wide deployment of frequency reuse
  Improved frequency reuse is asserted to be a feature of LAA
    … and of 802.11ax!
  Wide deployment of frequency reuse requires transmitters attempting improved frequency reuse to understand the likelihood of interfering with other systems
    Note: this assertion assumes a desire to satisfy the Guiding Principle,
    eg LAA can never attempt improved frequency reuse when just using just ED because the other systems might be a legacy 802.11 system that will suffer interference
  ED is not sufficient to make this evaluation; a common PD mechanism is required!

## Slide 15: The existence of billions of 802.11 systems today means that an 802.11 based PD must be used
  The lesson of simulation, analysis and history is that both ED and PD are required of effective multi-technology coexistence
    Requiring ED is easy because energy is generic
    Requiring PD is harder because the different technologies need to agree on the form of a PHY level communication mechanism
  The existence of billions of 802.11 in 5Ghz band means PD based on 802.11a must be used
    Back in 1998/99 when there was no legacy base, there was a choice – the form of PD could be negotiated by IEEE 802.11 WG and ETSI BRAN – and it was!
    In 2016 with billions of 802.11 based devices operating in 5GHz band the only answer is to use a backwards compatible mechanism – based on 802.11a!
    Discarding PD (as suggested by 3GPP RAN1) not only does not solve the LAA/802.11 problem, it also creates an new 802.11/legacy 802.11 problem
  The only possible discussion on the form of PD in 2016 might be one on how users of the 5GHz band might transition to a new PD in the future

## Slide 16: IEEE 802 should consider a range of “next steps” to explain and promote the need for 802.11 PD detection
Options for …
  Reject the 3GPP RAN1 request to rely on PD at -72bBm
    With reasons of course
  Request (again) 3GPP RAN1 to adopt 802.11 based PD detection
    Again with detailed explanations
  Suggest to 3GPP RAN1 that LAA at least have options for 802.11 based PD transmission
    Note that this will help 802.11 detect LAA for improved coexistence
… next steps
  Consider notifying other stakeholders of the IEEE 802 requests and suggestions
    Regulators: FCC, OFCOM, etc
    Other SDOs: Wi-Fi Alliance, ETSI BRAN, GSMA, WBA, etc
    Press: technical press, mass media
  Consider sponsoring lab tests to demonstrate issues
    Perhaps working with the Wi-Fi Alliance

## Slide 17: IEEE 802 should continue to request that 3GPP RAN1 defines LAA to use 802.11 PD detection
  The IEEE 802 proposed resolution of comment 3 in 19-16-0037-09 was for LAA to detect 802.11 with similar sensitivity that 802.11 detects 802.11, either by defining the use by LAA of:
    802.11 based PD at -82dBm (preferable!)
    ED at -77dBm or lower
  An even better solution that maximise communications between the two technologies would be for LAA to also respect 802.11 NAVs
  These proposals would solve the coexistence problem (consistent with the Guiding Principle) from an 802.11 perspective in that 802.11 would not be adversely affected by LAA
    Assuming other details of LAA, including LBT, are reasonable
  It is interesting to note that it is rumoured that at least one implementation of LTE-U does implement 802.11 based PD detection
    If true, this is a demonstration that such a requirement is not an undue burden

## Slide 18: IEEE 802 should suggest that 3GPP RAN1 defines LAA to use 802.11 PD transmission too
  It is equally important to solve the coexistence problem (consistent with the Guiding Principle) from an LAA perspective so that LAA is not adversely affected by 802.11
  An easy solution to this problem is for LAA to define the use of 802.11 based protection mechanisms, so that 802.11 devices can help protect LAA devices from 802.11 interference
    Transmission of 802.11 based PD; and/or
    Transmission of 802.11 based CTS-to-self
  Of course, it is the choice of 3GPP RAN1 as to whether they want protection from 802.11 systems …