## Slide 1: A proposed response to 3GGP on fourteen coexistence issues
10 March 2017
Authors:
Name | Company | Phone | email
Andrew Myles | Cisco | +61 2 84461010 +61 418 656587 | amyles@cisco.com

## Slide 2: 802.19 WG needs to decide on how to deal with latest and future LS’s from 3GPP RAN1
Executive summary
  IEEE 802 and 3GPP RAN/RAN1 have been playing “LS ping pong” for more than two years
  A small number of volunteers put together proposed text for a response to 3GPP
  A review of the summary table suggests we are making progress on many issues
  It is proposed that we review a draft proposed LS to 3GPP in relation to the 14 issues
  Rerun: Stepping back … is “LS ping pong” the best way to work with 3GPP RAN1 on LAA and eLAA?

## Slide 3: IEEE 802 and 3GPP RAN/RAN1 have been playing “LS ping pong” for more than two years …
3GPP RAN/RAN1
IEEE 802
Jun 2014: Reply LS on Areas of Mutual Interest to 802 LMSC and 3GPP
Jul 2014: Areas of Mutual Interest to 802 LMSC and 3GPP
Sep 2014: Licensed-Assisted Access using LTE
Nov 2014: Coexistence Lessons Learned
Mar 2015: Regarding Coexistence of Licensed Assisted Access (LAA) and IEEE 802
Jan 2015: Statement Regarding Coexistence of Licensed Assisted Access (LAA) and IEEE 802
Mar 2015: Regarding 1) Clarification of LBT Categories and 2) LAA / 802.11 Coexistence
Apr 2015: 802.11 Coexistence
Apr 2015: Clarification of LBT Categories
May 2015: Follow-up Liaison Statement Regarding LAA
Next page

## Slide 4: … IEEE 802 and 3GPP RAN/RAN1 have been playing “LS ping pong” for more than two years …
3GPP RAN/RAN1
IEEE 802
Jun 2015: LS on LAA capabilities and scope
Aug 2015: presentation at 29-Aug-15 LAA Workshop
Jun 2015: 3GPP RAN Workshop on Licensed-Assisted Access (LAA)
Mar 2016: Comments related to the LAA Specification
Jun 2015: LS on LAA capabilities and scope
May 2016: Review of 3GPP LAA Specification Rel. 13
Next page
Dec 2015: LAA CRs
Jun 2016: Response Liaison Statement to 802 regarding LAA
Previous page
Jun 2016: Response Liaison Statement to 802 regarding LAA

## Slide 5: … IEEE 802 and 3GPP RAN/RAN1 have been playing “LS ping pong” for more than two years
3GPP RAN/RAN1
IEEE 802
Previous page
Today
Nov 2015: Response LS to IEEE 802.11 regarding LAA
July 2016: Review of 3GPP LAA Specification Rel. 13
Nov 2016: LS related to ED issue

## Slide 6: A small number of volunteers put together proposed text for a response to 3GPP
  The most recent Liaison Statement (Nov 2016) from 3GPP RAN1 contains responses to LS’s from IEEE 802:
    July 2016: Review of 3GPP LAA Specification Rel. 13
    Nov 2016: LS related to ED issue
  After the Atlanta meeting in Jan 2017 a small number of volunteers provided outlines of text for a possible response LS to 3GPP
    Acting as editor, the Chair turned it into actual text
    … and apologises for not having time to clean up typo’s and style
  The general approach taken where there was remaining disagreement was to “agree to disagree” (without using those words) but to:
    Suggest gathering evidence via RAN4 testing
    Suggest gathering evidence from deployment experience
    Request confirmation of promised 3GPP actions

## Slide 7: A review of the summary table suggests we are making progress on many issues
# | Comment by IEEE 802 in Liaison Statement to 3GPP RAN1 | Previous status | Current status
1 | Radio equipment in unlicensed spectrum should not transmit energy for the primary purpose of blocking access to the channel to others | Possibility for consensus & resolution | Consensus, subject to additional RAN1 spec work
2 | Transmission of Discovery Reference Signals should be clearly bounded to avoid excess airtime overhead on unlicensed spectrum | Some consensus, but not fully resolved | Consensus, subject to field experience
3 | Radio equipment in unlicensed spectrum should detect neighboring networks with sufficient sensitivity to ensure fair coexistence | No consensus, and not resolved | No consensus, but possible with RAN4 testing
4 | LAA and IEEE 802.11 slot boundaries should align as accurately as possible to preserve spectral efficiency in unlicensed spectrum | No consensus, and not resolved | No consensus, but possible with RAN4 & field testing
5 | LAA and 802.11 multi-channel aggregation schemes should align | No consensus, wait for measurements | tbd

## Slide 8: A review of the summary table suggests we are making progress on many issues
# | Comment by IEEE 802 in Liaison Statement to 3GPP RAN1 | Previous status | Current status
6 | Radio equipment in unlicensed spectrum should stop transmission as soon as transmission of useful data is complete | Possibility for consensus & resolution | Consensus, subject to use of short sub-frames
7 | Channel access that is obtained using special access mechanisms for high priority data should not be used to transmit lower priority data | Consensus but not fully resolved | Consensus, subject to use of short sub-frames
8 | The maximum continuous transmission time should be limited to avoid blocking latency sensitive traffic on coexisting networks | Consensus but not fully resolved | No consensus, but possible with RAN4 & field testing
9 | Adjustment of channel access contention window should be based on comparable indicators of congestion to ensure fairness between technologies | No consensus, wait for measurements | No consensus, but possible with use of short sub-frames

## Slide 9: A review of the summary table suggests we are making progress on many issues
# | Comment by IEEE 802 in Liaison Statement to 3GPP RAN1 | Previous status | Current status
10 | Adjustment of channel access contention window should be clearly defined | Consensus, and resolved | Consensus, and resolved
11 | The channel access state machine during channel sensing should be clearly defined | Consensus, and resolved | Consensus, and resolved
12 | The use of the back off mechanism should be clearly defined | Substantial consensus, but not fully resolved | Consensus, and resolved
13 | Issues related to ED threshold and coexistence between LAA and IEEE 802.11 | n/a | No consensus, but possible with RAN4 testing
14 | Continued dialog towards a future framework for efficient sharing of the 5 GHz band | n/a | Waiting for RAN decision

## Slide 10: It is proposed that we review a draft proposed LS to 3GPP in relation to the 14 issues
  The proposed draft for review is 19-17-0030-00
  It is suggested we run through it today once in overview …
  … and then spend time in another session or off-line doing any serious editing
  … or, alternatively, send proposed text to Andrew Myles (amyles@cisco.com)

## Slide 11: Stepping back … is “LS ping pong” the best way to work with 3GPP RAN1 on LAA and eLAA?
  A meta issue arises as to whether IEEE 802 should continue this process of “liaison ping pong”?
  Back in late 2015, 3GPP RAN leadership committed to not closing the Release 13 specification until there was consensus from all stakeholders.
    It was explicitly stated that IEEE 802 was one of those stakeholders.
  However, 3GPP RAN1 closed the Rel 13 specification before it had even responded to the initial comments from IEEE 802, and has effectively ignored most IEEE 802 requests since then
    It is also rapidly completing the eLAA Rel 14 specification without any review so far from IEEE 802
  How should we collaborate better with 3GPP RAN1 going forward?
    Or should we give up?
    Possibly appealing to regulators and “court of pubic opinion”?
    Have we achieved all we need to achieve?