## Slide 1: 920 MHz Regulation Update in Japan
Date: 2024-01-15
Authors:
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Abstract
Share the new 920MHz regulation (Issued: Sep. 2022) [5][6] status in Japan towards Recommended Practice in IEEE 802.19.3a
This document gathers relevant material from 19-18/0053r0, 19-18/0084r0 and 19-19/0018.

## Slide 3: Channelization in Japan
Several wireless systems operate on same frequency band which were standardized as ARIB STD-T106, T107 and T108
ARIB STD-T108 (20mW) on 920.5 ~ 928.1MHz (7.6MHz) includes 802.15.4g system, but coexistence operation with Passive System (250mW) and STD-T108 (250mW) is required for 920.5 ~ 923.5MHz (3.0MHz). So, 923.5 ~ 928.1MHz (4.6MHz) is only channels
928.0
920.6
923.4
1W ARIB STD-T106 Licensed/Registered
250mW ARIB STD-T107 Unlicensed
916.0
919.2
Passive System (RFID, etc)
1mW ARIB STD-T108 Unlicensed
20mW ARIB STD-T108 Unlicensed
250mW ARIB STD-T108 Licensed/Registered
Active System (LPWA, 802.15.4g, etc)
IEEE802.15.4g, etc
Coexistence Operation
Channels for sensor networks
①
②
③
④
⑤
Ch: 200KHz
Ch: 100KHz
MHz
929.65
MCA
MCA: Multi-Channel Access Radio System

## Slide 4: Current Use Cases
Current use cases in the market for each wireless system*1.
Specified Low-Power Radio Station use case is the most likely one to require 802.15.4g and 802.11ah*2 coexistence measures
*1: MIC is going to deregulate the current standard to meet the future use cases (Inside/Outside, Tx Time, Duty Cycle, etc)[3]
*2: IEEE 802.11ah is not specified on ARIB STD-T108 at this moment [2]
② Specified Low-Power Radio Station (Unlicensed, Passive System)
Tx Power: 250mW
Frequency: 916.7~923.5MHz
Use Cases: RFID for inside/outside
ARIB STD-T107
① Indoor Radio Station
(Licensed/Registered, Passive System)
Tx Power: 1W
Frequency: 916.7~920.9MHz
Use Cases: RFID for Logistics Management, etc
ARIB STD-T106
⑤ Land Mobile Station
(Licensed/Registered, Active System)
Tx Power: 250mW
Frequency: 920.5 ~ 923.5MHz
Use Cases: LPWA for sensors (forest, bridge, etc)
ARIB STD-T108
④ Specified Low-Power Radio Station
(Unlicensed, Active System)
Tx Power: 20mW
Frequency: 920.5 ~ 928.1MHz
Use Cases: Smart Mater (Electric, Gas, Water), etc
ARIB STD-T108
③ Specified Low-Power Radio Station
(Unlicensed, Active System)
Tx Power: 1mW
Frequency: 915.9 ~ 929.7MHz
Use Cases: Home Security, Remote Control
ARIB STD-T108
[1][2][3]

## Slide 5: ARIB STD-T108 (20mW)
Specified Low-Power Radio Station (Unlicensed, Active System)*
Item |  | Parameters and functionality
Frequency Band |  | 920.5MHz ~ 928.1MHz (7.6MHz) 920.5 ~ 923.5 MHz (3.0MHz) --- Coexistence with others 923.5 ~ 928.1 MHz (4.6MHz) --- Channel for STD-T108
Channel bandwidth |  | 200KHz
Maximum aggregated channels |  | 5 CHs (1MHz)  920.5 – 923.5 MHz: 15 CHs (4MHz) with CS and Duty Cycle rule [5][6] 920.5 – 928.1 MHz: 20 CHs (4MHz) with CS and Duty Cycle rule [5][6]
Transmission Power |  | 20mW (13dBm)
Transmission method | Contents | Data signal
 | Modulation | Not specified
Antenna Gain |  | 3dBi or less (absolute gain). However, in case EIRP is less than the value of 3dBi plus 1mW or 20mW of antenna power, it is allowed to fill in the gap by the antenna gain
Carrier Sense (CS) and Duty Cycle | CS ≧ 5msec, 920.5 ~ 923.4 MHz | Tx Time ≦ 4sec, Wait ≧ 50ms
 | 5msec > CS ≧ 128us 920.5 ~ 928.1 MHz | Tx Time ≦ 400ms, Wait ≧ 2ms, Total Tx Time ≦ 360s/h/station
Note |  | Refer IEEE 802.15.4g for PHY parameters
[3][4]
*: MIC is going to deregulate the current standard to meet the future use cases [3]
[5][6] define new channel bandwidth up to 4 MHz which issued in Sep. 2022.

## Slide 6: Duty Cycle for Active System
Each specified low-power radio station can transmit radio signal for at most 360 seconds/hour in the current 920MHz regulation.
MIC (Ministry of Internal Affairs and Communications) is considering relaxing the current duty cycle regulation:
  When a specified low-power radio station use multiple channels in time division, duty cycle is 720 seconds/hour.
  Duty cycle of each channel is 360 seconds/hour/station.
[3]
Current regulation
Using single channel
Total Tx Time ≦ 360sec.
Per station ≦ 360sec.
Using multiple channels
360sec.
360sec.
360sec.
100sec.
80
100
80
3600 seconds
3600 seconds
Time
Time
3600 seconds
3600 seconds
Time
Time
360sec.
360sec.
720 sec.
Using multiple channels
Using single channel
Deregulation of Duty Cycle
Total Tx Time ≦ 360sec.
Per station ≦ 360sec.
120sec.
160
90
350

## Slide 7: Summary
802.15.4g specified on ARIB STD-T108 (20mW) can operate on
  920.5 ~ 928.1MHz (7.6MHz) , but
    920.5 ~ 923.5MHz (3.0MHz) --- Coex. with Passive Systems and LPWA
    923.5 ~ 928.1MHz (4.6MHz) --- Channel for sensor nets
MIC had extended the maximum channel numbers from 5 CHs (1MHz) to 20 CHs (4MHz) to support IEEE 802.11ah in 2022
We would like the IEEE 802.19.3a to consider coexistence between 802.15.4g and 802.11ah under the conditions and operational constraints noted above on Recommended Practice.

## Slide 8: References
MIC, http://www.soumu.go.jp/main_content/000544861.pdf, 2018/04/10
MIC, http://www.soumu.go.jp/main_content/000550848.pdf, 2018/05/14
MIC, http://www.soumu.go.jp/main_content/000551143.pdf, 2018/05/15
https://www.arib.or.jp/english/html/overview/doc/5-STD-T108v1_0-E1.pdf
MIC, https://www.soumu.go.jp/main_content/000833183.pdf
MIC, https://www.soumu.go.jp/main_content/000833184.pdf
MIC (Ministry of Internal Affairs and Communications)