## Slide 1: 802.15.4 Coexistence Feature Update TG 19.3a Contribution
Date: 2024-09-09
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Authors:
Name | Affiliations | email
Benjamin Rolfe | BCA, et al | Ben.rolfe @ ieee.org

## Slide 2: Summary
802.15.4 has had several amendments and a revision since 2019
Some useful features have been added to the MAC that we could use to enhance coexistence
Some changes have been made to add flexibility that could be used for coexistence recommendations
This identifies some new or revised features that might be useful to this group

## Slide 3: 802.15.4 Channel Access: 802.15.4-2024 (Revision E)
Multiple CSMA variations
  Multiple Clear Channel Assessment Methods
  Multipole Prioritized CSMA schemes
  Suspendable CSMA-CA algorithm *new*
Multiple scheduled access methods
  Some with, some without CSMA
  Some cleanup in Revision E
  Some changes to make TSCH more general in draft 15.4ab
  Peer-wise coordination (distributed) added in 802.15.4z
  Some use channel access with sensing (listen) in conjunction with scheduled access
New variation of CSMA that uses linear backoff and finer control of timing to support low latency

## Slide 4: Multiple CCA methods
Mode 1: Energy above threshold (ED).
Mode 2: Carrier sense only (CS)
CCA Mode 3: Combination of ED and CS
ED Threshold and Duration variable
Flexibility to meet different operating environments, performance profiles, and regulator requirements

## Slide 5: Random Access: multiple CSMA Variations
Simple unslotted CCA
Slotted CSMA with scheduled access
  Multiple superframe types defined
  TSCH, DSME and RCC support slotted CSMA
CSMA with Priority (PCA)
Added flexibility since 802.15.4-2020 to CCA and CSMA-CA

## Slide 6: Brief look at CSMA
Simple and flexible
  Can reduce to simple LBT without iterative backoff
  Can bound backoff growth

## Slide 7: Optional backoff suspension in CSMA-CA algorithm
Incorporated into 802.15.4-2024 (Rev E)
Adds capability to sensed channel using the selected CCA mode during the backoff delay period.
Provides improved performance in congested spectrum
Grew out of changing requirements in key applications such as smart energy/grid modernization in Japan and other regions
Expands trade-off space for optimizing and adaptation
More information: https://mentor.ieee.org/802.15/dcn/23/15-23-0234-02-04me-proposed-csma-changes.docx
https://mentor.ieee.org/802.15/dcn/23/15-23-0167-00-0000-the-csma-gap-analysis-between-ieee-802-15-4-and-japanese-standard-jj-300-10.pptx

## Slide 8: Added contention-based channel access introduced in draft P802.15.4ab: SSBD
Spectrum Sensing Based deferral
CSMA with linear ba ckoff and a few other changes
Iterative sense/backoff/sense as in CSMA
  Uses linearly growth in random backoff
  Provides for fine resolution bounding of channel access latency
  Intended for low-latency use cases
Include optional persistence
  Simplified version of 802.11 persistent channel access
  Alters channel backoff bounds for retransmission attempts

## Slide 9: SSBD
Similar to CSMA with
  Linear backoff growth
  Can reduce to simple LBT
  Includes fallback to Aloha option
  Optimized for low-latency uses
  Includes optional persistence

## Slide 10: 802.15.4s Spectrum resource measurement (SRM) (rolled into 802.15.4-2024)
Provides functionality and data structures to exchange MAC performance and spectrum characterization information
  Channel access and retransmission performance
  Receiver performance
  Channel characterizations
Could be useful for new coexistence recommendations

## Slide 11: Other possibly interesting things: 802.15.9
Created to support Key Management Protocol transport over 802.15.4
Includes fragmentation which might be useful for link adaptation

## Slide 12: Conclusion
These are just a few of the changes and new features since 2019
Lots of tools we can use
This is only half of the story (802.15.4)
Next step: look into 802.11-2024