## Slide 1: Follow up on measurement of radio noise over Sub-1 GHz band emitted from mini PC and laptop PC, and its impact on communication performance of IEEE 802.11ah
Date: 2025-03-10
Authors:
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Introduction
The sub-1 GHz band is used by not only IEEE 802.11ah and IEEE 802.15.4, but also other radio systems. Moreover, several kinds of machinery emit powerful radio noise in this frequency band, and it may have a large impact on the system performance of wireless communication systems.
Measurement results of radio noise emission over the Sub-1 GHz bands from Mini PCs and laptop PCs were reported [1].
This contribution reports about…
  Calibrated measure spectrogram of radio noise emission from three mini PCs and two laptop PCs,
  Experimental evaluation result of the impact of the radio noise from a mini PC on the communication performance (packet delivery rate and jitter) of IEEE 802.11ah.

## Slide 3: Recap: DUTs (mini PCs)
We measured radio emission from three different mini PCs as in [1]. They are made in different countries/area.
Mini PC-C
Mini PC-B
Mini PC-A
CPU: AMD Ryzen 7 5700U
1.8-4.3 GHz
CPU: AMD Ryzen5 7535U
2.0-4.55 GHz
CPU: Intel Core i7-1165G7
2.8-4.7 GHz

## Slide 4: Recap: DUTs (laptop PCs)
We also measured radio emission from two different laptop PCs. They are manufactured by different vendors.
Laptop PC-A
Laptop PC-B
CPU: Intel Celeron 3865U (Kaby Lake), 1.8 GHz
CPU: Intel Core i5-7200U, 2.50-3.10 GHz

## Slide 5: Recap: Measurement experiment
We conducted measurement in an anechoic chamber. In the experiment, IQ sampling data was recorded by a data logger during 60 seconds in booting the PCs. Measurement covers the Sub-1 GHz bands in EU, USA (US) and Japan (JP).
The recorded I/Q data was converted to spectrogram.
Data logger
LNA
（20dB）
Cable (3.5 m)
DUT
Antenna
Distance between antenna and DUT is changed.
BPF
Mini-Circuits VBFZ-925-S 800M-1050MHz
Mini-Circuits
ZX60-83LN+

## Slide 6: Configurations of spectrum measurement
Sampling: 16-bit sampling for I/Q data @ 80 Msamples/s
Center frequency: 895 MHz
FFT size: 4000 (without overlapping)
Window function: Hann window
Antenna: Monopole antenna
Measurement Distance: 2 cm, 15 cm, 100 cm, 200 cm

## Slide 7: Recap: Measurement environment
Mini PC
(DUT)
Monopole antenna
For 900 MHz band
BPF
Laptop PC
(DUT)
Monopole antenna
For 900 MHz band
Data logger

## Slide 8: Measurement result for 60 seconds (without DUT)
Radio emission from measurement equipment (data logger) is observed at some frequencies.
Distance: 2 cm
Distance: 15 cm
Distance: 100 cm
Distance: 200 cm

## Slide 9: Measurement result for 60 seconds (mini PC-A)
Weak wideband radio emission (lower than -90 dBm / 1 MHz) is observed at 2 cm from mini PC-A. It may affect CCA results and/or transmission performance of IEEE 802.11/15.4 devices if they are operated at a low SNR.
Distance: 2 cm
Distance: 15 cm
Distance: 100 cm
Distance: 200 cm

## Slide 10: Measurement result for 60 seconds (mini PC-B)
Mini PC-B also emits weak wideband radio noise (lower than -90 dBm / 1 MHz) at 2 cm.
Distance: 2 cm
Distance: 15 cm
Distance: 100 cm
Distance: 200 cm

## Slide 11: Measurement result for 60 seconds (mini PC-C)
Strong wideband radio emission (higher than -80 dBm / 1 MHz) is observed at 2 cm from mini PC-C. Even at 15 cm, radio noise level is sometimes higher than -85 dBm / 1 MHz.
Distance: 2 cm
Distance: 15 cm
Distance: 100 cm
Distance: 200 cm

## Slide 12: Measurement result for 60 seconds (laptop PC-A)
The level of radio noise emitted from laptop PC-A is lower than -90 dBm / 1 MHz.
Kazuto Yano, ATR
Distance: 2 cm
Distance: 15 cm
Distance: 100 cm
Distance: 200 cm

## Slide 13: Measurement result for 60 seconds (laptop PC-B)
The level of radio noise emitted from laptop PC-B sometimes exceeds -85 dBm / 1 MHz even at 15 cm.
Distance: 2 cm
Distance: 15 cm
Distance: 100 cm
Distance: 200 cm

## Slide 14: Measurement of communication performance of IEEE 802.11ah near mini PC-C
The receiver power of the radio emission from mini PC-C sometimes exceeds -80 dBm / 1 MHz at 2 cm. This is 15 dB higher than the minimum sensitivity for MCS0 with 1 MHz signal bandwidth of IEEE 802.11ah.
Hence, we measured the communication performance between two laptop PCs using Iperf over IEEE 802.11ah in an anechoic chamber. An IEEE 802.11ah STA is located near mini PC-C.
Router
（DHCP server）
HUB
Laptop PC
Ethernet
5 m
IEEE 802.11ah
STA
IEEE 802.11ah
AP
Laptop PC
2 cm
or
15 cm
mini PC-C
(radio noise source)
Monitor
HDMI

## Slide 15: Configurations of measurement of communication performance
Measurement: 60 s, 10 times
Transmission power: AP = 11.2 dBm or 0.9 dBm, STA = 11 dBm
MCS index: MCS0, MCS3, MCS7
Signal bandwidth: 1 MHz
Center frequency: 921 MHz
Traffic: UDP, 1470 bytes payload
Offered load: 30 kb/s @ MCS0, 84 kb/s @ MCS3, 195 kb/s @ MCS7
Status od mini PC: Power off, booting (flowing boot messages on the screen), high CPU load (using stress command of Linux, no change on the screen)

## Slide 16: Measurement environment
IEEE 802.11ah
AP
IEEE 802.11ah STA and mini PC-C
Distance between
AP and mini PC-C: 5 m
Monitor
IEEE 802.11ah
STA
Mini PC-C

## Slide 17: Packet delivery rate performance
Only when mini PC-C was booting, packet loss occurred in downlink transmission at MCS3 and MCS7. This result implies that data frames collided with radio noise, and the monitor or HDMI cable/connector can also be a radio noise source.
MCS0
MCS3
MCS7

## Slide 18: Jitter performance
When mini PC-C was both booting and at high CPU load, the jitter performance was degraded. In particular, the jitter performance of uplink transmission was degraded only when mini PC-C us at high CPU load. It means that mini PC-C itself emits radio noise.
MCS0
MCS3
MCS7

## Slide 19: Summary
This contribution showed calibrated measurement results of radio noise emitted over the Sub-1 GHz bands from three mini PCs and two laptop PCs at different distances.
  One of mini PC and laptop PC emit strong radio noise. The radio noise level is higher than -85 dBm / 1 MHz at 15 cm from the radio noise source.
This contribution also showed the packet delivery rate and jitter performance of UDP data transmission over an IEEE 802.11ah link near the mini PC that emits strong radio noise.
  The result of experiment showed that the radio noise degrades the communication performance of an IEEE 802.11ah link if an IEEE 802.11ah device is located near the mini PC.
  It was also shown that a monitor or HDMI cable/connector can also be a radio noise source.

## Slide 20: Reference
[1] doc. IEEE 802.19-24/0038r0