| Project | IEEE 802.21 Media Independent Handover Services <http://www.ieee802.org/21/> |
| --- | --- |
| Title | MIH Registration |
| Date Submitted |  |
| Source(s) | Srinivas Sreemanthula, Eric Njedjou, Mathieu Peresse, Yoshihiro Oba |  |
| Ref: | 21-06-0644-02-0000-mih-registration.doc |
| Abstract | This contribution provides clarifications to MIH registration defined in commentary. |
| Purpose | Discuss and adopt in the draft. |
| Notice | This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21. |
| Patent Policy | The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development <http://standards.ieee.org/board/pat/guide.html>. |

## MIH Registration (Insert in section 8.4.1.1)

MIH registration provides a basis for network controlled inter-technology handover framework since it allows UE to select a network control node among many that may be available. This mechanism essentially works as a trigger for network MIH entities to be aware of a UE’s presence. This mechanism is an optional mechanism that enables two MIH entities to create an MIH pairing based on the policies configured in the UE or after capability discovery mechanism. MIH network entities may not be able to provide any MIH services to the UE without this signaling from UE. Following the registration, the MIH network entities can register for events as seen by the multi-radio UE and send commands for handover control. From the UE point of view, the MIH pairing can also be seen as providing authorization for a certain network control node to send MIH commands to leverage inter-technology access resources and improve the overall user experience. While having an established MIH pairing, the UE may not process certain commands originated for other network MIH nodes.

The following figure shows a reference communication state diagram for this MIH registration. Initially, MIH node performs a MIH peer discovery to determine the end point address. After MIH node discovery, MIH node will perform capability discovery to determine what services are supported at the other end followed by the MIH registration to create the pairing. Upon successful registration, the MIH peers can request for specific event registrations/subscriptions or send MIH commands to request for specific actions to be taken.

### MIH_Register.Request

#### Function

This primitive is used by a peer MIH Function to communicate with the MIH Function in the network to perform registration.

#### Semantics of service primitive

MIH_Register.Request

(

Source Identifier (MIH-ID),

Destination Identifier (MIH-ID),

RequestCode

)

Local or Remote: Remote

MIHF (Network) <> MIHF (Network)

MIHF (network) <- MIHF (client)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| Source Identifier | Identifier | Any valid individual or group identifier (e.g. NAI or FQDN) | Source of this message. Optional for re-registration. |
| Destination Identifier | Identifier | Any valid individual or group identifier (e.g. NAI or FQDN) | Destination of this message |
| Request Code | Enumerated type | 0 - Registration 1 - Re-Registration | Re-registration scope to be defined. |

#### When generated

The MIH Function generates this message when it needs to perform a MIH registration to a particular destination MIH function.

#### Effect on receipt

Upon receipt, the MIH Function can verify the credentials and perform additional security measures (not defined in 802.21) to complete the registration.

### MIH_Register.Response

#### Function

This primitive is used by a peer MIH Function to communicate with the MIH Function in the network to indicate the result of a registration request.

#### Semantics of service primitive

MIH_Register.Response

(

Source Identifier ,

Destination Identifier,

ValidityTime,

Result Code,
Failure Code

)

Local or Remote: Remote

MIHF (Network) <> MIHF (Network)

MIHF (network) -> MIHF (client)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| Source Identifier | Identifier | Any valid individual or group identifier | Source of this message |
| Destination Identifier | Identifier | Any valid individual or group identifier | Destination of this message |
| ValidityTime | Integer |  | Time in secs |
| Result code | BOOL | SUCCESS, FAILURE |  |
| Failure code | Enumerated type | Integer | If Result code indicates failure |

#### When generated

The MIH Function generates this message when after completion of registration request processing.

#### Effect on receipt

Upon receipt, the MIH Function can determine that the result of registration request.

### MIH_DeRegister.Request

#### Function

This primitive is used by a peer MIH Function to communicate with the MIH Function in the network to perform a de-registration.

#### Semantics of service primitive

MIH_DeRegister.Request

(

Source Identifier (MIH-ID),

Destination Identifier (MIH-ID),

)

Local or Remote: Remote

MIHF (Network) <> MIHF (Network)

MIHF (network) <- MIHF (client)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| Source Identifier | Identifier | Any valid individual or group identifier (e.g. NAI or FQDN) | Source of this message. Optional. |
| Destination Identifier | Identifier | Any valid individual or group identifier (e.g. NAI or FQDN) | Destination of this message |

#### When generated

The MIH Function generates this message when it needs to perform a MIH de-registration to a particular destination MIH function to deregister a previous registration.

#### Effect on receipt

Upon receipt, the MIH Function can perform de-registration and delete the registration context.

### MIH_DeRegister.Response

#### Function

This primitive is used by a peer MIH Function to communicate with the MIH Function in the network to indicate the result of a deregistration request.

#### Semantics of service primitive

MIH_DeRegister.Response

(

Source Identifier ,

Destination Identifier,

Result Code,

Failure Code

)

Local or Remote: Remote

MIHF (Network) <> MIHF (Network)

MIHF (network) -> MIHF (client)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| Source Identifier | Identifier | Any valid individual or group identifier | Source of this message |
| Destination Identifier | Identifier | Any valid individual or group identifier | Destination of this message |
| Result code | BOOL | SUCCESS, FAILURE |  |
| Failure code | Enumerated type | Integer | If Result code indicates failure |

#### When generated

The MIH Function generates this message when after completion of deregistration request processing.

#### Effect on receipt

Upon receipt, the MIH Function can determine that the result of deregistration request.

### MIH_Registration Request (Create 8.5.1.3)

| Name | Type | Length | Value |
| --- | --- | --- | --- |
| Source Identifier | xxx | variable | MIHF-ID (e.g. NAI or FQDN) |
| Destination Identifier | xxx | variable | MIHF-ID (e.g. NAI or FQDN) |
| Request Code | xxx | BOOL | 0 - Registration 1 - Reregistration |

### MIH_Registration Response (Create 8.5.1.4)

| Name | Type | Length | Value |
| --- | --- | --- | --- |
| Source Identifier | xxx | variable | MIHF-ID (e.g. NAI or FQDN) |
| Destination Identifier | xxx | variable | MIHF-ID (e.g. NAI or FQDN) |
| Validity Period | Integer | 4 | Time Registration is valid |
| Reg Result Code | BOOL | 1 | 1 - Success; 0 - Failure |
| Reg Failure Code | Enumerated value | Enum | TBD |

### MIH_DeRegistration Request (Insert into 8.5.1.5)

| Name | Type* | Length | Value |
| --- | --- | --- | --- |
| Source Identifier | Xxx | variable | MIHF-ID (e.g. NAI or FQDN) |
| Destination Identifier | Xxx | Variable | MIHF-ID (e.g. NAI or FQDN) |

### MIH_DeRegistration Response (Insert into 8.5.1.6)

| Name | Type* | Length | Value |
| --- | --- | --- | --- |
| Source Identifier | Xxx | variable | MIHF-ID (e.g. NAI or FQDN) |
| Destination Identifier | Xxx | Variable | MIHF-ID (e.g. NAI or FQDN) |
| Reg Result Code | Xxx | BOOL | 1 - Success; 0 - Failure |
| DeReg Failure Code | Xxx | Enum | TBD |

* Need to define the type codes for new elements.