Figure 1 MIH services and their initiation

(Alice: I couldn’t decide the thick one or the thin one. Since the updated text doesn’t describe the additional network 1 or network 2, I removed it. Actually it was better to show multiple instances of link layer technologies here -Vivek)

Figure 4 General MIHF reference model and SAPs

(Alice: since all the components can communicate through the SAP, I removed the arrows from the power point slides. OK -Vivek

Figure 6 MIH reference model for IEEE 802.3

Figure 7 MIH reference model for IEEE 802.11

(Alice: The picture is a little bit imbalanced. this probably needs communication with TGu?....Show MIHF extending down…)

Figure 8 MIH reference model for IEEE 802.16

BTW, Figure 9 and 10 in the original doc needs to update MIH-3GLINK-SAP to MIH_3GLINK_SAP.

# Text boxes

Information Service

LLC_SAP

Event Service

LLC_SAP

MIH_LINK_SAP

MIH_LINK_SAP

MIH_SAP

MIH_NET_SAP

Information Service

Media Independent Handover Function (MIHF)

MIH Event Service

MIH Command Service

MIH Information Service

Link Layer
(802.3, 802.11, 802.16)

Command Service

L3
Transport


L2
Transport

Command Service

Link Layer                          (802.11, 802.16, 802.3, ….)

MIH Function

Event Service, Command Service, Information Service

MIH Users

Layer 3 or higher Mobility Protocol (L3MP)

MIH Users

Layer 3 or higher Mobility Protocol (L3MP)

Event Service

Information Service

MIH_SAP

LSAP

LLC-Logical Link Control 
or other MAC Client

MIH_SAP

PHY

Event Service

Media Independent Handover Function (MIHF)

MIH Event Service

MIH Command Service

MIH Information Service

CS_SAP

MAC

MIH Users

Layer 3 or higher Mobility Protocol (L3MP)

PLME_SAP

LLC

LSAP

MAC State

Convergence Function

MSCF_SAP

MSCF_SME_SAP

MLME_SAP

SME

PLME

MLME

MLME_PLME_SAP

PLCP and PMD sublayers

PHY_SAP

MAC

MAC_SAP

Command Service

Media Independent Handover Function (MIHF)

MIH Event Service

MIH Command Service

MIH Information Service

MIH Users

Layer 3 or higher Mobility Protocol (L3MP)

MIH_SAP

Security Sublayer

MAC Common Part Sublayer (MAC CPS)

Management Entity

MIH_SAP

MIH_SAP

Media Independent Handover Function (MIHF)

MIH Event Service

MIH Command Service

MIH Information Service

Layer 3 or higher Mobility Protocol (L3MP)

Service-Specific Convergence Sublayer (CS)

MAC_SAP

PHY_SAP

PHY

C_SAP

M_SAP

Information Service

Event Service

Command Service

LLC_SAP

MIH_LINK_SAP

Network 1

(e.g. 802.16)

MIH Function

Event Service, Command Service, Information Service

MIH Users

Layer 3 or higher Mobility Protocol (L3MP)

LLC_SAP

MIH_LINK_SAP

Network 2

(e.g. 802.11)