| Project | IEEE 802.21 MIH <http://www.ieee802.org/21/> |
| --- | --- |
| Title | 802.21 D11.0 Table 22 |
| Date Submitted | June 18, 2008 |
| Source(s) | Yuu-Heng Alice Cheng (Telcordia) and Yoshihiro Ohba (Toshiba) |
| Re: | IEEE 802.21 Session #27 in July 2008 |
| Abstract | Additional fields required for Table 22 in D11.0 |
| Purpose | Sponsor Ballot recirculation 4 comment resolution |
| Notice | This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21. |
| Patent Policy | The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development <http://standards.ieee.org/board/pat/guide.html>. |

# Introduction

It is not sufficient to use only ACK-Rsp bit to distinguish source and destination state machine for response messages. Because piggy back response messages (S) and the ACK response for a response (D) are both response messages with ACK-Rsp. The difference between the two messages are if additional payload exists.

# Proposed resolution

Update Table 22 as following

State Machines to be searched for incoming message

| Operation code | Destination identifier TLV | ACK-Rsp bit | Contains MIH service specific TLVs or a fragment payload | State machine instances to be searched: transaction source state machine (S) or transaction destination state machine (D) |
| --- | --- | --- | --- | --- |
| Request (0x1) / Indication (0x3) | - | 0 | - | D |
|  | - | 1 | - | S |
| Response (0x2) | Broadcast | - | - | D |
|  | Unicast | 0 | - | S |
|  |  | 1 | Yes | S |
|  |  |  | No | D |