## Slide 1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: 21-09-0059-01-0sec
Title: TGa_Proposal_Antonio_Izquierdo (Protecting the Information Service end-to-end with Hash Trees).
Date Submitted: July 2, 2009
Present at IEEE 802.21 meeting in July of 2009
Authors: Antonio Izquierdo (NIST), Nada Golmie (NIST), Lily Chen (NIST) and David Cypher (NIST)
Abstract: In this document an understanding of the existing capabilities and architecture contained in IEEE Std. 802.21-2008 is presented; a question is asked about a new service feature; and a proposal is made, if the answer to the question is yes. The proposal is to use hash trees as a mechanisms to provide end to end security services for the Information Service.
<number>
Notes: <number>

## Slide 2
<number>
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as stated in Section 6 of the IEEE-SA Standards Board bylaws <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/faq.pdf>
Notes: <number>

## Slide 3: Outline
MIH specific protection
Part I
  Usage scenarios
Part II
  Information distribution
  A question before proceeding
Part III
  Information structure
  Trust assumptions
  Protecting the messages
  Protecting the information
  Required signaling
  Discussion topics
Summary

## Slide 4: MIH specific protection
In this document we discuss an MIH specific protection mechanism.
This protection mechanism is independent of the MIH access authentication used for access controls.
Work Item # | Supported Functionality | Note
1 | Proactive Re-Authentication | NO
1 | EAP Pre-authentication | NO
1 | Key Hierarchy and Derivation 1 | NO
1 | Higher-Layer Transport for MN-CA, MN-SA and SA-CA signaling | NO
1 | Link-Layer Transport for MN-SA signaling | NO
1 | Authenticator Discovery Mechanism | NO
1 | Context Binding Mechanism | NO
2 | Access Authentication | NO
2 | MIH-Specific Authentication | NO
2 | Key Hierarchy and Derivation 2 | NO
2 | MIH-Specific Protection | YES
2 | Protection by MIH Transport Protocol | NO
2 | Visited Domain Access | NO

## Slide 5: Part I
Existing capabilities and architecture contained in IEEE Std. 802.21-2008

## Slide 6: IEEE Std 802.21 – Information Service
From 5.3.4, 6.5, 7.4.25, and 8.6.4
Outside the scope
  The definition of the information server
  How the information is developed or deployed.
  The algorithm for deciding what information to provide
What is defined
  Structure and semantics
  Primitives
  Messages
  A framework by which an MIHF discovers and obtains network information

## Slide 7: Information Request / Response
Using Figure 20 MIIS information flow, we apply tangible devices to the logical functions
When accessing the Information Service, a client (local) and a server (remote) exchange request and response messages.
Depending on the location of the Point of Service (PoS) and the entity requesting the information, the exchange may take place between different pairs of nodes as shown in Figures a-d.
  IS is a POS which provides at least the MIH information service (MIIS) and is not a PoA for the MN.
  MN is a mobile node
  PoA is a point of attachment (depending on the role at an instant in time the PoA may also be a point of service when it is offering services (e.g., as a server))
a
b
c
d
[POS]

## Slide 8: Part II
A Question (or Questions)

## Slide 9: Information distribution using MIH
Using the functions and capabilities in IEEE Std. 802.21-2008, information distribution among MIH nodes can proceed as follows:
  Any MIH node can potentially request information from a POS offering the information services and redistribute that information.
    The MN can build its information by directly requesting information from an IS (a PoS offering information services).
    An IS or PoA can build or augment its information by requesting information from another IS.
    The source and destination MIHF addresses in the MIH_Get_Information request / response messages are pair wise between the two MIHF entities.

## Slide 10: Situation to be Considered
The information received in an “Information Response” consists
  Information (IA) originated from the direct “server” who sends the message “Information Response”; and
  Information (IB) not originated from the direct “server” but someone else.
However the client sees no difference in the information. From its view point it is just information coming from the sender of the “Information Response”
Information Response
IA
IB

Client
Server
IA
IB

## Slide 11: The question(s)
Do you (MIHF requestor) want the function, feature, or capability to know who originally generated the information contained in the MIH_Get_Information_Response message (MIHF responder)?
Do you want the function, feature, or capability to know who originally generated the information in the MIH_Push_Information indication message?
Information Response
IA
IB

Client
Server
IA
IB

## Slide 12: Part III
A proposal
  Conditional on a Yes answer to the question(s) in Part II

## Slide 13: Main Challenge
If the information is protected through digital signature by the original Information Server (IS), then when an intermediate PoS composes a response for a client, the signature will not be valid any more, if the response
  only includes a subset of the information; or
  consists of information pieces from different signatures.
A
B
Sig
A
Sig
B
Sig
IS
Intermediate PoS
MN1
MN2

## Slide 14: Main Contribution
A scheme to allow an intermediate PoS re-using the information from the IS to form responses for different clients with end to end integrity protection and information origination authentication from the IS to clients.
A
B
Sig
A
Sig
B
Sig
IS
MN1
MN2
Intermediate PoS

## Slide 15: Trust Assumptions
Each Information Server is trusted to generate information over which it has authority (authorized IS):
  E.g., a network-wide IS can provide information about the whole network, while a local IS may only provide information about its subnet.
The messages exchanged between the different entities are protected through the transport protocols such as IPsec and TLS.
The intermediate PoSs are trusted to cache, access, re-use the information provided by the IS.
However can we trust the PoS to deliver all the information requested and available to it?
  Probably not policy constraints

## Slide 16: Main Idea
Generally, a signature on data A and B can be generated in two steps
  Use hash function h to generate a hash value h (A ||B)
  Apply a public key algorithm S on h(A ||B) to obtain a signature Sig(A||B) = S(H(A||B)).
A hash tree is introduced to generate the final hash value for the signature.
A
B
H(A)
H(B)
H(H(A)||H(B))
S
Sig = Sig(H(A)||H(B))
Hash Tree

## Slide 17: Using Hash Trees
Assume that a PoS provides only information A to a client. But the signature is generated over a tree with leaf A and leaf B. Then it will send A, h(B) and signature Sig.
A
H(A)
H(B)
H(H(A)||H(B))
S
Sig = Sig(H(A)||H(B))
Hash Tree
Information piece B is not provided. However, the signature can be verified without B.

## Slide 18: Information Structure
The information is structured as a logical tree.
  Basic data types are the leaves of the tree.
  Each container Information Element (IE) or data type (e.g., lists) is an intermediate node (and the root of a sub-tree).
  The IE that provides the information requested is the root of the tree.

## Slide 19: Protecting the information (1)
By using hash trees it is possible to maintain the integrity and proof of information origination in an end to end fashion even if
  Only partial information in a tree is included; or
  The information is selected from different responses from IS (In this case, multiple signatures may be included).
The root of the tree is signed by the authorized IS that generated the information.
  This allows the MN to verify the authenticity of the information under the root.

## Slide 20: Protecting the information (2)
The intermediate PoS can filter the information provided to a MN by removing part of the information tree and providing its hash instead.
  The MN would use the hash to validate the rest of the tree.
The intermediate PoS can store the information and the signature and reuse them to compose responses for later requests.
  The signature will be valid as long as the information is not altered.
The hashes may be added to the Information Elements and data types of interest or stored in a separate structure.

## Slide 21: Protecting the information (3)
Changes into
Modifying the IEs and data types

## Slide 22: Protecting the information (4)
Using a separate structure
Additional hash information

## Slide 23: Required signaling
In order for this mechanism to work, the MN has to be able to compute the hash of the information elements and data types in the same way as the authorized IS did, and validate the digital signature of the root.
This means that the MN and the authorized IS have to agree on the hashing and signing algorithms, and the structure of the hash tree (what elements are leaves and which ones are intermediate nodes)
The MN must also have access to the required public keys and their certificates of the different authorized ISs.
Several mechanisms and protocols can be used to negotiate these parameters, including:
  TLS
  IKE
  SIP
  Etc

## Slide 24: Discussion Topics
Hash trees:
  What is the minimum data type or container to be considered a leaf?
  How are the elements removed from the tree?
    Are they substituted by ‘dummy’ elements?
  What is the ‘signing’ policy: Information Elements? Lists?
    Signing top elements reduces the signature validations required per request.
    Signing low elements allows for more flexibility for the intermediate PoS to cache and reuse information.
Signaling:
  What functionalities are required for the signaling?
    Can they be integrated with the access control and / or authentication?
  What is the most appropriate protocol or mechanism to perform the signaling?
  When is the signaling performed?

## Slide 25: Summary
Part I
  IEEE Std 802.21-2008 provides capabilities, as is, for distributing information.
Part II
  Information distribution
  The Question: Is knowing who originated the information important?
  If no, STOP here
  If yes, please continue to part three
Part III
  Propose using hash trees for securing information distributed throughout the network.
    Securing the information service requires security mechanisms to apply protections on the information in an end to end manner.
      Mobile Nodes must be able to verify that the information they gathered through the information services is indeed provided by an authorized server and has not been tampered with even if the other PoSs are caching and / or filtering the information.
    Hash trees make it possible to fulfill the above security requirements.