## Slide 1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: 21-09-0060-00-0sec
Title: Security Related Information Elements
Date Submitted: April 22, 2009
Present at IEEE 802.21 meeting in May of 2009
Authors: Antonio Izquierdo (NIST), David Cypher (NIST), Nada Golmie (NIST), and Lily Chen (NIST)
Abstract: This document proposes a set of information elements to facilitate fast handovers.
<number>
Notes: <number>

## Slide 2
<number>
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as stated in Section 6 of the IEEE-SA Standards Board bylaws <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/faq.pdf>
Notes: <number>

## Slide 3: Outline
The Needs for Security Related Information Elements (IEs)
IEs for Establishing Layer 2 (L2) Authenticated and Protected Link
IEs for Establishing Layer 3 (L3) Security Associations
IEs for Security Policies and Capabilities
Use Scenarios for Proposed Information Elements
Discussion Topics and Next Steps
<number>
Notes: <number>

## Slide 4: Proposal Characterization List
Work Item # | Supported Functionality | Note
1 | Proactive Re-Authentication | No*
1 | EAP Pre-authentication | No*
1 | Key Hierarchy and Derivation 1 | No
1 | Higher-Layer Transport for MN-CA, MN-SA and SA-CA signaling | No
1 | Link-Layer Transport for MN-SA signaling | No
1 | Authenticator Discovery Mechanism | Yes*
1 | Context Binding Mechanism | No
2 | Access Authentication | No*
2 | MIH-Specific Authentication | No*
2 | Key Hierarchy and Derivation 2 | No
2 | MIH-Specific Protection | No
2 | Protection by MIH Transport Protocol | No
2 | Visited Domain Access | No
Note*: Does not propose or modify security mechanisms.
It provides information for the decision of what security mechanisms to invoke.

## Slide 5
In order to make a handover decision, the authentication mechanisms required by the targeted Point of Attachments (PoAs) are important. The information may include
Authentication methods
  If Extensible Authentication Protocol (EAP) methods are used for authentication, then
    Which EAP methods?
      The time it takes to execute EAP-TLS is different from EAP-GPSK
    Whether it supports an EAP re-authentication and/or a pre-authentication
  If it is not an EAP authentication, then what it is?
<number>
Security Information (L2)
EAP Re-Auth
3GPP AKA
EAP TLS
Notes: <number>

## Slide 6
In order to select a new access router, the mechanism for security association establishment may be needed such as,
Whether to support IKEv2 Mobility and Multihoming Protocol (MOBIKE) to optimize the establishment of the new IPsec security associations.
<number>
Security Information (L3)
PAR
NAR
222.101.009.110
108.101.000.110
Notes: <number>

## Slide 7: Security Information (Policies)
AR1
AR2
Information on security policies may be considered to make sure that
the handover decision is made with a network whose security policies comply with the requirements of the mobile node’s home network.

## Slide 8: IEs for Establishing L2 Authenticated and Protected Link*
The L2 Security IEs may carry the following information
Authentication Protocol | EAP, 3GPP AKA, etc
EAP-methods | EAP-TLS, EAP-GPSK, EAP-TTLS, etc
EAP Re-authentication | Yes or No
EAP Pre-authentication | Yes or No
*The information about media specific security mechanisms, such as different cipher suites in 802.11, may be obtained through L2 advertisements.

## Slide 9: IEs for Establishing L3 Security Associations
The L3 Security IEs may carry the following information
Support MOBIKE | Yes or No

## Slide 10: IEs for Security Policies and Capabilities
IEs for security policies and capabilities may carry the following information.
Security policies and capabilities may be presented at each layer.
Accept open authentication | Yes or No
Accept password based EAP method | Yes or No
The identifier of the certificate authority | 

## Slide 11: Use Scenario for Proposed IEs - Prior to authentication with any PoA (UIR=1)
MN
Candidate PoA1
MIIS
Information Request (UIR =1)**
Information Response (with Security IEs about PoA1 and PoA2 and AR)**
PoA2 is selected
Authentication*
Candidate AR***
Establish security association for IPsec with IKE
[Handshake for layer 2 protections]
*The right end of the arrow is not the end point for the information but a pass through entity.
Data Traffic*
Candidate PoA2
Advertisement
Advertisement
AR
** The message can be passed through the link with PoA1 or PoA2.
*** There could be more than one ARs.
AR is selected

## Slide 12: Use Scenario for Proposed IEs After connected (UIR = 0)
MN
Current PoA_1
PAR
MIIS
Information Request (UIR = 0)
Information Response (with Security IEs)
Make handover decision with the time needed for authentication
Selected PoA
Re-Auth, Pre-Auth or full Auth or Other Auth*
NAR
Establish security association for IPsec with MOBIKE or IKE
Since the handover decision is made with the estimated time for authentication and other security procedures, it minimize disruption to the data traffic.
[Handshake for layer 2 protected communications]
*The right end of the arrow is not the end point for the information but a pass through entity.
Data Traffic*

## Slide 13: Security IEs representations
Additional IEs to current IEEE Std. 802.21-2008 structure
  General information elements
  Access network specific information elements
  PoA-specific information elements
  PoA-specific higher layer service information elements
Add new IE(s) to existing
  IE_CONTAINER_NETWORK
  IE_CONTAINER_POA
Individual IEs or Data structured IEs
Reference IEEE Std. 802.21-2008 6.5.6.2, Annex F (F.3.9), and Annex G
Separate security structure containing IEs for security
  Define a security container
    IE_CONTAINER_SECURITY
  Include security IEs
    High layer
      Policies
    Layer 3
      MOBIKE
    Layer 2
      Authentication Protocol

## Slide 14: Security IEs representations (graphic)
Additional individual IEs to current IEEE Std. 802.21-2008 structure
Name of information element | Description | Data type
General information elements |  | 
… |  | 
Access network specific information elements |  | 
IE_SEC_OPEN_AUTHENTICATION |  | BOOLEAN
IE_SEC_PASSWORD_BASED_EAP_METHOD |  | Tbd
IE_SEC_CERTIFICATE_AUTHORITY_ID |  | Tbd
PoA-specific information elements |  | 
IE_SEC_AUTHENTICATION_PROTOCOL |  | Tbd
IE_SEC_EAP_METHODS |  | Tbd
IE_SEC_EAP_REAUTHENTICATION |  | BOOLEAN
IE_SEC_EAP_PREAUTHENTICATION |  | BOOLEAN
PoA-specific higher layer service information elements |  | 
IE_SEC_SUPPORT_MOBIKE |  | BOOLEAN

## Slide 15: Security IEs representations (graphic)
One IE with data structure instead of multiple individual IEs
Name of information element | Description | Data type
PoA-specific information elements |  | 
IE_SEC_AUTHENTICATION_PROTOCOL |  | X1
Data type name | Derived from | Definition
X1 | SEQUENCE ( CHOICE(NULL, EAP), CHOICE(NULL, OTHER) ) | 
EAP | SEQUENCE ( CHOICE(NULL, FULL), CHOICE(NULL, Pre_authentication), CHOICE(NULL, Re_authentication) ) | 
FULL | UNSIGNED_INT(1) | Values 0: EAP-TLS 1:EAP-GPSK 2: EAP-AKA 3-255 Reserved
OTHER |  | 

## Slide 16: Security IEs representations (graphic)
Separate security structure containing IEs for security
IE_CONTAINER_SECURITY_INFORMATION | 
Information element ID = (see Table G.1) | Length = variable
IE_SEC_OPEN_AUTHENTICATION | 
IE_SEC_PASSWORD_BASED_EAP_METHOD | 
IE_SEC_CERTIFICATE_AUTHORITY_ID | 
IE_SEC_AUTHENTICATION_PROTOCOL | 
IE_SEC_EAP_METHODS | 
IE_SEC_EAP_REAUTHENTICATION | 
IE_SEC_EAP_PREAUTHENTICATION | 
IE_SEC_SUPPORT_MOBIKE | 

## Slide 17: Discussion Topics and Next Steps
Discussion Topics
  Shall we include information elements with respect to whether a local re-authentication server is available for a given candidate PoA, if re-authentication is supported?
  Shall we include whether direct or indirect pre-authentication is supported?
  What security related IEs should be included in non-connected situations (i.e. Unauthenticated Information Request (UIR) = 1)?
  Is there any other factor which should be considered?
Next steps
  Identify necessary security related IEs.
  Define the IEs.
  Analyze compatibility with the existing IEs.

## Slide 18: Summary
Establishing a new security link is a time consuming procedure in a handover.
The time consumption must be considered when making a handover decision and a network selection.
802.21a shall define information elements to facilitate seamless and secure handover.