## Slide 1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: 21-09-0062-00-0sec
Title: Solution Proposal for 802.21a TG
Date Submitted: May, 03, 2009
Presentation at IEEE 802.21a in Montreal, March, 2009
Authors or Source(s):
Anirudh Bhatt, Shubhranshu Singh (Samsung)
Abstract: This is a solution proposal contribution for the 802.21a TG in response to 21-09-0044-00-0sec call-for-proposals. Intention is to further discussion and accordingly update the slides. It addresses work item #1 as well as work item #2, as mentioned in the 21-09-0017-02-0sec & 21-08-0172-02-0sec

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/guide.html>

## Slide 3: Presentation Scope
The proposal addresses below two work items mentioned in the IEEE 802.21a PAR
  Work Item #1: Mechanisms to reduce the latency during authentication and key establishment for handovers between heterogeneous access networks that support IEEE 802.21
  Work Item #2: Mechanisms to provide data integrity, replay protection, confidentiality and data origin authentication to IEEE 802.21 MIH protocol exchanges and enable authorization for MIH services

## Slide 4: Proposal Characterization List
This proposal supports the below functionalities:
Work Item # | Supported Functionality | Reference to TR section(s) | Note (Supported?)
1 | Proactive Re-Authentication | 2.3.3 | YES
1 | EAP Pre-authentication | 2.3.2 | YES
1 | Key Hierarchy and Derivation 1 | 2.3.3.1 | YES
1 | Higher-Layer Transport for MN-CA, MN-SA and SA-CA signaling | 2.3.2.3 | 
1 | Link-Layer Transport for MN-SA signaling | 2.3.2.3 | 
1 | Authenticator Discovery Mechanism | 2.3.2.3, 2.3.3.4 | YES
1 | Context Binding Mechanism | 2.3.2.3, 2.3.3.4 | 
2 | Access Authentication | 3.6.1 | YES
2 | MIH-Specific Authentication | 3.6.2 | YES
2 | Key Hierarchy and Derivation 2 | 3 | 
2 | MIH-Specific Protection | 3.6.1.1, 3.6.2.1 | YES
2 | Protection by MIH Transport Protocol | 3.6.1.2, 3.6.2.2 | YES
2 | Visited Domain Access | 3.6.3.1 | 

## Slide 5: Terminologies
Terminologies as defined in the TR are applicable

## Slide 6: Work Item #1: Mechanisms to reduce the latency during authentication and key establishment for handovers between heterogeneous access networks that support IEEE 802.21

## Slide 7: Assumptions
Applicable in particular in the scenarios where only one radio can operate at a given time
Slides are prepared in particular for inter-technology handover scenario where EAP is used for access authentication protocol
The proposed solution is applicable to network initiated as well as mobile initiated scenarios
HOKEY key hierarchy RFC5295 is supported by the employed EAP methods

## Slide 8: Requirements
Requirements listed in the TR are applicable. Some additional requirements are:
  Any key should be transported with its integrity and confidentiality maintained
  The derived keys from the root keys must be cryptographically separate
  A key Distribution Exchange mechanism may be used to distribute the keys to the appropriate MIH PoS entity

## Slide 9: Proposed Solution
The main objective is to pre-establish the key at the target authenticator before MN movement.
We propose to transport the specific keys, along with any context information
    We call this key as “pre-authentication root key” and is derived from the EMSK
    For transferring the key (and confirmation) along with any relevant context information, MIH_MN/Net_HO_Query_Resources.request & MIH_N2N_HO_Query_Resources.response or MIH_MN/Net_HO_Commit request & MIH_N2N_HO_Commit response messages’ extension is used
    Details of usage definitions of the key along with the management of the root keys to follow this proposal version (in the text version of the proposal)

## Slide 10: Proposed Solution (Contd…)
Pre-authentication assumes the prior knowledge of the target authenticator.
  Wherever possible, this can easily be learnt by exploiting the availability of IS
    MIH_Get_Information.request & MIH_Get_Information.response with new IE is used for the purpose

## Slide 11: ERP Based Approach
To achieve low latency handovers, we propose re-authentication protocol that completes in less than 2 round trips, in accordance with RFC 5296
  Before MN moves to the target network, it sends the trigger or command message to the Authentication server via target authenticator
  The trigger/command message carries information to derive keys from key hierarchy
  The AAA server verifies that MN has previously authenticated successfully and then derives relevant key and transports it to candidate authenticator over AAA protocol along with confirm message

## Slide 12: An example flow sequences for our ERP based approach
ERP Based Approach (Contd…)

## Slide 13: Work Item #2: Mechanisms to provide data integrity, replay protection, confidentiality and data origin authentication to IEEE 802.21 MIH protocol exchanges and enable authorization for MIH services

## Slide 14: Assumptions
Out of scope
  Entity and capability discovery [3.5 GA2]
Requirements
  Access Control using AAA [3.5 GA5]
  Mutual Authentication using AAA or CA [3.5 GA6]
  MIH specific protection [3.5 GA7]
  Transport Protocol protection [3.5 GA7]
  PoS and PoA co-location not considered [3.5 GA4]
  L2 and MSTP transport supported [3.5 GA1]

## Slide 15: Generic MIH SAP Reference Model
MIH USER
TRANSPORT SERVICE
PROVIDER
MEDIA SPECIFIC
SAP
SECURITY
MODULE
MIH_SAP
MIH FUNCTION
MIH_LINK_SAP
MIH_NET_SAP
MIH_SEC_SAP

## Slide 16: SAP Considerations
Security Module
  Will provide facilities for MIH entity authentication and MIH protocol security
  MIH messages may broker security to be used as well as initiate/piggyback the authentication process
MIH_SEC_SAP shall provide functionalities for interacting with external security module
  Most MN shall have security functionalities provided by OS/middleware
  MIHF can manage and maintain process transparent security credentials like keys

## Slide 17: Security Profile
Can be managed at MIH User
  MIH User to Security Module communication out of scope
Can be informed as part of capability discovery mechanism
  Authentication mechanism supported
  Security mechanism supported
  AAA Server information
Proposed new parameters for MIH_Capability_Discover
  MIHAuthenticationMechanismList
  MIHSecurityMechanismList

## Slide 18: Authentication
Authentication method brokering
  Can be done with MIH_Capability_Discover
  MIH User will have to take a call on what mechanism to use
Authentication initiation
  MIH_Register Message
  Piggyback brokered MIHAuthneticationInformation and request for supported MIHSecurityMechanismList
  TLV to be utilized by MIH User and Security module
  Security Module starts Authentication based on brokered authentication mechanism used
  MIH User on the peer MIH node will send a MIH_Register.Response message back after a successful authentication with a agreeable MIHSecurityMechanismList
    Security module – MIH User communication out of the scope
Alternate key distribution mechanism using existing trust relationship between MIH entities should be used

## Slide 19: Authentication (Contd…)

## Slide 20: MIH Based Security
MIH Packets injected by MIH_SAP may be sent to the Security Module thru MIH_SEC_SAP for protection
  MIH_SEC_SAP will output MIHProtocolPDU for the MIH_TP_Data.Request function
  MIH_TP_Data.Indication will yield MIHProtocolPDU which will be given to the MIH_SEC_SAP for decryption/verification
  For Use case 1.1 and 2.1 [MIH based Security]
MIH Security [integrity/confidentiality/etc] can be provided using standard algorithms and techniques
  AES can be an example algorithm
Different aspects may be dealt separately as per security needs
  Someone may decide to have MN – IS communication to only have integrity
  Can be reflected in the brokered security mechanism

## Slide 21: Transport Protocol Protection
MIH_SEC_SAP need not be used in case of transport protocol protection
MIH_TP_Data can be used as is
Transport service provider (e.g. MSTP, IPSEC) will protect the MIH PDU as required
  The transport protocol security limitations and needs can be brokered during authentication
  MIH User may communicate with the transport protocol service provider/security module for providing required protection

## Slide 22: Thanks!