## Slide 1
21-04-00xx-00-0021
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN:
Title: TGa_Proposal_Rafa_Marin
Date Submitted: May 03, 2009
Presented at IEEE 802.21 session May 2009 in Montreal
Authors or Source(s):
Rafael Marin-Lopez (UMU), Fernando Pereñiguez(UMU), Fernando Bernal (UMU), Antonio F. Gomez (UMU)
Abstract: Architecture for Proactive EAP Re-authentication aimed for reducing the latency of network access authentication based on EAP. It is based on the design of a new EAP method (EAP-FRM).

## Slide 2
21-04-00xx-00-0021
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/guide.html>

## Slide 3: Table of content
21-04-00xx-00-0021
Proposal Characterization List
Pro-active EAP Re-authentication based on ERP
Proposal: Proactive EAP Re-authentication based on EAP-FRM
  Architecture
  Proactive Operation
  Use Cases
  Implementation
  EAP-FRM packets
  Possible AAA extensions
  Security remarks
Prototype
Discussion
Summary

## Slide 4: Proposal Characterization List
21-04-00xx-00-0021
*Possible use.
Work Item # | Supported Functionality | Note
1 | Proactive Re-Authentication | Yes
1 | EAP Pre-authentication | No
1 | Key Hierarchy and Derivation 1 | No
1 | Higher-Layer Transport for MN-CA, MN-SA and SA-CA signaling | No
1 | Link-Layer Transport for MN-SA signaling | No
1 | Authenticator Discovery Mechanism | No
1 | Context Binding Mechanism | No
2 | Access Authentication | No*
2 | MIH-Specific Authentication | No
2 | Key Hierarchy and Derivation 2 | No
2 | MIH-Specific Protection | No
2 | Protection by MIH Transport Protocol | No
2 | Visited Domain Access | No

## Slide 5: Pro-active EAP Re-authentication based on ERP
21-04-00xx-00-0021
EAP Extensions for EAP Re-authentication Protocol (ERP)
EAP - Initiate / Re-auth-Start
EAP- Initiate/ Re-auth[seq,authP]
EAP - Finish / Re-auth[seq,authS]
AAA (EAP- Initiate/ Re-auth[seq,authP]
AAA(EAP - Finish / Re-auth[seq,authS]
MN
(ER Peer)
Candidate Authenticator
(MIH PoS)
(ER Authenticator)
ER Server
Serving
Authenticator

## Slide 6: Pro-active EAP Re-Authentication based on ERP
21-04-00xx-00-0021
Drawbacks:
  It requires modifications in current EAP peers, EAP authenticators and EAP/AAA servers.
  It modifies the standard EAP state machines.
  Current EAP lower-layers require modifications
    Standard wireless technologies and protocols that use EAP need to be modified.
  Potential harder deployment.
Is it possible a solution that alleviates these problems by keeping a reduced latency for network access authentication?
  Tradeoff: easier deployment vs reduced latency.

## Slide 7: Proposal: Proactive EAP Re-Authentication based on EAP-FRM
21-04-00xx-00-0021
We have defined an architecture for fast EAP re-authentication based on a new EAP method (EAP-FRM).
The architecture supports Proactive EAP Re-authentication.
EAP-FRM works on a standalone EAP authenticator but the method itself can contact a backend authentication server.
Achieved Goals:
  Reduce the impact on existing EAP standards and wireless technologies.
  Keep reduced number of roundtrips to get fast access network and fast proactive EAP re-authentication operation.
  Flexibility for allowing operators to choose whatever fast re-authentication protocol they may design or already designed.

## Slide 8: Architecture
21-04-00xx-00-0021
EAP authenticator is configured to start EAP-FRM when EAP authentication is needed instead EAP Request/Id.
If MN doesn’t support EAP-FRM it sends EAP-Response/Nak. and EAP auth. starts EAP-Request/Id.
If MN supports EAP-FRM, it sends EAP-Response/FRM with fast re-authentication information.
EAP authenticator may or may not contact a backend authentication server.
EAP transport based
in EAP-FRM
Transport Protocol
(e.g. AAA protocol)
EAP-Request /FRM()
MN
(EAP Peer)
Authenticator
MIH PoS
(EAP Auth.)
Backend Auth Server
(e.g. ER/AAA)
Request* ()
Response* ()
EAP- Success ()
.
.
.
EAP-Response /FRM()

## Slide 9: Proactive Operation
21-04-00xx-00-0021
Current EAP lower-layers supporting EAP pre-authentication can directly be used in this case.
EAP transport based
in EAP-FRM
Transport Protocol
(e.g. AAA protocol)
EAP-Request /FRM()
MN
(EAP Peer)
Candidate Authenticator (MIH PoS)
(EAP Auth.)
ER/AAA server
Trigger [e.g EAPOL-Start]*
Request* ()
Response* ()
EAP- Success ()
.
.
.
EAP-Response /FRM()
Serving Authenticator
*Optional

## Slide 10: Use Case 1: EAP-FRM with ERP
21-04-00xx-00-0021
ERP payload is transported in EAP-FRM (e.g. sequence number, authentication tag, etc...).
EAP-Request / FRM(IRS)
EAP- Response/ FRM (IR)
EAP-Request / FRM (FR)
AAA-Req (IR)
AAA-Resp(FR, rMSK)
EAP- Response / FRM ()
EAP- Success ()
MN
(EAP Peer)
Candidate Authenticator (MIH PoS)
(EAP Auth.)
ER/AAA Server
Serving Authenticator

## Slide 11: Use Case 2: EAP-FRM with 3PFH
21-04-00xx-00-0021
EAP-FRM can transport a 3-party protocol such as 3PFH.
Serving Authenticator
EAP-Request /FRM()
EAP-Response/ FRM(3PFH1)
MN
(EAP Peer)
EAP-Request / FRM (3PFH4)
AAA-req (3PFH2)
AAA-resp(3PFH3)
AAA Server
EAP-Response / FRM()
EAP-Success ()
Candidate Authenticator (MIH PoS)
(EAP Auth.)

## Slide 12: Implementation
21-04-00xx-00-0021
EAP-FRM method implementation can call a transport protocol API to contact an AAA server (or similar such as ERS server)
EAP layer
EAP peer layer
EAP Peer (MN)
EAP-FRM method layer
MSK
EAP lower- layer
EAP layer
EAP Authenticator (MIH PoS)
AAA/IP
AAA/IP
AAA Server
EAP-FRM method layer
MSK
EAP lower-layer
EAP auth. layer
MSK

## Slide 13: EAP-FRM packet
21-04-00xx-00-0021
Options Field (1 byte)
  P flag (1 bit): Proactive mode
    Useful when EAP lower-layer does not support indication of proactive mode of operation (e.g. IKEv2)
FRP Type (1 byte): Type of the transported fast re-authentication protocol (e.g. Kerberos, 3PFH, ERP*, etc...)
Payload: List of TLVs (e.g. TLV FRP, TLV server, TLV identity)
*Only payload
Payload (optional) [TLVs]
Code
Identifier
Length
0
8
16
31
Type=EAP-FRM
Options
FRP-Type
P

## Slide 14: Possible AAA extensions
21-04-00xx-00-0021
Grouped
AVP
AVP Code: Grouped AVP
Flags
Length
0
8
16
31
AVP Code: Fast Re-authentication Protocol
Flags
Length
AVP Data: Protocol Identifier (3PFH, KDE, Kerberos,...)‏
AVP Code: Fast Re-authentication Payload
Flags
Length
AVP Data: Protocol Payload
Code
Identifier
Lenght
0
8
16
31
Type=FRP
Length
Payload . . .
Authenticator
Radius
Header
Attributes
(TLV)‏
Diameter Grouped AVP (FRP)
  to transport the Fast Re-authentication payload between the authenticator and the AAA server.
Diameter Application (TBD)
  Define a new application
  Use an existing one.
RADIUS Attribute
  May be included in request and response.

## Slide 15: Security Remarks
EAP-FRM itself does not introduce any new vulnerability to EAP.
EAP-FRM can carry different fast re-authentication protocols (e.g. 3PFH).
The security of the overall EAP-FRM process strongly depends on the inherent security of the fast re-authentication protocol in use.
Thus, it is highly recommendable to design/use a fast re-authentication protocol with suitable security properties.

## Slide 16: Prototype
21-04-00xx-00-0021
wpa_supplicant: (EAP-FRM method peer implementation)
hostpad: EAP-FRM method auth./server implementation
freeradius: Auth./Authz module to process the FRP attribute and the fast re-authentication protocol.
AAA
AR
pAP
nAP
Free Radius
hostapd (EAP auth./server)
wpa_supplicant (EAP peer)

## Slide 17: Discussion
The proposal tries to cover pro-active EAP re-authentication without modifying any existing EAP standard or wireless technology vs. pro-active EAP re-authentication based on ERP
The general architecture may be useful for Work Item #2 Access Authentication “Use Case 1: Access Control is applied” (Use case 1.1). Opinions?
Design a new and specific fast re-authentication protocol for EAP-FRM in the context of 802.21a or to use existing ones?
21-04-00xx-00-0021

## Slide 18: Summary
Proactive EAP re-authentication based on ERP implies severe modifications to existing EAP standards and EAP lower-layers.
We propose a fast re-authentication architecture based on a new EAP method named EAP-FRM.
EAP-FRM works in standalone authenticators but can contact a backend authentication server (e.g. AAA server).
The architecture allows Proactive EAP re-authentication based on EAP-FRM.
EAP-FRM shows that it is possible to provide flexible fast re-authentication and Proactive EAP Re-authentication without modifying standards.
A small testbed has been deployed to show the benefits of our solution.
Future direction: study indirect proactive EAP re-authentication based on EAP-FRM; analyze context binding; provide additional details.
21-04-00xx-00-0021