## Slide 1
03-05-0xxx-00-0sec
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
Title: PLA-MIH: A Secure IEEE802.21 Signaling Scheme
Date Submitted: May 3, 2009
Authors or Source(s):
Sumanta Saha (HUT), Dmitrij Lagutin (HIIT)‏
Abstract: This presentation proposes a novel solution to secure MIH signaling and protect from various threats by using a trust-enabled network layer protocol named PLA.
<number>

## Slide 2
03-05-0xxx-00-0sec
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SAdards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/guide.html>
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as stated in Section 6 of the IEEE-SA Standards Board bylaws <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/faq.pdf>
<number>

## Slide 3
IEEE 802.21a Work Item 2
As published in the call for proposals there are two work items for the MIH security work group. This document proposes a solution for work item 2:
  Work Item #2: Mechanisms to provide data integrity, replay protection, confidentiality and data origin authentication to IEEE 802.21 MIH protocol exchanges and enable authorization for MIH services
The proposal uses a novel network layer protocol named Packet Level Authentication (PLA) [1], developed at TKK and HIIT, Finland, to secure the communication between the entities of MIH [3].
The primary advantage of the proposal lies in its simplicity and extensibility. As the security mechanisms are directly embedded into the network layer, no added AAA related roundtrip time is required. Moreover, it is possible to extend the use of the protocol to the traffic payload to further secure the traffic.
Analysis of the security solution has been done according to the threat list published in 21-07-0122-02-0000 and 21-08-0107-01-0sec-threat-modeling-and-analysis-for-mih-protocol-security.
03-05-0xxx-00-0sec
<number>

## Slide 4
Packet Level Authentication (PLA)‏
PLA aims to improve security on the network layer by providing availability and accountability
PLA is based on per packet public key signature techniques, these are feasible on the Internet scale due to new efficient cryptographic algorithms and advances in semiconductor technology
Good analogy to PLA is a paper currency: anyone can independently verify the authenticity of the bill without contacting the bank that has issued the bill
  Similarly, any node in the network can independently verify authenticity of the PLA protected packet without a trust relationship with the sender or other nodes that have handled the packet
03-05-0xxx-00-0sec
<number>

## Slide 5
PLA header
PLA adds an own header using the standard IP extension mechanisms, the PLA header contains:
  Certificate from a trusted third party (TTP) showing that the user is valid and trusted entity
    For efficiency reasons, PLA uses identity based implicitly certified keys, therefore the sender's public key is calculated from the TTP certificate information
  Timestamp and sequence number to detect delayed and duplicated packets
  Signature over the packet with a sender's private key
PLA header contains all necessary information to detect modified, duplicated and delayed packets. Therefore any node in the network can detect and drop such packets before they reach the destination
03-05-0xxx-00-0sec
<number>

## Slide 6: PLA header
<number>

## Slide 7
PLA cryptographic solutions
PLA uses elliptic curve cryptography due to its compact key and signature sizes
  A 163-bit ECC key has the same strength as a 1024-bit RSA key
  Overall, the PLA header takes only 1000 bits of space
Scalability for high-speed network can be accomplished using a dedicated hardware to accelerate cryptographic operations. Simulations has shown the performance of almost a million verifications per second with an 90nm ASIC [2]
  In this proposal, we are using PLA only for signaling, therefore it is not necessary to use a dedicated hardware for cryptographic operations
03-05-0xxx-00-0sec
<number>

## Slide 8
PLA-MIH introduction
We propose using PLA to secure MIH signaling [3]
The proposed system introduces certificate authorities (CAs) which are similar to PLA's trusted third parties
  Different CA certificate rights are used to distinguish between Mobile Node (MN) and Point of Attachment (PoA)
Main advantage of the proposed system: any node that receives the PLA protected MIH signaling packet can immediately determine:
  Whether the packet is authentic (not modified, delayed or duplicated)‏
  Whether the packet is sent by an MN or PoA
  Which operator (CA) has authorized the sender
  Such an approach reduces the latency during the authentication phase
03-05-0xxx-00-0sec
<number>

## Slide 9
Trust relationships
We assume following trust relationships in the system:
  Operator's certificate authority (CA) certify its users and PoAs
  Operators form trust relationships between each other using CAs
03-05-0xxx-00-0sec
<number>

## Slide 10
Bootstrapping
How the user will get an initial certificate from a CA?
For flexibility, two kinds of certificates are used
  The user will receive a long-term certificate from the operator during, e.g., creation of the contract. Such a certificate will be valid for months or years
  Long-term certificate will be used to retrieve a short-term certificate to be used for MIH authentication. Such a short-term certificate will be valid for hours or days
If the short-term certificate is expired or lost, it can be retrieved in an automated way with a long-term certificates
  Expiration of long-term certificate is unlikely, in that case user would need to contact the operator manually to retrieve a new certificate
03-05-0xxx-00-0sec
<number>

## Slide 11: PLA-MIH Signaling
At this stage we assume that all the PoAs and the MNs have valid certificates issued by the CA of the operator. The signaling of MIH over PLA can be divided primarily into two scenarios
  Handover between PoAs administered by a single operator
  Handover between PoAs administered by multiple operators
In both cases, PLA is used as a network layer protocol to protect the signaling between IS, ES and CS in MIH architecture
This proposal assumes that only the traffic over layer 3 and above is protected. However, similar idea can be extended to the MAC layer to protect even the broadcast messages for service and link discovery.
<number>

## Slide 12: Example MIH signaling with single operator
While transferring from one service to another provided by the same operator, the scenario is simple due to the fact that all the PoAs and MNs have certificates issued by the same CA.
Upon receiving signed packets with attached certificates, the receiver verifies the authenticity of the packet and the sender. If the receiver believes the sender, it processes the data; otherwise the packet is discarded.
An MN cannot fake as a PoA as the certificates have a “rights” field which indicates what rights the certificate owner has.
<number>

## Slide 13
Example MIH signaling with single operator
03-05-0xxx-00-0sec
<number>

## Slide 14: Example MIH signaling across multiple operators
Handover between services offered by different operators is slightly more complex because there must be trust relationship among the operators and the MN should know whether or not to trust the certificate presented to it by the new PoA.
The authors propose a simple solution to the problem. While performing the signaling with the old-PoA the MN can communicate the identity of the new-PoA and then the old-PoA sends the credentials of the operator of the new-PoA to the MN. Later, with this credential, the MN can verify the issuer of the certificate presented by the new-PoA.
On the other hand, there are two possibilities to verify the certificate from the MN by the new-PoA. It can either validate the issuer from its own cache, or it can optionally contact its own CA to validate the issuer of the certificate from the MN.
After the validation check, the operation goes on normally. There can be further optimization in signaling if the MN is provided a new certificate by the new-PoA. In that case, thereafter the MN is considered as a local MN to the new operator and a simple handover signaling can be followed for further handovers.
<number>

## Slide 15
Example MIH signaling across multiple operators
03-05-0xxx-00-0sec
<number>

## Slide 16
PLA-MIH: Security Analysis
Threats to MN
  Identity Spoofing: Identity of an infrastructure node is spoofed
    Solution: PLA header and certificate information proves the identity of the sender
  Tampering of information
    Solution: The integrity of the message is protected by the signature in the packet
  Information disclosure: MN can get access to unauthorized information
    Solution: PLA header has the “rights” field which instantly shows what right the sender have; whether it is an MN or a PoA.
Threats to IS
  DoS attack by flooding: Flooding with numerous requests
    Solution: It is not instantly possible to thwart botnet-type DoS attack. However, upon detection of malicious behavior the IS can report the certificate identity to the CA and thus revoke it.
  Other attack solutions are same as MN
03-05-0xxx-00-0sec
<number>

## Slide 17
PLA-MIH: Security Analysis (Contd.)‏
Threats to ES/CS
  Tracking information disclosure: Profiling user movement and tracking events
    Solution: To prevent tracking confidentiality is required. However, PLA does not provide confidentiality as such. It is possible to establish a shared secret in the first packet exchanges and then use that for encrypting further traffic.
  Threats to MN and IS are also application to ES/CS and can be alleviated in the above stated way
03-05-0xxx-00-0sec
<number>

## Slide 18
Evaluation
Compared to contemporary security solutions, PLA-MIH has the following advantages:
  Trust built in directly to the network layer protocol, thus avoiding building security system over already built architecture
  Easily extendable and flexible security system
  Use of asymmetric cryptography ensures high-level of security
  No need to contact CA or AAA server most of the time, reducing network round trip delay
  Possibility of implementing similar paradigm in link layer advertisement and thus allowing MNs to determine malicious nodes even before attaching to them
  Proved availability of small-scale hardware which accelerates the operator manifold.
03-05-0xxx-00-0sec
<number>

## Slide 19
References
D. Lagutin. Redesigning Internet - The Packet Level Authentication architecture. Licentiate`s thesis, Helsinki University of Technology, Faculty of Information and Natural Sciences, Department of Information and Computer Science, June 2008. Available at: http://www.tcs.hut.fi/Software/PLA/new/doc/Lagutin-Redesigning%20Internet-The%20Packet%20Level%20Authentication%20architecture.pdf
J. Forsten, K. Järvinen and J. Skyttä. Packet Level Authentication - Hardware Subtask Final Report. Available at: http://www.tcs.hut.fi/Software/PLA/new/doc/PLA_HW_final_report.pdf
IEEE standards committee, “Part 21: Media Independent Handover Services,” IEEE 802.21 (IEEE Std), Jan. 2009.
03-05-0xxx-00-0sec
<number>