## Slide 1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: 21-09-0066-00-0Sec
Title: Proactive Authentication and MIH Security
Date Submitted: May 03, 2009
Authors or Source(s):
Subir Das, Ashutosh Dutta, Yuu-Heng(Alice) Cheng (Telcordia Technologies)
ToshiKazu Kodama (Toshiba)
Abstract:
This document proposes proactive authentication techniques and MIH protocol level security mechanisms with reference to the call proposal 21-09-0044-00-0Sec-802-21a-call-for-proposals.ppt.

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/guide.html>
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as stated in Section 6 of the IEEE-SA Standards Board bylaws <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/faq.pdf>
<number>
21-09-0066-00-0sec

## Slide 3: Proposal Characterization List
21-09-0066-00-0sec
<number>
Work Item # | Supported Functionality | Note
1 | Proactive Re-Authentication | Yes
1 | EAP Pre-authentication | Yes
1 | Key Hierarchy and Derivation 1 | No*
1 | Higher-Layer Transport for MN-CA, MN-SA and SA-CA signaling | Yes
1 | Link-Layer Transport for MN-SA signaling | Yes
1 | Authenticator Discovery Mechanism | No*
1 | Context Binding Mechanism | Yes
2 | Access Authentication | Yes
2 | MIH-Specific Authentication | Yes
2 | Key Hierarchy and Derivation 2 | Partial
2 | MIH-Specific Protection | Yes
2 | Protection by MIH Transport Protocol | No
2 | Visited Domain Access | No*
Note*: Does not mention explicitly but the proposed approach may be applicable

## Slide 4: Proactive Authentication Proposal

## Slide 5: Proactive Authentication Approaches
EAP Pre-Authentication
  Direct Pre-Authentication
  Indirect Pre-Authentication
EAP Re-Authentication(ERP)*
  Direct Re-Authentication
  Indirect Re-Authentication
* Re-authentication is performed before handover
<number>
21-09-0066-00-0sec

## Slide 6: Direct Proactive Authentication
Serving PoA
M
I
H
MN
RP1
MIH PoS
(SA)
MIH PoS
(CA)
RP5
Candidate PoA
Home AAA
Server
MN-CA Signaling
(via serving network)
EAP over AAA
RP2
SA Serving Authenticator
CA  Candidate Authenticator
<number>
21-09-0066-00-0sec

## Slide 7: Indirect Proactive Authentication
Serving PoA
M
I
H
MN
RP1
RP2
MIH PoS
(SA)
MIH PoS
(CA)
RP5
Candidate PoA
Home AAA
Server
MN-SA Signaling
EAP over AAA
SA-CA Signaling
SA Serving Authenticator
CA  Candidate Authenticator
<number>
21-09-0066-00-0sec

## Slide 8: Requirements and Terminologies used for the Proposal
As Described in Sections 2.3.2.3 and 2.3.3.4 of technical requirements (21-08-0012-02-0sec-mih-security-technical-report)
Terminologies
  EAP: Extensible Authentication Protocol
  ERP : EAP Re-Authentication Protocol
  SA : Serving Authenticator
  CA : Candidate Authenticator
<number>
21-09-0066-00-0sec
Notes: <number>

## Slide 9: EAP Transport
EAP needs to be carried over the serving access network to the candidate authenticator
EAP over higher layer
  MIH Protocol
EAP over lower layer
  Media specific transport (e.g., Ethernet)
Note: A combination of lower and higher layers transport may be required depending upon architecture
<number>
21-09-0066-00-0sec
Notes: <number>

## Slide 10: Definitions
Media Independent Authenticator (MI-Auth)
  Media Independent authenticator is an entity that facilitates proactive authentication of other entities attached to the other end of a link
Proactive Authentication
  An authentication process that is performed between MI-Auth and other entities before handover to another access network,
  Two cases:
    Proactive Authentication using EAP (a.k.a., EAP Pre-Authentication)
    Proactive Authentication using ERP (a.k.a., EAP Re-Authentication)
Authentication Process
  The cryptographic operations and supporting data frames that perform the authentication
<number>
21-09-0066-00-0sec
Notes: <number>

## Slide 11: Architecture- Example A
Media Specific Authenticator(MSA)
POA1
Media Independent Authenticator(MIA)
MIHF
POA2
Media Specific Authenticator(MSA)
POA1
POA2
Media Independent
Access Functions
(MIH POS+)
Media Specific
Access Functions
MN
MN
Serving Access
Network
Candidate Access
Network
RP1
Remote
Interface definition
out of scope
RP1
<number>
21-09-0066-00-0sec
Notes: <number>

## Slide 12: Architecture- Example B
Media Specific Authenticator(MSA)
POA1
Media Independent Authenticator (MIA)
MIHF
POA2
Media Specific Authenticator(MSA)
POA1
POA2
Media Independent
Access Functions
(MIH POS+)
Media Specific
Access Functions
MN
MN
Media Independent Authenticator (MIA)
MIHF
Serving Access
Network
Candidate Access
Network
RP5
RP1
RP2
RP1
RP2
<number>
21-09-0066-00-0sec
Notes: <number>

## Slide 13: EAP over MIH Protocol
Assumptions
  Authenticator is a MIH PoS (e.g., example architectures A and B)
  MIHF-ID of MN is used as the media-independent identity of the MN
  MIHF-ID of authenticator is used as the media-independent identity of the authenticator
  Authenticator holds MSK (Master Session Key) or rMSK (Re-authentication MSK) generated by EAP
  MSK or rMSK is used for deriving media-independent pair-wise master key (MI-PMK)
  When MN hands over to the target MSA and it has an media-specific PMK (MS-PMK) derived from an MI-PMK for the target MSA, it runs media-specific secure association using the MS-PMK.
<number>
21-09-0066-00-0sec

## Slide 14: Features
Support for both direct and indirect proactive authentication
Support for both network-initiated and mobile-initiated proactive authentication
<number>
21-09-0066-00-0sec

## Slide 15: Network-initiated Direct Proactive Authentication (EAP)
MIH Pro-auth request (Result, EAP, Lifetime, IC)
These two entities are same for architecture A
Peer (MN)
MIA Candidate
Authenticator
:
MIA Serving
Authenticator
MIH Pro-auth request (EAP)
MIH Pro-auth response (EAP)
MIH Pro-auth response (IC)
MIH Pro-auth Request (MN-MIHF-ID)
MIH Pro-auth Response
<number>
21-09-0066-00-0sec

## Slide 16: Network-initiated Direct Proactive Authentication (ERP)
These two entities are same for architecture A
Peer (MN)
Candidate MIA
Serving MIA
MIH Pro-auth indication
MIH Pro-auth Request (ERP)
MIH Pro-auth Response (Result, ERP)
MIH Pro-auth Request (MN-MIHF-ID)
MIH Pro-auth Response
<number>
21-09-0066-00-0sec

## Slide 17: Mobile-initiated Direct Proactive Authentication (EAP)
Peer (MN)
Candidate MIA
The same procedure as network-initiated Direct Proactive Authentication (EAP)
Serving MIA
MIH Pro-auth Request
(MN-MIHF-ID)
MIH Pro-auth Request
(CA-MIHF-ID)
These two entities are same for architecture A
MIH Pro-auth Response
MIH Pro-auth Response
<number>
21-09-0066-00-0sec

## Slide 18: Mobile-initiated Direct Proactive Authentication (ERP)
Peer (MN)
Candidate MIA
Serving MIA
These two entities are same for architecture A
MIH Pro-auth Request (ERP)
MIH Pro-auth Response (Result, ERP)
<number>
21-09-0066-00-0sec

## Slide 19: Network-initiated Indirect Proactive Authentication (EAP)
Peer (MN)
Candidate MIA
:
Serving MIA
MIH Pro-auth response
(CA-MIHF-ID, EAP)
MIH Pro-auth request
(Result, EAP, Lifetime, IC)
MIH Pro-auth response (IC)
MIH Pro-auth response (IC)
MIH Pro-auth request
(Result, EAP, Lifetime, IC)
MIH Pro-auth response
(MN-MIHF-ID, EAP)
MIH Pro-auth request
(CA-MIHF-ID, EAP)
MIH Pro-auth request
(MN-MIHF-ID, EAP)
These two entities are same for architecture A
<number>
21-09-0066-00-0sec

## Slide 20: Network-initiated Indirect Proactive Authentication (ERP)
Peer (MN)
Candidate MIA
Serving MIA
MIH Pro-auth Request
(CA-MIHF-ID, ERP)
MIH Pro-auth Finish
(Result, ERP)
MIH Pro-auth request
(Result, ERP)
MIH Pro-auth Initiate
(MN-MIHF-ID, ERP)
MIH Pro-auth Request
(MN-MIHF-ID)
These two entities are same for architecture A
MIH Pro-auth Request
(CA-MIHF-ID)
MIH Pro-auth Response
MIH Pro-auth Response
<number>
21-09-0066-00-0sec

## Slide 21: Mobile-initiated Indirect Proactive Authentication (EAP)
Peer (MN)
Candidate MIA
Serving MIA
MIH Pro-auth Request
(CA-MIHF-ID)
MIH Pro-auth Request
(MN-MIHF-ID)
The same procedure as network-initiated Indirect Proactive Authentication
Procedure (EAP)
The same procedure as Network-initiated Indirect Proactive Authentication
Procedure (EAP)
These two entities are same for architecture A
MIH Pro-auth Response
MIH Pro-auth Response
<number>
21-09-0066-00-0sec

## Slide 22: Mobile-initiated Indirect Proactive Authentication (ERP)
Peer (MN)
Candidate MIA
Serving MIA
MIH Pro-auth Request
(CA-MIHF-ID, ERP )
MIH Pro-auth Request
(MN-MIHF-ID, ERP)
These two entities are same for architecture A
MIH Pro-auth Response
(CA-MIHF-ID, ERP )
MIH Pro-auth Response
(MN-MIHF-ID, ERP)
<number>
21-09-0066-00-0sec

## Slide 23: Attachment to Target MSA (EAP/ERP)*
Peer (MN)
Target MIA
Secure Association
Target MSA
Media Specific Key distribution
(MS-PMK) (Push or Pull)
* After handover
Serving MSA
MIH_Registration
Serving MIA
<number>
21-09-0066-00-0sec

## Slide 24: Direct Proactive Authentication Termination (EAP/ERP)
Peer (MN)
Candidate/Target
/Serving MIA
MIH Pro-auth Termination request (IC)*
MIH Pro-auth Termination response (IC)*
Peer (MN)
Candidate/Target
/Serving MIA
MIH Pro-auth Termination request (IC)*
MIH Pro-auth Termination response (IC)*
Network-initiated
Mobile-initiated
* It may be possible to extend MIH De-register message to achieve this
<number>
21-09-0066-00-0sec

## Slide 25: Indirect Proactive Authentication Termination (EAP/ERP)
Peer (MN)
Candidate MIA
Serving MIA
MIH Pro-auth Termination request
(IC)
MIH Pro-auth Termination request
(IC)
MIH Pro-auth Termination response
(IC)
MIH Pro-auth Termination response
(IC)
Peer (MN)
Candidate
MIA
Serving
MIA
MIH Pro-auth Termination request
(IC)
MIH Pro-auth Termination request
(IC)
MIH Pro-auth Termination response
(IC)
MIH Pro-auth Termination response
(IC)
Network-initiated
Mobile-initiated
<number>
21-09-0066-00-0sec

## Slide 26: Proposed MIH Primitives
Proactive Authentication Event
  MIH_Pro_authentication_result_Indication (local and remote)*
  Link_Pro-authentication_key_install_indication (local only)*
Proactive Authentication Command
  MIH_Pro-authentication_start_Request
  MIH_Pro-authentication_start Indication
  MIH_Pro-authentication_start_Response
  MIH_Pro-authentication_start_Confirm
  MIH_Pro-authentication_Termination_Request**
  MIH_Pro-authentication_Termination_Indication**
* Need to define a new event type in MIH/Link_Event_Subscribe
**It may be possible to extend MIH_De-register to achieve this
<number>
21-09-0066-00-0sec

## Slide 27: Proposed MIH Primitives (contd..)
Proactive Key Distribution Command (local)
  MIH_Pro-authentication_key_install_Request
  MIH_Pro-authentication_key_install_Confirm
  Link_Pro-authentication_key_install_Request
  Link_Pro-authentication_key_install_Confirm
<number>
21-09-0066-00-0sec

## Slide 28: Event Primitive
MIH_Pro-authentication_result_Indication
  Parameters
    Source Identifier: MIHF-ID of MN or CA or SA
    MN-MIHF-ID: MIHF-ID of MN
    CA-MIHF-ID: MIHF-ID of CA
    Status {Success, Failure}
<number>
21-09-0066-00-0sec

## Slide 29: Event Primitive
Link_Pro-authentication_key_install_indication
  Parameters
    Link layer identifier of MN or MSA
<number>
21-09-0066-00-0sec

## Slide 30: Command Primitive
MIH_Pro-authentication_start_{Request, Indication}
  Parameters
    Source Identifier: MIHF-ID of MN or SA*
    Destination Identifier: MIHF-ID of CA or SA*
    MN-MIHF-ID: MIHF-ID of MN
    CA-MIHF-ID: MIHF-ID of CA
* Source ID is for Indication and Destination ID is for request
<number>
21-09-0066-00-0sec

## Slide 31: Command Primitive (Contd..)
MIH_Pro-authentication_start_{Response, Confirm}
  Parameters
    Source Identifier: MIHF-ID of CA or SA*
    Destination Identifier: MIHF-ID of MN or SA*
    MN-MIHF-ID: MIHF-ID of MN
    CA-MIHF-ID: MIHF-ID of CA
    Status
* Source ID is for Confirm and Destination ID is for response
<number>
21-09-0066-00-0sec

## Slide 32: Command Primitive (contd..)
MIH_Pro-authentication_Termination_{Request,Indication}
  Parameters
    Source Identifier: MIHF-ID of MN, CA or SA*
    Destination Identifier: MIHF-ID of MN, CA or SA*
    MN-MIHF-ID: MIHF-ID of MN
    CA-MIHF-ID: MIHF-ID of CA
* Source ID is for Indication and Destination ID is for request
<number>
21-09-0066-00-0sec

## Slide 33: MIH Protocol Security Proposal

## Slide 34: Definition
MIH Security Association (SA)
  An MIH SA is the security association between the peer MIH entities
    Established to protect MIH messages
  The MIH SA is bound to the authenticated identities of the peer MIH entities
<number>
21-09-0066-00-0sec
Notes: <number>

## Slide 35: Proposal
MIH SA within MIH protocol
  Use TLS for the authentication and key establishment protocol
    TLS handshake can be carried out over MIH protocol
    TLS provides cipher suites negotiation which provides crypto agility
    Use of existing authentication and key management protocol will greatly reduce the risk of introducing security flaws
Pros: Once MIH SA is defined within MIH protocol, there is no need to have MIH transport level security
<number>
21-09-0066-00-0sec
Notes: <number>

## Slide 36: Use Case 1: Access Control
Assumptions
  Access control is applied through the access controller
  The access control is applied through an access authentication with the MIH service provider through an Authentication Server (AS), e.g., an EAP Server or an AAA server
  Upon a successful authentication, the MN is authorized to access the MIH services through PoS’es
    The access authentication includes a key establishment procedure so that keys are established between the MN and the Authentication Server.
<number>
21-09-0066-00-0sec
Notes: <number>

## Slide 37: Two Scenarios for Use Case 1
Integrated scenario: MIH Services and Network Access Service use the same AS
  MIH keying material is bootstrapped from EAP keying material that is established during initial or proactive authentication for network access service
Split scenario: MIH Services and Network Access Service use different ASes
  MIH keying material is bootstrapped from EAP keying material that is established during initial authentication for MIH Services
<number>
21-09-0066-00-0sec
Notes: <number>

## Slide 38: Use Case 2: No Access Control
Assumptions
  Access control is not applied through any access controller
  The mutual authentication may be based on a pre-shared key or a trusted third party like certificate authority
  The authentication is MIH specific. That is, the mutual authentication will assure the MIHF identity of one party to another
    The MN and the PoS will conduct a mutual authentication and key establishment of MIH specific keys
<number>
21-09-0066-00-0sec
Notes: <number>

## Slide 39: Use Case 1:Integrated Scenario (1a)
Peer (MN)
AS
MSA(PoA)
Initial Authentication/
Secure Association
AAA messages
TLS Handshake
Protected MIH Messages w/ access control
PoS
AAA message
MIH message for key request
MIH SA established
AS: Authentication server for both network access and MIH Services
<number>
21-09-0066-00-0sec

## Slide 40: Use Case 1:Integrated Scenario (1b)
Peer (MN)
AS
MIA(PoS))
Proactive Authentication
AAA messages
TLS Handshake
Protected MIH Messages w access control
MIH SA established
AS: Authentication server for both network access and MIH Services
<number>
21-09-0066-00-0sec

## Slide 41: Use Case 1:Split Scenario
Peer (MN)
AS2
MSA(PoA)
Initial Authentication
AAA messages
TLS Handshake
Protected MIH Messages w access control
PoS
AAA message
EAP message
AS1
MIH SA established
AS1: Authentication server for both network access
AS2: Authentication server for MIH Services
<number>
21-09-0066-00-0sec

## Slide 42: Use Case 2: No Access Control
Peer (MN)
PoS
TLS Handshake
Protected MIH Messages w/o access control
MIH SA established
<number>
21-09-0066-00-0sec

## Slide 43: Key Hierarchy for MIH SA
TLS master secret
MIIK
MIEK
MSK or rMSK or EMSK
PSK (dynamic) as
TLS credentials
TLS master secret
MIIK
MIEK
PSK (static) or public key as
TLS credentials
Use Case 1
Use Case 2
PSK (static) or public key as
EAP credentials
<number>
21-09-0066-00-0sec
Notes: <number>

## Slide 44: What Needs to be Defined?
A mechanism to advertise the capability of MIH-level security
A mechanism to carry TLS message in the MIH protocol and binding TLS keying material to MIH contexts
Key derivation algorithms for MIH SA key hierarchy
  MIH message format for using negotiated ciphering mechanisms via TLS *
* Some IETF work may be needed
<number>
21-09-0066-00-0sec
Notes: <number>