## Slide 1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: 21-09-0066-01-0Sec
Title: Proactive Authentication and MIH Security
Date Submitted: July 05, 2009
Authors or Source(s):
Subir Das, Ashutosh Dutta, (Telcordia Technologies)
ToshiKazu Kodama (Toshiba)
Abstract:
This document proposes proactive authentication techniques and MIH protocol level security mechanisms with reference to the call proposal 21-09-0044-00-0Sec-802-21a-call-for-proposals.ppt.

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/guide.html>
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as stated in Section 6 of the IEEE-SA Standards Board bylaws <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/faq.pdf>
<number>
21-09-0066-01-0sec

## Slide 3: Proposal Characterization List
21-09-0066-01-0sec
<number>
Work Item # | Supported Functionality | Note
1 | Proactive Re-Authentication | Yes
1 | EAP Pre-authentication | Yes
1 | Key Hierarchy and Derivation 1 | Yes
1 | Higher-Layer Transport for MN-CA, MN-SA and SA-CA signaling | Yes
1 | Link-Layer Transport for MN-SA signaling | Yes
1 | Authenticator Discovery Mechanism | No*
1 | Context Binding Mechanism | Yes
2 | Access Authentication | Yes
2 | MIH-Specific Authentication | Yes
2 | Key Hierarchy and Derivation 2 | Yes
2 | MIH-Specific Protection | Yes
2 | Protection by MIH Transport Protocol | No
2 | Visited Domain Access | No*
Note*: Does not mention explicitly but the proposed approach may be applicable

## Slide 4: Proactive Authentication Proposal

## Slide 5: Proactive Authentication Approaches
EAP Pre-Authentication
  Direct Pre-Authentication
  Indirect Pre-Authentication
EAP Re-Authentication(ERP)*
  Direct Re-Authentication
  Indirect Re-Authentication
* Re-authentication is performed before handover
<number>
21-09-0066-01-0sec

## Slide 6: Direct Proactive Authentication
Serving PoA
M
I
H
MN
RP1
MIH PoS
(SA)
MIH PoS
(CA)
RP5
Candidate PoA
Home AAA
Server
MN-CA Signaling
(via serving network)
EAP over AAA
RP2
SA Serving Authenticator
CA  Candidate Authenticator
<number>
21-09-0066-01-0sec

## Slide 7: Indirect Proactive Authentication
Serving PoA
M
I
H
MN
RP1
RP2
MIH PoS
(SA)
MIH PoS
(CA)
RP5
Candidate PoA
Home AAA
Server
MN-SA Signaling
EAP over AAA
SA-CA Signaling
SA Serving Authenticator
CA  Candidate Authenticator
<number>
21-09-0066-01-0sec

## Slide 8: Requirements and Terminologies used for the Proposal
As Described in Sections 2.3.2.3 and 2.3.3.4 of technical requirements (21-08-0012-02-0sec-mih-security-technical-report)
Terminologies
  EAP: Extensible Authentication Protocol
  ERP : EAP Re-Authentication Protocol
  SA : Serving Authenticator
  CA : Candidate Authenticator
<number>
21-09-0066-01-0sec
Notes: <number>

## Slide 9: EAP Transport
EAP needs to be carried over the serving access network to the candidate authenticator
EAP over higher layer
  MIH Protocol
EAP over lower layer
  Media specific transport (e.g., Ethernet)
Note: A combination of lower and higher layers transport may be required depending upon architecture
<number>
21-09-0066-01-0sec
Notes: <number>

## Slide 10: Definitions
Authentication Process : The cryptographic operations and supporting data frames that perform the authentication
Media Specific Authenticator and Key Holder (MSA-KH): Media specific authenticator and key holder is an entity that facilitates authentication of other entities attached to the other end a link specific to a media
Media Independent Authenticator and Key Holder (MIA-KH): Media Independent authenticator and key holder is an entity that interacts with MSA-KH and facilitates proactive authentication of other entities attached to the other end of a link of a MSA-KH
<number>
21-09-0066-01-0sec
Notes: <number>

## Slide 11: Definitions contd..
Proactive Authentication : An authentication process that is performed between MIA-KH and other entities attached to the other end of a link of a MSA-KH. This process occurs when the other entities intend to perform a handover to another link
Serving MIA-KH : The MIA-KH that is currently serving to a mobile node which is attached to an access network
Candidate MIA-KH: The MIA-KH that is serving to an access network which is in the mobile node’s list of potential candidate access networks.
<number>
21-09-0066-01-0sec
Notes: <number>

## Slide 12: Architecture- Example A
<number>
21-09-0066-01-0sec
Media Specific Authenticator and Key Holder
(MSA-KH)
POA1
Media Independent Authenticator and Key Holder
(MIA-KH)
MIHF
POA2
Media Specific Authenticator and
Key Holder
(MSA-KH)
POA1
POA2
Media Independent
Access Functions
(MIH POS+)
Media Specific
Access Functions
MN
MN
Serving Access
Network
Candidate Access
Network
RP1
Interface _MIA-KH-MSA-KH
RP1
Interface _MIA-KH-MSA-KH
Media Specific
Access Functions
Notes: <number>

## Slide 13: Architecture- Example B
<number>
21-09-0066-01-0sec
Media Specific Authenticator and Key Holder
(MSA-KH)
POA1
Media Independent Authenticator and Key Holder
(MIA-KH)
MIHF
POA2
Media Specific Authenticator and Key Holder
(MSA-KH)
POA1
POA2
Media Independent
Access Functions
(MIH POS+)
Media Specific
Access Functions
MN
MN
Media Independent Authenticator and Key Holder
(MIA-KH)
MIHF
Serving Access
Network
Candidate Access
Network
RP5
RP1
RP2
RP1
RP2
Int_MIA-KH-MSA-KH
Int_MIA-KH-MSA-KH
Notes: <number>

## Slide 14: EAP over MIH Protocol
Assumptions
  Authenticator is a MIH PoS (e.g., example architectures A and B)
  MIHF-ID of MN is used as the media-independent identity of the MN
  MIHF-ID of authenticator is used as the media-independent identity of the authenticator
  Authenticator holds MSK (Master Session Key) or rMSK (Re-authentication MSK) generated by EAP
  MSK or rMSK is used for deriving media-independent pair-wise master key (MI-PMK)
  When MN hands over to the target MSA-KH and it has an media-specific PMK (MS-PMK) derived from an MI-PMK for the target MSA-KH, it runs media-specific secure association using the MS-PMK.
<number>
21-09-0066-01-0sec

## Slide 15: Features
Support for both direct and indirect proactive authentication
Support for both network-initiated and mobile-initiated proactive authentication
<number>
21-09-0066-01-0sec

## Slide 16: Network-initiated Direct Proactive Authentication (EAP)
MIH Pro-Auth Request (Result, EAP, Lifetime, IC, PoA-Link-Addr-List)
These two entities are same for architecture A
Peer (MN)
MIA-KH Candidate
Authenticator
:
MIA-KH Serving
Authenticator
MIH Pro-Auth Request (EAP)
MIH Pro-Auth Response (EAP)
MIH Pro-Auth Response (IC, MN-Link-Addr-List)
MIH Pro-Auth Request (MN-MIHF-ID)
MIH Pro-Auth Response
<number>
21-09-0066-01-0sec

## Slide 17: Network-initiated Direct Proactive Authentication (ERP)
These two entities are same for architecture A
Peer (MN)
Candidate MIA-KH
Serving MIA-KH
MIH Pro-Auth Indication (ERP)
MIH Pro-Auth Request (ERP, MN_Link_Addr_List)
MIH Pro-Auth Response (Result, ERP,PoA_Link_Addr_List)
MIH Pro-Auth Request (MN-MIHF-ID)
MIH Pro-Auth Response
<number>
21-09-0066-01-0sec

## Slide 18: Mobile-initiated Direct Proactive Authentication (EAP)
Peer (MN)
Candidate MIA-KH
The same procedure as network-initiated Direct Proactive Authentication (EAP)
Serving MIA-KH
MIH Pro-Auth Request
(CA-MIHF-ID)
These two entities are same for architecture A
MIH Pro-Auth Response
<number>
21-09-0066-01-0sec

## Slide 19: Mobile-initiated Direct Proactive Authentication (ERP)
Peer (MN)
Candidate MIA-KH
Serving MIA-KH
These two entities are same for architecture A
MIH Pro-Auth Request (ERP, MN_Link_Addr_List)
MIH Pro-Auth Response (Result, ERP, PoA_Link_Addr_list)
<number>
21-09-0066-01-0sec

## Slide 20: Network-initiated Indirect Proactive Authentication (EAP)
<number>
21-09-0066-01-0sec
Peer (MN)
Candidate MIA-KH
:
Serving MIA-KH
MIH Pro-Auth Request
(CA-MIHF-ID, Result, EAP, Lifetime,
IC, PoA_Link_Addr_List)
MIH Pro-Auth Response
(CA-MIHF-ID, IC,
MN_Link_Addr_List)
MIH Pro-Auth Response
(MN-MIHF-ID, IC,
MN_Link_Addr_List)
MIH Pro-Auth Request
(MN-MIHF-ID, Result, EAP, Lifetime,
IC, PoA_Link_Addr_List)
MIH Pro-Auth Response
MIH Pro-Auth Request
(CA-MIHF-ID, EAP)
MIH Pro-Auth Request
(MN-MIHF-ID)
These two entities are same for architecture A
MIH Pro-Auth Request
(MN-MIHF-ID, EAP)
MIH Pro-Auth Response
(MN_MIHF-ID, EAP)
MIH Pro-Auth Response
(CA-MIHF-ID, EAP)

## Slide 21: Network-initiated Indirect Proactive Authentication (ERP)
<number>
21-09-0066-01-0sec
Peer (MN)
Candidate MIA-KH
Serving MIA-KH
MIH Pro-Auth Request
(CA-MIHF-ID, ERP, MN_Link_Addr_List)
MIH Pro-Auth Response
(CA-MIHF-ID, Result, ERP,
PoA_Link_Addr_List)
MIH Pro-Auth Response
(MN-MIHF-ID, Result, ERP,
PoA_Link_Addr_List)
MIH Pro-Auth Request
(MN-MIHF-ID, ERP,
MN_Link_Addr_List)
These two entities are same for architecture A
MIH Pro-Auth Indication
(MN-MIHF-ID, ERP)
MIH Pro-Auth Request
(MN-MIHF-ID)
MIH Pro-Auth Response
MIH Pro-Auth Indication
(CA-MIHF-ID, ERP)

## Slide 22: Mobile-initiated Indirect Proactive Authentication (EAP)
Peer (MN)
Candidate MIA-KH
Serving MIA-KH
MIH Pro-Auth Request
(CA-MIHF-ID)
MIH Pro-Auth Request
(MN-MIHF-ID)
The same procedure as network-initiated Indirect Proactive Authentication
Procedure (EAP)
The same procedure as Network-initiated Indirect Proactive Authentication
Procedure (EAP)
These two entities are same for architecture A
MIH Pro-Auth Response
(MN-MIHF-ID)
MIH Pro-Auth Response
(CA-MIHF-ID)
<number>
21-09-0066-01-0sec

## Slide 23: Mobile-initiated Indirect Proactive Authentication (ERP)
Peer (MN)
Candidate MIA-KH
Serving MIA-KH
MIH Pro-Auth Request
(CA-MIHF-ID, ERP, MN_Link_Addr_List)
MIH Pro-Auth Request
(MN-MIHF-ID, ERP, MN_Link_Addr_List)
These two entities are same for architecture A
MIH Pro-Auth Response
(CA-MIHF-ID, ERP , PoA_Link_Addr_List)
MIH Pro-Auth Response
(MN-MIHF-ID, ERP, PoA_Link_Addr_List)
<number>
21-09-0066-01-0sec

## Slide 24: Attachment to Target MSA-KH (EAP/ERP)*
* After handover
Peer (MN)
Target MIA-KH
Secure Association
Target MSA-KH
Media Specific Key distribution
(MS-PMK) (Push or Pull)
Serving MSA
MIH_Registration
Serving MIA
<number>
21-09-0066-01-0sec

## Slide 25: Direct Proactive Authentication Termination (EAP/ERP)
Peer (MN)
Candidate/Target
/Serving MIA-KH
MIH Pro-Auth Termination request (IC)
MIH Pro-Auth Termination response (IC)
Peer (MN)
Candidate/Target
/Serving MIA-KH
MIH Pro-Auth Termination request (IC)
MIH Pro-Auth Termination response (IC)
Network-initiated
Mobile-initiated
* It may be possible to extend MIH De-register message to achieve this
<number>
21-09-0066-01-0sec

## Slide 26: Indirect Proactive Authentication Termination (EAP/ERP)
Peer (MN)
Candidate/TargetMIA-KH
Serving MIA-KH
MIH Pro-auth Termination request
(IC, CA-MIHF-ID)
MIH Pro-auth Termination request
(IC, MN-MIHF-ID)
MIH Pro-auth Termination response
(IC, CA-MIHF-ID)
MIH Pro-auth Termination response
(IC, MN-MIHF-ID)
Peer (MN)
Candidate/Target
MIA-KH
Serving
MIA-KH
MIH Pro-auth Termination request
(IC, CA-MIHF-ID)
MIH Pro-auth Termination request
(IC, MN-MIHF-ID)
MIH Pro-auth Termination response
(IC, CA-MIHF-ID)
MIH Pro-auth Termination response
(IC, MN-MIHF-ID)
Network-initiated
Mobile-initiated
<number>
21-09-0066-01-0sec

## Slide 27: Proposed MIH Primitives
Proactive Authentication Event
  MIH_Pro_authentication_result_Indication (local)
  Link_Pro-authentication_key_install_indication (local)
Proactive Authentication Command
  MIH_Pro-authentication_start_Request
  MIH_Pro-authentication_start Indication
  MIH_Pro-authentication_start_Response
  MIH_Pro-authentication_start_Confirm
  MIH_Pro-authentication_Termination_Request
  MIH_Pro-authentication_Termination_Indication
  MIH_Pro-authentication_Termination_Confirm
  MIH_Pro-authentication_Termination_Response
<number>
21-09-0066-01-0sec

## Slide 28: Proposed MIH Primitives (contd..)
Proactive Key Distribution Command (local)
  MIH_Pro-authentication_key_install_Request
  MIH_Pro-authentication_key_install_Confirm
  Link_Pro-authentication_key_install_Request
  Link_Pro-authentication_key_install_Confirm
<number>
21-09-0066-01-0sec

## Slide 29: Event Primitive
MIH_Pro-authentication_result_Indication
  Parameters
    Source Identifier: MIHF-ID of MN or CA or SA
    MN-MIHF-ID: MIHF-ID of MN
    CA-MIHF-ID: MIHF-ID of CA
    Link layer identifier of MN and MSA-KH
    Status {Success, Failure}
<number>
21-09-0066-00-0sec

## Slide 30: Event Primitive
Link_Pro-authentication_key_install_indication
  Parameters
    Link layer identifier of MN or MSA-KH
<number>
21-09-0066-00-0sec

## Slide 31: Command Primitive
MIH_Pro-authentication_start_{Request, Indication}
  Parameters
    Source Identifier: MIHF-ID of MN or SA*
    Destination Identifier: MIHF-ID of CA or SA*
    MN-MIHF-ID: MIHF-ID of MN
    CA-MIHF-ID: MIHF-ID of CA
* Source ID is for Indication and Destination ID is for Request
<number>
21-09-0066-00-0sec

## Slide 32: Command Primitive (Contd..)
MIH_Pro-authentication_start_{Response, Confirm}
  Parameters
    Source Identifier: MIHF-ID of CA or SA*
    Destination Identifier: MIHF-ID of MN or SA*
    MN-MIHF-ID: MIHF-ID of MN
    CA-MIHF-ID: MIHF-ID of CA
    Status
* Source ID is for Confirm and Destination ID is for Response
<number>
21-09-0066-00-0sec

## Slide 33: Command Primitive (contd..)
MIH_Pro-authentication_Termination_{Request,Indication}
  Parameters
    Source Identifier: MIHF-ID of MN, CA or SA*
    Destination Identifier: MIHF-ID of MN, CA or SA*
    MN-MIHF-ID: MIHF-ID of MN
    CA-MIHF-ID: MIHF-ID of CA
    Key Cache
* Source ID is for Indication and Destination ID is for Request
<number>
21-09-0066-00-0sec

## Slide 34: Command Primitive (contd..)
MIH_Pro-authentication_Termination_{Response,Confirm}
  Parameters
    Source Identifier: MIHF-ID of CA or SA*
    Destination Identifier: MIHF-ID of MN or SA*
    MN-MIHF-ID: MIHF-ID of MN
    CA-MIHF-ID: MIHF-ID of CA
    Status
* Source ID is for Confirm and Destination ID is for Response
<number>
21-09-0066-00-0sec

## Slide 35: MI-PMK and MS-PMK
KDF : Key derivation function specified in RFC 5246
  The default KDF (i.e., IKEv2 PRF+ with based on HMAC-SHA-256 ) is used unless explicitly negotiated between peer MIHFs
MI-PMK = KDF(MK, “MI-PMK” | RAND_P | RAND_A | length)
  Length of MI-PMK is 64 octets
  MK (Master Key): MSK or rMSK
  RAND_P: A random number generated by peer
  RAND_A: A random number generated by authenticator
MS-PMK =KDF(MI-PMK, “MS-PMK” | MN_LINK_ID | POA_LINK_ID | length)
  Length of MS_PMK depends on each media. In the case of 802.11, Length=32.
  MN_LINK_ID: Link identifier of MN, encoded as LINK_ID data type
  POA_LINK_ID: Link identifier of media-specific authenticator, encoded as LINK_ID data type
21-09-0066-01-0sec
<number>

## Slide 36: PRF+ (cf. RFC 4306)
PRF+ : PRF+ key expansion specified in IKEv2 [RFC4306]
PRF+ (K,S) = T1 | T2 | T3 | T4 | ...
Where:
‘|’ means concatenation
T1 = PRF (K, S | 0x01)
T2 = PRF (K, T1 | S | 0x02)
T3 = PRF (K, T2 | S | 0x03)
T4 = PRF (K, T3 | S | 0x04)
…
continuing as needed to compute the required length of key material. The default PRF is taken as HMAC-SHA-256 [SHA256]. Since PRF+ is only defined for 255 iterations it may produce up to 8160 octets of key material.
21-09-0066-01-0sec
<number>

## Slide 37: MIH Protocol Security Proposal

## Slide 38: Definition
MIH Security Association (SA)
  An MIH SA is the security association between the peer MIH entities
    Established to protect MIH messages
  The MIH SA is bound to the authenticated identities of the peer MIH entities
<number>
21-09-0066-01-0sec
Notes: <number>

## Slide 39: Proposal
MIH SA within MIH protocol
  Use (D)TLS for authentication, key establishment and ciphering
    (D)TLS handshake can be carried out over MIH protocol
    (D)TLS provides cipher suites negotiation which provides crypto agility
    Use of existing authentication and key management protocol will greatly reduce the risk of introducing security flaws
Pros: Once MIH SA is defined within MIH protocol, there is no need to have MIH transport level security
<number>
21-09-0066-01-0sec
Notes: <number>

## Slide 40: Use Case 1: Access Control
Assumptions
  Access control is applied through the access controller
  The access control is applied through an access authentication with the MIH service provider through an Authentication Server (AS), e.g., an EAP Server or an AAA server
  Upon a successful authentication, the MN is authorized to access the MIH services through PoS’es
    The access authentication includes a key establishment procedure so that keys are established between the MN and the Authentication Server.
  When proactive authentication is supported, proactive authentication and authentication for MIH services use the same AS
<number>
21-09-0066-01-0sec
Notes: <number>

## Slide 41: Use Case 2: No Access Control
Assumptions
  Access control is not applied through any access controller
  The mutual authentication may be based on a pre-shared key or a trusted third party like certificate authority
  The authentication is MIH specific. That is, the mutual authentication will assure the MIHF identity of one party to another
    The MN and the PoS will conduct a mutual authentication and key establishment of MIH specific keys
<number>
21-09-0066-01-0sec
Notes: <number>

## Slide 42: Use Case 1: Access Control
Peer (MN)
AS
MIA(PoS))
EAP/MIH messages
EAP/AAA messages
(D)TLS Handshake
Protected MIH Messages w access control
MIH SA established
Note: EAP may be performed in the context of proactive authentication as well
<number>
21-09-0066-01-0sec

## Slide 43: Use Case 2: No Access Control
Peer (MN)
PoS
(D)TLS Handshake
Protected MIH Messages w/o access control
MIH SA established
<number>
21-09-0066-01-0sec

## Slide 44: Key Hierarchy for MIH SA
MSK or rMSK
PSK (dynamic) as
(D)TLS credentials
PSK (static) or public key as
(D)TLS credentials
Use Case 1
Use Case 2
<number>
21-09-0066-01-0sec
(D)TLS handshake uses the (D)TLS credentials for authentication and establishment of (D)TLS key material for MIH SA
Notes: <number>

## Slide 45: Security Capabilities
New capabilities for MIH capability discovery
  MIH_SEC_CAP derived from BITMAP(16)
    Bit 0: Direct pre-authentication
    Bit 1: Indirect pre-authentication
    Bit 2: Direct re-authentication
    Bit 3: Indirect re-authentication
    Bit 4: MIH SA with access control
    Bit 5: MIH SA without access control
    Bit 6-15: Reserved
21-09-0066-01-0sec
<number>

## Slide 46: TLS Support
(D)TLS-PSK derivation in existence of access control for MIH services
  PSK = KDF(MK, “TLS-PSK” | RAND_P | RAND_A | length)
    MK (Master Key) : MSK or rMSK
New TLVs
  TLS (Transport Layer Security) TLV
    Data type: OCTET_STRING
    Content: a (D)TLS message
      Once MIH SA is established, the entire raw MIH PDU excluding Source and Destination MIHF Identifier TLVs must be carried in the payload of the TLS TLV
  Session ID TLV
    Data type: OCTET_STRING
    Content: a (D)TLS session identifier assigned via (D)TLS handshake
  Security Capability TLV
    Data type: MIH_SEC_CAP
    Content; See previous slide
    Carried in MIH_Capability_Discover messages
21-09-0066-01-0sec
<number>

## Slide 47: TLS Support (cont’d)
MIHS (MIH Security) PDU := MIHS header, followed by optional Source and Destination MIHF-ID TLVs, followed by an optional Session ID TLV, followed by (D)TLS TLV
  Source and Destination MIHF Identifier TLVs must be included in absence of MIH SA or when the sender’s transport address has been changed
    In the latter case, the mapping between the sender’s transport address and the MIHF identifier shall be updated, and MIH Registration message may be carried in the TLS TLV
  Session ID TLV must be included in existence of MIH SA
  The transport protocol entities to be associated with a TLS session are MIHF peers and identified by MIHF identifiers. Therefore, the transport address of an MIHF can change over the lifetime of a TLS session as long as the mapping between the transport address and MIHF identifier of an MIHF is maintained
MIHS Header
  SID=5 Security Service, AID=0
  ACK-Req=0, ACK-Rsp =0, UIR=0, M=0, FN=0
  Opcode=3 (Indication)
  Transaction ID= 0
21-09-0066-01-0sec
<number>

## Slide 48: MIHS PDU for Authentication and Key Establishment
21-09-0066-01-0sec
<number>
MIHS Protocol Header
Source MIHF
Identifier TLV
Destination MIHF
Identifier TLV
MIHS PDU
TLS TLV
(TLS record type = handshake or change cipher spec)

## Slide 49: MIHS PDU in existence of MIH SA
21-09-0066-01-0sec
<number>
MIHS Protocol Header
MIH Protocol Header
MIH Service Specific TLVs
MIH PDU
MIHS PDU
TLS TLV
(TLS record type = application data)
Carried as (D)TLS application data
Session ID TLV

## Slide 50: MIHS PDU upon Transport Address Change
21-09-0066-01-0sec
<number>
MIHS Protocol Header
MIH Protocol Header
MIH Service Specific TLVs
MIH PDU
MIHS PDU
TLS TLV
(TLS record type = application data)
Carried as (D)TLS application data
Session ID TLV
Source MIHF
Identifier TLV
Destination MIHF
Identifier TLV