IEEE P802.21 Media Independent Handover Services

Tentative Minutes of the IEEE P802.21a Security Task Group

Chair: Yoshihiro Ohba

Editor: Lily Chen

H Anthony Chan is taking the minutes

# Second Day PM2 Meeting: Kona 1; Tuesday, September 22, 2009

## Meeting called to order by Yoshihiro Ohba, Chair of IEEE 802.21a Security Task Group Chair at 4:00PM

## Meeting Agenda (21-09-0144-02-0sec)

The agenda is as follows:

For PM2 on Tuesday, September 22nd , 2009:

| Subject | Contributor | Time |
| --- | --- | --- |
| Security TG Meeting Called to Order | Yoshihiro Ohba | 04:00pm |
| Agenda for September 2009 Meeting | Yoshihiro Ohba | 04:02pm |
| Opening Note | Yoshihiro Ohba | 04:05pm |
| Approval of outstanding meeting minutes | Group | 04:15pm |
| 802.21a Proposal (0104-02) | Rafa Marin Lopez | 04:20pm |
| 802.21a Proposal (0066-02/ 0102-02 / 142-00) | Subir Das | 05:10pm |
| Recess |  | 06:00pm |

For AM1 and AM2 on Wednesday

| Subject | Contributor | Time |
| --- | --- | --- |
| Key Distribution Discussion (0126-02) | Rafa & Subir | 08:00am |
| A Study on IEEE 802.11r Approach (0148-01) | Lily Chen | 09:00am |
| Editor’s assessment on generating a 21a document | Lily Chen | 09:30am |
| Recess for Coffee Break |  | 10:00am |
| Proposals harmonization discussion | Proposers | 10:30am |
| Closing Note | Yoshihiro Ohba | 12:10pm |
| Adjourn |  | 12:30pm |

The agenda is approved by unanimous consent.

## Opening Notes (meeting notes 21-09-0153-00-0sec)

### Progress So Far

#### January 2009: The 1st 802.21a meeting

Initial CFP discussion

#### Between Jan and March: Two Teleconferences

#### March 2009: Issued CFP

7 proposals were submitted in response to CFP

#### May 2009: Proposal Presentation I

The 7 proposals were presented and discussed

#### Between May and July 2009: Three teleconferences

#### July 2009: Proposal Presentation II

#### Between July and Sept 2009: Two teleconferences

### Main Objective of This Meeting

#### The third (and last) Proposal Presentation to present and discuss 802.21a proposals

#### Reach consensus on key distribution approach

#### Achieve harmonization among proposals as much as possible before Down-selection in November meeting

### List of 802.21a Revised Proposals

#### Group 1: Work item #1 only

21-09-0060 (Security Related IEs)

21-09-0103 (Authenticator Discovery Mechanism)

21-09-0104 (EAP-FRM) to be presented in September meeting

#### Group 2: Work item #2 only

21-09-0059 (Protecting the IS e2e with hash tree)

21-09-0107 (Packet Level Authentication)

#### Group 3: Work items #1 and #2

21-09-0105 (Solution Proposal for 802.21a )

21-09-0066/ 0102  (Proactive Auth and MIH Security) to be presented in September meeting

## July plenary meeting minutes (21-09-0138-00), and July  Teleconference minutes (21-09-0147-00)

These outstanding minutes are unanimously approved.

## 802.11a proposal (21-09-104-02) is presented by Rafa Marin Lopez

### 21-09-0139-00 was also presented to explain received comments and the proposers’ response to the comments on the proposal.

### Discussion

Comment that the proposed EAP method (i.e., EAP-FRM) should be defined in IETF.

Comment that there is already an Internet-Draft for the proposed EAP method.

Presenter agreed to ask IETF to publish the Internet-Draft as an Informational or Experimental RFC.

## Answers to 802.11a proposal in (21-09-0142-00) is presented by Subir Das

### Updated proposal documents: (21-09-0066-02, 21-09-0102-02)

### Answers to comment on how are keys derived.

#### Section 3.4 describes the key generation algorithm whereby POA link address and MN link addresses are used

MS-PMK =KDF(MI-PMK, “MS-PMK” | MN_LINK_ID | POA_LINK_ID | length)]

#### Keys are generated after successful authentication

#### The POA-Link-Addr-List and MN-Link-Addr_List are represented as LIST(Link_ID) and the link end point in IEEE 802.21-2008 is L2 end point

#### MN can know the POA link layer address via IS

### Answers to comment on whether pro-auth request and response in Figure 5 are integrity protected.

#### Initial pro-auth request and response messages are not integrity protected

#### IC TLV description is missing. Added them in 21-09-0066-02-0sec and also IC TLV is defined (reference slide #36)

#### Candidate authenticator can initiate the pre-authentication.

### Answers to comment on how pull mechanism works in Figure 13.

#### The model of having MIA-KH as EAP server, MSA-KH as pass through authenticator, and MN as EAP peer, the pull mechanism would work

#### For push things seem to be complex since it needs media support

#### Further discussion:

The need of MIA-KH may be exemplified to enable MN to pro-authentication to a target network.

The logical function of MIA-KH may be located in ERP server.

## Recess at 6:20PM

# Third Day AM1 Meeting: Kona 1; Wednesday, September 23, 2009

## Meeting called to order by Yoshihiro Ohba, Chair of IEEE 802.21 Security Task Group Chair at 8:00AM

## Agenda change (to be updated to 21-09-0144-03-0sec):

Added slot for Shubhranshu

For AM1 and AM2 on Wednesday

| Subject | Contributor | Time |
| --- | --- | --- |
| Key Distribution Discussion (0126-02) | Rafa & Subir | 08:00am |
| A Study on IEEE 802.11r Approach (0148-01) | Lily Chen | 09:00am |
| Editor’s assessment on generating a 21a document | Lily Chen | 09:30am |
| Recess for Coffee Break |  | 10:00am |
| Proposals harmonization discussion | Proposers | 10:30am |
| PKMv2 discussion | Shubhranshu Singh | 11:00am |
| Closing Note | Yoshihiro Ohba | 12:10pm |
| Adjourn |  | 12:30pm |

Change is unanimously approved.

## Key Distribution Discussion (21-09-0126-02) is presented by Rafa Marin Lopez and Subir Das

### Background was in (21-09-0066-01)

Refer to Architecture example A in slide 12

#### Given the authentication keys, the issue is how to provide keys to MN:

MN is first turned on, perform authentication for network access with MSA-KH using media-specific authentication mechanism. MIA-KH is not involved in this media-specific authentication..

Then MN performs .MIH authentication with MIA-KH.

MN now moves to a target network.

The key in the target network is in general different from that of the previous network.

Pre-authentication: MN provides its credential to new network through previous attachment.

#### Pull:

After performing pre-authentication, MN may go to the target network. It then requests media-specific authentication keys from MIA-KH via MSA-KH.

#### Push:

After performing pre-authentication, the media-specific authentication keys are pushed to MSA-KH when MN actually goes to the target network.

### Options:

#### Co-locate MIA-KH with existing AAA proxy/server For pull, no change in existing link-layer specifications or implementations is needed for the pull mechanism. Push requires changes.

#### Not co-locating MIA-KH with existing proxy/server. For pull, no change in existing link-layer specifications is needed, but changes in AP/BS implementations may be needed for routing AAA messages to MIA-KH or existing AAA proxy/server depending on whether media-specific authentication key is pulled from MIA-KH or existing AAA proxy/server. . Push requires changes.

### Pull key distribution:

Refer to Key distribution figure in slide 9 of 21-09-0126-02

#### Conclusion: For pull model, there is no need to change existing link layer specifications. In addition, if MIA is co-located with existing AAA proxy/server, there may be no need to change link layer AP/BS implementations.

## A Study on IEEE 802.11r Approach (21-09-0148-02) is presented by Lily Chen

### IEEE 802.11 4-way handshake

After EAP authentication (not in 802.11), MSK is distributed from EAP server to authenticator. It then performs 4-way handshake using the 2 sets of keys: STA-PMK and AP-PMK.

802.11r key distribution: 802.21r states that “The protocol for distribution of keying material from the R0KH to the R1KH is outside the scope of this standard.”

### What we learn:

#### Key distribution is not a part of IEEE 802.11r.

#### A specific EAP method is not a part of IEEE 802.11.

#### It is independent to whether it is a Pre-authentication; Re-authentication; or Full-authentication.

### Do we have to introduce specific EAP methods in IEEE 802.21a?

#### No. EAP methods are specified by IETF and included in specific WG drafts.

### Shall MIHF or any IEEE 802.21 entities handle specific authentication?

#### If it is in EAP layer or above, then we will need to add function of a peer, an authenticator, or a server the 21 entity.

#### If it is a lower layer, then it cannot be media independent.

### Need to address these fundamental questions, even if we need to change the schedule.

### Editor’s assessment on generating a 21a document (21-09-0155-00) is deferred to AM2 section

## Recess at 10:05PM

# Third Day AM2 Meeting: Kona 1; Wednesday, September 23, 2009

## Meeting called to order by Yoshihiro Ohba, Chair of IEEE 802.21 Security Task Group Chair at 10:42AM

## Editor’s assessment on generating a 21a document (21-09-0155-00) is presented by Lily Chen

### Exercise for Work item 1: add modifications to each existing clause, e.g.,

#### Terminologies (Clause 3);

#### New IEs and services (Clause 6);

#### New primitives (Clause 7);

#### MIH function and new messages (Clause 8);

#### New interface(?).

### Each proposer:

#### Identify the changes needed for each clause in IEEE 802.21-2008 to accommodate the proposed mechanisms – To see which way a given proposal can be included..

### Exercise for Work Item 2

#### Add a new clause “Security” to cover MIH security: May need to introduce some new terminologies in Clause 3.

#### For protecting MIH (remote) message, multiple options may be included with specific recommendations, depending on the deployment environment. E.g.

Define MIH specific protections (with MIH specific authentication); (With or without MIH specific authentication; or Integrity and/or confidentiality. Peer to peer model or cache/distribute model.)

Recommend transport layer protection such as TLS.

## Proposal harmonization discussion

### Discussions in previous presentations were already part of harmonization discussion. No additional harmonization discussion happened.

## PKMv2 discussion (21-09-159-00) by Shubhranshu Singh

### In WiMAX network reference model, ASN-GW is an EAP authenticator. BS as Authentication Relay transparently forwards EAP messages between MS and ASN-GW over R6 interface.

### Once EAP authentication is successful, AK is distributed from ASN-GW to BS using a key distribution message defined in a WiMAX Forum specification.

## Closing Notes (21-09-0154-00) by Yoshihiro Ohba

### Progress in September 2009 meeting

#### Completed proposal presentation III with detailed text

#### EAR-FRM: Proposer agreed to ask IETF to publish EAP-FRM Internet-Draft as Informational or Experimental RFC.

#### Proactive auth and MIH Security: Detailed usage of IC TLV is added.

#### Key distribution and MIA/MSA discussions

Identified that pull model may not require any changes to link-layer specifications or implementations.

#### Made exercise on generating an 802.21a document

### Plan for November 2009 meeting

#### No down-selection in November.

#### More discussion on work item 1 with more detailed and comprehensive analysis on MIA/MSA architecture

#### Continue the exercise for generating 802.21a document: each proposal is expected to have suggested document structure using the 802.21 syntax.

### Teleconferences

#### Oct 15 (Thursday) 10AM-noon Eastern Time

#### Oct 29 (Thursday) 10PM-midnight Eastern Time

## Adjourn at 12:30PM until November plenary

# Attendees

Only the attendance of 802.21WG are available at this time. Refer to the attendees in 21-09-0152-04.