## Slide 1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: 21-12-0064-00-srho
Title: Access Information Database Design for 4G
Date Submitted: May 16, 2012
To be presented at IEEE 802.21 May Interim Meeting / Atlanta
Authors or Source(s): Charles E. Perkins, Futurewei
Abstract: This document discusses the requirement for access information database and how it can be achieved via MGW-based approach

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/guide.html>
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as stated in Section 6 of the IEEE-SA Standards Board bylaws <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/faq.pdf>

## Slide 3: MGW-oriented handover optimization supported by roaming agreement
SMGW
HMGW
TMGW
Inter MGW SA
Preregistration
MN movement
AN
tAN
AN

## Slide 4: Heterogeneous radio interfaces  need for access information
When UE sees degraded signal from current link, an alternate radio link may offer improve service  handover
Most current solutions geared towards same operator, same radio access technology (i.e., same RAT)
However, new trends indicate limitations of this approach
  “WiFi Offload” getting surprising amount of attention
  LTE will have trouble handling projected growth of data
Solution: enable UEs to make use of multiple radio interfaces
Existing solutions define services for access information
  3GPP: ANDSF; IEEE 802.21: MIIS; IETF: PAWS
  Each operator should be authoritative for its own network

## Slide 5: Access model for roaming partners
How does one operator provide all the information useful to its customers that have heterogeneous radios?
Likely authoritative for only one radio technology (RAT)
Access needed to authoritative data from roaming partners (at least)
Partner information should be cached by operator to avoid frequent cross-network access
Even more important for “single-radio” solutions
Needed: cross-network database access – so that each operator can fetch and provide to UEs authoritative data

## Slide 6: Other data must be stored as well (not just ISP location)
Per-UE policy
Local WiFi hotspots
Frequency selection, sector IDs, IP addresses
Emergency services on alternate RATs
Other pay-as-you-go services
Each category of access data has a requirement for freshness indication as well
Database organization is important
  Know when to delete data
  Know how to prioritize redundant data

## Slide 7: Proposal: local caching
For fastest response, UE should receive local access information from a local cache agent
Only information about local neighborhood(s) kept
  But, what is “local”
  What about redundant data?
Base stations often have overlapping neighborhoods
Same database access mechanism can be used by roaming partners and local cache agents
  But, likely restricted to specific neighborhood only
  Access formats, triggers to be defined
  Publish/subscribe model a good choice
  Caching policy restrictions for per-UE information

## Slide 8: AIDB-cache: AIDB local cache functional module
For IEEE 802.21, the MGW is one possibility
  otherwise could integrate with MIIS framework
In any case, augment initial network entry/attach to establish [UE  AIDB-cache ] security association
Advantage: faster handovers, avoid future overhead
Disadvantage: not always needed
  handovers commonly (typically?) between same ISP
  but anyway can establish along with other access (e.g., TS-33.401 figure 6.2-1)

## Slide 9: AIDB per operator network useful for handovers
Operators A and B are roaming partners
Access network AN1 overlaps access network AN2
AIDB cache AN1 subscribes to small part of AIDBA (Operator A)
AIDB cache AN1 subscribes to small part of AIDBB (Operator B)
AIDBA
AIDBB
A
N1
A
N2
Home AIDB access
Partner AIDB access

## Slide 10: Additional information is cached when UE attaches to AN1
UE attaches to home access network AN1
Access network AN1 fetches UE’s policy information from AIDBA
UE-specific policy at AN1 can restrict UE’s view of cache at AN1
AIDBA
AIDBB
A
N1
A
N2
Home AIDB access

## Slide 11: Similarly, additional information is cached when UE attaches to AN2
UE attaches to roaming access network AN2
Access network AN2 fetches UE-specific policy information from AIDBA
UE-specific information at AN2 can restrict UE’s view of cached data at AN2
AIDBA
AIDBB
A
N1
A
N2
Partner AIDB access

## Slide 12: MGW-based AIDB cache
Advantage: MGW adoption proceeding in IEEE 802.21c
Advantage: same access mechanism for all relevant radio access technologies
Advantage: simplified signaling compared to OMA
Advantage: UE can rely on MGW to identify proper target network
Disadvantage: does not exist in LTE – much work needed before any standard could appear

## Slide 13: Classes of Location Information
Fetched from local network LDB
Fetched from roaming partner
Inserted from inferred neighborhood
  From UEs
  From "friendly" network equipment (e.g., BS, AP) over secure interfaces
Inserted from neighborhood discovery
  i.e., by self-organizing network algorithms

## Slide 14: Policy information
Neighbor policy information
  Fetched per neighbor via "official" LDB transfers
  else, no mechanism for inferring policy
UE policy information
  Only when returned via authentication mechanisms
  No information --> best effort and, optionally, some grades of QoS when spare capacity exists

## Slide 15: SMGW  AIDB TLVs
"RAT-block" := (MGWaddr, tAN, RAT-type, LDB-cache_timeout, UE_policy)
UE_policy is also a complex type including timeout
Message types:
RAT-request (MNID, [RAT-block]+)
RAT-reply (MNID, MGW, tAN, RAT-type, UE policy)

## Slide 16: AIDB data fetch requirements
Needed between roaming partners  IPsec
Needed between operator authoritative database and local caches
Need to define “neighborhoods” and, if for MGW, “zones”
  A “neighborhood” is a set of reachable access points
  A “zone” would be a set of neighborhoods
Publish/subscribe model needed
New TLVs (? For ANQP ?)
Trigger events
  Timeouts, if defined, are per TLV
Need full zone transfer and incremental update formats

## Slide 17: MN moves: using SMGW
Handover preparation:
MN decides to move, requests assistance from SMGW
SMGW acquires information about {tAN, tBS, pAN, …}
SMGW signals target network to assist in preauthentication / preregistration for MN
Subsequent signaling same as before
(a) MN  MGW in originating network (i.e., “SMGW”).
(b) SMGW TMGW in network of a roaming partner
Overall, MN  SMGW  TMGW  {tAN, tBS, pAN, …}

## Slide 18: Annex N (srho-secure-key-distribution)

## Slide 19: SMGW as proxy N/W selector
  /* Let Ksmgw define security association SMGW  MN */
    TLV: MN-TMGW_setup.request to SMGW
      preferred.RATs
      nonce
   Here, SMGW could contact AIDB to find TMGW
  /* Let Kstmgw define security association SMGW  TMGW */
    TLV: SMGW-TMGW_setup.request for MN
      preferred.RATs
      SA lifetime
      MNaddr
      nonce
      Ktmgw ⊕ PNGstmgw (MNaddr, nonce)

## Slide 20: Standardization requirement
Proposal: multicast address for local AIDB cache
New TLVs for authoritative AIDB requests, replies
New TLVs for AIDB cache requests, replies

## Slide 21: Operation requirements
New database organization / expertise
Possible need to purge “problematic” neighbors
Blacklists / whitelists
Approach seems much easier than alternatives