## Slide 1
<number>
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: 21-09-0014-00-0sec
Title: Security Group TR
Date Submitted: 20th January, 2009
Presented at IEEE 802.21 session #30 in LA
Authors or Source(s):
Shubhranshu Singh (Samsung)
Abstract: The slides summarizes Security SG TR “1-08-0172-02—0Sec-SecuritySG-technical-Report.doc”
Notes: <number>

## Slide 2
<number>
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as stated in Section 6 of the IEEE-SA Standards Board bylaws <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/faq.pdf>
Notes: <number>

## Slide 3: Background
Security-related handover signaling increases latency and often service continuity can’t be met impacting user experience
  Thus need for optimization
  TR discusses related use cases, requirements, assumptions and possible approaches
IEEE 802.21-2008 Spec does not address MIH protocol security
  TR discusses integrity, replay protection, confidentiality, data origin authentication and authorization
Intra & Inter-AAA domain handover poses different challenges
  TR lists related requirements & assumptions
This TR too is intended to provide guidelines & requirements to the 802.21a TG

## Slide 4: Terminologies (1/2)
Candidate Authenticator: The authenticator on a candidate Point of Attachment (PoA) with respect to the mobile node
EAP Pre-authentication: Utilization of EAP to pre-establish EAP keying material on an authenticator prior to attaching the peer to the access network managed by that authenticator
Serving Authenticator: The authenticator on the serving PoA/PoS
Target Authenticator: The authenticator on the target PoA/PoS
AAA domain: See RFC2903

## Slide 5: Terminologies (2/2)
AAA domain: See RFC2903
Roaming Scenario: The scenario where an Access Service Network (ASN) provider has Service Level Agreement (SLA) that allows a device/user to move between two ASNs.
Non-roaming Scenario: The scenario where there is no Service Level Agreement (SLA) between two ASN providers such that a device/user may not be able to move between the ASNs without authentication from target ASN.
  More listed in 21-08-0172-02—0Sec-SecuritySG-technical-Report.doc

## Slide 6: Dual and Single Radio Handovers
Dual radio handover:
  Both radios are active.
    Target preparation can be done via the target radio i.e. make-before-break
Single radio handover:
  Only one radio is active at a time
    Target preparation is done using the active radio i.e. break-before-make
    Hard to avoid service disruption without additional optimization

## Slide 7: Security signaling optimization during handover

## Slide 8: Security Signaling Optimization
Scenarios addressed in the TR

## Slide 9: General assumptions
EAP is used as the access authentication protocol for each of the media types. The EAP methods provide mutual authentication and required key material.
A MN is authenticated with the serving authenticator through an EAP method
MN shall be able to discover candidate authenticators
Furthermore, HOKEY key hierarchy may be supported by the employed EAP methods

## Slide 10: General Requirements
Subscriber possesses MN which gives access to 802 access networks.
Transition between networks shall be automatic and shall not require the manual intervention of the user. The Network and MN should work in tandem to provide the most optimal handover experience.
It shall conduct an authentication prior to handover to a target network. That is, a transition to a different network shall be authorized based on an authentication.
The handover procedure shall establish a security context in the target network
The resource consumption (including network traffic and power consumption) of the authentication and key establishment for handovers should be minimized with respect to a full EAP authentication.
The delay caused by the authentication and key establishment for handovers should be minimized.

## Slide 11: Use Scenarios
Scenarios 1
  A mobile device transitions between two 802-based networks of different media types (e.g., 802.11 and 802.16) within the same AAA domain
Scenario 2
  A mobile device transitions between two networks of different media types (e.g., 802.16 and 802.11) and deployed in different AAA domains
Scenario 3
  A mobile device transitions between two networks with the same media types (e.g., 802.16) and deployed in different administrative domains

## Slide 12: Potential Approaches

## Slide 13: EAP Pre-authentication (1/2)
Direct Pre-authentication

## Slide 14: EAP Pre-authentication (2/2)
Indirect Pre-authentication

## Slide 15: EAP Pre-Authentication General Requirements (1/2)
MIH PoS shall support the functionalities of authenticator for EAP pre-authentication
MN shall support the functionality of peer for EAP pre-authentication
An authenticator discovery mechanism shall be defined. The authenticator discovery mechanism must provide a mapping between a link-layer address and an IP address of an authenticator
A context binding mechanism shall be defined so that a link-layer specific security context is bound to the EAP keying material generated as a result of EAP pre-authentication. The link-layer specific security context includes link-layer addresses of a peer and an authenticator

## Slide 16: EAP Pre-Authentication General Requirements (2/2)
Higher-layer transport shall be supported for carrying EAP pre-authentication messages between MN and CA, between MN and SA and between SA and CA
Link-layer transport shall be supported for carrying EAP pre-authentication messages between MN and SA
The EAP pre-authentication process shall define a ‘lifetime’ parameter (pre-authentication validity time-out)

## Slide 17: Proactive Re-authentication
MN/Serving network discovers one/more target network
MN/Serving network chooses one target network to handover to and initiates EAP re-authentication between MN and target Authenticator
Upon a successful EAP re-authentication, the authenticator will receive an rMSK that is delivered from the EAP server
rRK-1
rRK-2
rMSK-2
rMSK-1
EMSK or DSRK
rIK-1
rIK-2

## Slide 18: EAP Re-authentication General Requirements (1/2)
MIH PoS shall support the functionalities of authenticator for EAP re-authentication
MN shall support the functionality of peer for EAP re-authentication
An authenticator discovery mechanism shall be defined. The authenticator discovery mechanism must provide a mapping between a link-layer address and an IP address of an authenticator
A context binding mechanism shall be defined so that a link-layer specific security context is bound to the EAP keying material generated as a result of EAP re-authentication. The link-layer specific security context includes link-layer addresses of a peer and an authenticator.

## Slide 19: EAP Re-authentication General Requirements (2/2)
Higher-layer transport shall be supported for carrying EAP re-authentication messages between MN and CA/TA and between CA/TA and ERS
Link-layer transport shall be supported for carrying EAP re-authentication messages between MN and CA/TA
There shall be a trust relationship between each CA/TA and ERS, which may be established via mutual authentication
If an ERS is a local authentication server, then there shall be a trust relationship between the ERS and home EAP server, which may be established via mutual authentication
There shall be a protected channel for confidentiality and integrity between each CA/TA and the ERS for the rMSK delivery

## Slide 20: MIH Protocol Security

## Slide 21: Terminologies (1/2)
Access control policy: The set of rules that define the conditions under which an access may take place
Home subscriber network: - Network managed by an operator with whom the subscriber has a business relationship
Visited network: A network managed by an operator other than the subscriber’s home operator which the subscriber is receiving services
Trusted third party: An entity trusted by MIHF peer to provide authentication support, for example, issuing certificate for the public keys. AAA server is a trusted third party to MN and PoS when the AAA services are available.

## Slide 22: Terminologies (1/2)
MIH Service provider: A business entity which provides MIH services
MIH Home Service Provider: A MIH Service Provider, with whom the MN has a subscription for MIH services
AAA services: Authentication, authorization and accounting services for network access, MIH access, or both access
MIH specific protection: To provide authenticity/integrity and confidentiality for MIH messages so that the protection is independent of the transport protocols for MIH messages. MIH specific protection is applied end-to-end between two MIHFs

## Slide 23: MIH Protocol Security
General Considerations
  Whether access to MIH services is controlled by the MIH service controller/provider or not
  Whether AAA services are available for MIH services or not. It might not make much difference if there is a dedicated AAA service for MIH or shared AAA service with media/network
  Whether it is possible to use any infrastructure e.g. PKI or not
  Which transport protocol used for MIH protocol message exchange
  Whether the transport protocol used for MIH protocol message exchange are protected

## Slide 24: MIH Protocol – Threat Analysis
Threats are identified by classifying them according to the below actions involved in vertical handover using the MIH protocol
  Information Query
  Resource availability check
  Resource preparation
  Resource release
Identified Threats
  Identity Spoofing
  Tampering
  Information disclosure
  Denial of Service

## Slide 25: Use case Framework
MIH Access control?
Access Authentication (maybe mutual through access controller, e.g. service provider)
Yes
Mutual Authentication (through a Trusted Third Party, e.g. PKI)
Key establishment (MN and PoS)
MIH Authenticity/integrity and confidentiality
MIH specific auth?
yes
Transport Authenticity/integrity and confidentiality
MIH specific protection?
no
no
yes
The transport protections may or may not be in the place

## Slide 26: Use Cases (contd..)
Access Control is applied:
  Access control is applied through the access controller
  Use case 1.1:
    Access Authentication with a Key establishment procedure
MIH Access control?
Access Authentication (maybe mutual through access controller, e.g. service provider)
yes
no
Mutual Authentication (through a Trusted Third Party, e.g. PKI)
Key establishment (MN and PoS)
MIH Authenticity/integrity and confidentiality
MIH specific auth?
yes
Transport Authenticity/integrity and confidentiality
MIH specific protection?
no
no
yes
The transport protections may or may not in the place

## Slide 27: Use Cases (Contd…)
MIH Access control?
Access Authentication (maybe mutual through access controller, e.g. service provider)
yes
no
Mutual Authentication (through a Trusted Third Party, e.g. PKI)
Key establishment (MN and PoS)
MIH Authenticity/integrity and confidentiality
MIH specific auth?
yes
Transport Authenticity/integrity and confidentiality
MIH specific protection?
no
no
yes
Use case 1.2:
  Access Authentication without a Key establishment procedure
The transport protections may or may not in the place

## Slide 28: Use Cases (Contd…)
Access Control is not applied
  Use case 2.1:
    MN & PoS mutually authenticates and establishes security keys
MIH Access control?
Access Authentication (maybe mutual through access controller, e.g. service provider)
yes
no
Mutual Authentication (through a Trusted Third Party, e.g. PKI)
Key establishment (MN and PoS)
MIH Authenticity/integrity and confidentiality
MIH specific auth?
yes
Transport Authenticity/integrity and confidentiality
MIH specific protection?
no
no
yes
The transport protections may or may not in the place

## Slide 29: Use Cases (Contd…)
Use case 2.2:
  No mutual authentication and Key establishment
MIH Access control?
Access Authentication (maybe mutual through access controller, e.g. service provider)
yes
no
Mutual Authentication (through a Trusted Third Party, e.g. PKI)
Key establishment (MN and PoS)
MIH Authenticity/integrity and confidentiality
MIH specific auth?
yes
Transport Authenticity/integrity and confidentiality
MIH specific protection?
no
no
yes
The transport protections may or may not in the place

## Slide 30: Use Cases
3. Visited Domain access
  MN access MIH services through a visited MIH service provider
  Use case 3.1
    The MIH protocol security policies are same as that of the home domain
  Use case 3.2
    The MIH protocol security policies are different from those of home domain

## Slide 31: Thank You