## Slide 1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
Title: Multi-Radio Power Conservation Management
Date Submitted: February 13 2009
Presented at IEEE 802 plenary in VanCouver
Authors or Sources: Kevin Knoll, Dennis Edwards, Behcet Sarikaya, Junghoon Jee, Anthony Chan
Abstract: 802.21 MRPM Tutorial

## Slide 2: Contents
Need for 802.21c MRPM
Existing power management in individual networks
802.21 Medium Independent Handover framework (if needed)
MRPM principle
Use cases
MRPM Mechanism Examples

## Slide 3: Interface power consumption
Interface modes
  Active or powered on
  Sleep or idle with paging channel on
  Powered off
Interface power 70% of total power
Multi-radio usage more mainstream
Source: mobisys 2006
Power breakdown for a connected multi-radio mobile device in idle mode
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: Multiple interfaces sharing a battery
802.11
802.16
3GPP;
3GPP2
802.11
802.16
3GPP;
3GPP2
+
–
+
–
+
–
+
–
Multiple-interface device:
will drain battery fast if power consumption is optimized only within each individual network technology
Single-interface device:
Different technologies have different modes of operation each with different power consumption

## Slide 5: Battery life for multiple interfaces without MPRM
 | Active | Standby | Normal sleep |  | Off | Battery life (approx. numbers only for cellular )
1 interface | A |  |  |  |  | 2 hrs
1 interface |  | A |  |  |  | 24 hrs
2 interfaces |  | A,B |  |  |  | 12 hrs
3 interfaces |  | A,B,C |  |  |  | 8 hrs
1 interface |  |  | A |  |  | 6  24 hours
2 interfaces |  |  | A,B |  |  | 3  24 hours
3 interfaces |  |  | A,B,C |  |  | 2  24 hours

## Slide 6: Summary of Problem
Multi-mode terminals are becoming popular
Multi-mode terminals consume more power
Each radio power is managed independently of the other radios
Connection managers being used in terminals
  They are proprietary
  They don’t make use of any network signaling
Integrated radio management is needed to enhance battery life by enabling control of multi-radio power states depending on characteristics of each radio’s power consumption and application needs.
Example: Keep only one radio powered on and power off the rest.

## Slide 7: MRPM
Purpose: Enhance the user experience by extending the battery operating life of multi-radio mobile devices.
Scope: Define mechanisms to reduce power consumption of multi-radio mobile devices on heterogeneous IEEE 802.21 compliant networks.
Not in Scope: Enhancements to the MAC/PHY of individual access technologies for making them more power efficient are outside the scope of this project.

## Slide 8: Contents
Need for 802.21c MRPM
Existing power management in individual networks
802.21 Medium Independent Handover framework (if needed)
MRPM principle
Use cases
MRPM Mechanism Examples

## Slide 9: Broad category of Modes (varies in specific networks)
On/Active: actively running a network application such as transmitting data to or receiving data from the network.
Standby: On and ready to transmit and to receive data
Sleep mode: off but wakes up at regular intervals in synchrony with network to transmit and to receive data when needed. Sleep interval varies
Deep sleep mode: very longer sleep interval
Off: completely off

## Slide 10: Broad category of Modes (varies in specific networks)
On/active
Actively running a network application
Standby
Always ready to communicate
Sleep
Check at scheduled times whether to communicate
Time
Power
T
P
T
P
Life
Life
Life

## Slide 11: Power Management in 802.11/16
 | Mode/state | Tx | Rx | Registration | Control signaling | Bearer traffic | Time to wake-up
WiFi | Active | Full | Full | Yes | Yes | Yes | N/A
 | Power save | No | DTIMs | Yes | DTIMs only | No | Long
 | Sleep | No | Some DTIMs | Yes | Some DTIMs | No | > PS
 | Off | No | No | No | No | No | Power-up
WiMAX | Active | Full | Full | Yes | Yes | Yes | N/A
 | Sleep, class 1 | Partial | Partial | Yes | Yes | Yes | Quick
 | Sleep, class 2 | Partial | Partial | Yes | Yes | Yes | Quick
 | Sleep, class 3 | Partial | Partial | Yes | Yes | Yes | Quick
 | Idle | No | Wake-up paging only | No | Wake-up paging only | No | Long
 | Off | No | No | No | No | No | Power-up

## Slide 12: Power Management in 3GPP/3GPP2
 | Mode/state | Tx | Rx | Registration | Control signaling | Bearer traffic | Time to wake-up
3GPP | Active | Full | Full | Yes | Yes | Yes | N/A
 | Control hold | Partial | Partial | Yes | Yes | Yes | Quick
 | Suspended | Partial | Partial | Yes | Yes | Yes | > Control hold
 | Dormant | Little | V. Limited | Yes | V. Limited | Burst | Long
 | Off | No | No | No | No | No | Power-up
3GPP2 | Connected | Full | Full | Yes | Yes | Yes | N/A
 | Idle (camped) | Partial | Partial | Yes | Yes | No | Quick
 | I (not camped) | Partial | Partial | No | Partial | No | Long (san/camp)
 | Off | No | No | No | No | No | Power-up

## Slide 13: Possible time scales for 802.11
DTIM interval
Beacon interval
In sleep mode (extended PS mode), may adjust sleep interval, but no GTK update.
In power-saving (PS) mode, response time is several beacon intervals: fraction of a second.
Automatic PS delivery (APSD) mode: Use algorithm to adjust PS time to finer granularity or when there are packets to transmit
In active mode, response time depends on traffic and QoS class.
Location and BSS change: during wake at the designated DTIM
Sleep interval
CSMA/CA (Active mode)
PS mode
Deep sleep
10ms
100ms
1s
10s
1ms
>10s
APSD time granularity

## Slide 14: Possible time scale for 802.16m
Sleep interval
Idle to active (802.16e)
Deep sleep
Idle to active (802.16m)
10ms
100ms
1s
10s
1ms
>10s
Location determination
Handover delay
Multicast channel reselection
Idle mode (not registered): periodically listens to paging broadcast over a large area, performs location update,
Sleep mode (registered): variable sleep interval (2-1024 frames, frame duration =2-20 ms), with variable connections:
Type I: for NRT-VR, BE
Type II: for RT-VR, UGS
Type III: management operations, periodic ranging (for HO)

## Slide 15: Contents
Need for 802.21c MRPM
Existing power management in individual networks
802.21 Medium Independent Handover framework (if needed)
MRPM principle
Use cases
MRPM Mechanism Examples

## Slide 16: Medium Independent Handover framework
(if needed)

## Slide 17: Contents
Need for 802.21c MRPM
Existing power management in individual networks
802.21 Medium Independent Handover framework (if needed)
MRPM principle
Use cases
MRPM Mechanism Examples

## Slide 18: MRPM principle
Keep an energy efficient radio “on” for receiving notification of incoming service.
Put unused radios in low power state.
Notify the “on” radio of traffic destined for an “off-available” radio, through new network functions, so that the device may wake up the off-available radio.

## Slide 19: Battery life for multiple interfaces without MPRM
 | Active | Standby | Normal sleep |  | Off | Battery life (approx. numbers only for cellular )
Standby |  | A |  |  |  | 24 hrs
2 interfaces |  | A,B |  |  |  | 12 hrs
MRPM |  | A | B |  |  | 24 – 3.5 hrs
 |  | A |  |  | B | 24 hrs
Sleep |  |  | A |  |  | 6  24 hrs
2 interfaces |  |  | A,B |  |  | 3  24 hrs
MRPM |  |  |  |  |  | 
 |  |  | A |  | B | 6  24 hrs

## Slide 20: Battery life versus ?
Connectivity
Different modes of operation
in different technologies
Active/on
Off
+
–
CDMA
Sleep?
802.11
Sleep?
802.16
Sleep?
802.11
Idle?
+
–
Response time
+
–
+
–
Data rate?
Discharge rate?
Temperature?
Charge count?
Battery life
also depends on
Play back-start
Fast call set up
Record-start
Streaming-start
Background-start
PTT (interactive)
Webpage-start

## Slide 21: Power saving versus application requirements
There are tradeoffs between power-saving and operational capabilities.
The operations involved include:
  Handover
  Response to paging
  Location update, etc.
The capability to perform each operation while optimizing power saving depends on Application requirements

## Slide 22: Possible time scale coming from applications
10ms
100ms
1s
10s
Play back-start (interactive)
Fast call set up
1ms
Lip synchronization
Jitter in voice and video
Record-start (interactive)
Streaming-start
Background-start
>10s
PTT (interactive)
Delay (conversational)
Hold  on
Sleep  on
(IEEE C802.20-03/13r1)
Mean Web think time
Webpage-start

## Slide 23: Sleep interval
T
P
Life
T
P
Life
Normal sleep
Shorter response time to paging
Shorter battery life
Deep sleep
Longer response time to paging
Longer battery life

## Slide 24: Broad category of Modes (varies in specific networks)
On/Active: actively running a network application such as transmitting data to or receiving data from the network.
Standby: On and ready to transmit and to receive data
Sleep mode: off but wakes up at regular intervals in synchrony with network to transmit and to receive data when needed. Sleep interval varies
Deep sleep mode: very longer sleep interval
Off: completely off

## Slide 25: Response time versus power saving
Network (MIH) can be informed of the response time requirements of the applications
Knowing the response times of the different modes for different interfaces is useful to figure out the multiple interface power saving strategy to trade-off between response time and power saving and to determine the appropriate sleep interval.
Network can be informed of the actual multiple-interface power saving states of the MN to determine how to reach the MN (whether to wake, and wake which interface)

## Slide 26: Battery life for multiple interfaces without MPRM
 | Active | Standby | Normal sleep | Deep sleep | Off | Battery life (approx. numbers only for cellular )
Standby |  | A |  |  |  | 24 hrs
2 interfaces |  | A,B |  |  |  | 12 hrs
MRPM |  | A | B |  |  | 24 – 3.5 hrs
 |  | A |  | B |  | 24 hrs almost
 |  | A |  |  | B | 24 hrs
Sleep |  |  | A |  |  | 6  24 hrs
2 interfaces |  |  | A,B |  |  | 3  24 hrs
MRPM |  |  | A | B |  | 6  24 hrs almost
 |  |  | A |  | B | 6  24 hrs
1 interface |  |  |  | A |  | >> 6  24 hours

## Slide 27: Contents
Need for 802.21c MRPM
Existing power management in individual networks
802.21 Medium Independent Handover framework (if needed)
MRPM principle
Use cases
MRPM Mechanism Examples

## Slide 28
To be filled in

## Slide 29: Contents
Need for 802.21c MRPM
Existing power management in individual networks
802.21 Medium Independent Handover framework (if needed)
MRPM principle
Use cases
MRPM Mechanism Examples

## Slide 30: Examples of MRPM mechanisms
1. Provide input parameters for multi-radio power management policy.
2. Enable the optimal power configuration of different radios in a multi-radio mobile device: whether radio is “on,” “off-available,” or “off-do-not-disturb.”
3. Enable power management through co-ordination across multiple networks of different radios, taking into account the power management functions in individual radios and networks and QoS requirements. The power management of the overall system involves the following:
  3.1 Keep an energy efficient radio “on” for receiving notification of incoming service.
  3.2 Put unused radios in low power state.
  3.3 Notify the “on” radio of traffic destined for an “off-available” radio, through new network functions, so that the device may wake up the off-available radio.
4. Reduce or avoid futile scanning by unused radios.

## Slide 31: Broad category of Modes (varies in specific networks)
On/Active: actively running a network application such as transmitting data to or receiving data from the network.
Standby: On and ready to transmit and to receive data
Sleep mode: off but wakes up at regular intervals in synchrony with network to transmit and to receive data when needed. Sleep interval varies
Deep sleep mode: very longer sleep interval
Off: completely off

## Slide 32: Category of Modes under MRPM
on
off-available
off-do-not-disturb

## Slide 33
Others to be filled in

## Slide 34: Multi-radio power conservation management
PAR/5C is at:
https://mentor.ieee.org/802.21/file/08/21-09-0021-00-mrpm-revised-par-and-5c.doc
Feedback:
anthonychan@huawei.com; jhjee@etri.re.kr;
STDS-802-21@LISTSERV.IEEE.ORG

## Slide 35: Thank you