IEEE P802.22
Wireless RANs

| Combined MCS, Mode and Precoder Design for Point to Point MIMO in WRAN with Limited CSI Feedback |
| --- |
| Last Revised - Date: 2007-01-03 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Vincent K. N. Lau | HKUST | Hong Kong, China | 852-2358-7066 | eeknlau@ece.ust.hk |
| Wai Ho Mow | HKUST | Hong Kong, China | 852-2358-7070 | eewhmow@ece.ust.hk |
| Roger S. Cheng | HKUST | Hong Kong, China | 852-2358-7072 | eecheng@ece.ust.hk |
| Ross D. Murch | HKUST | Hong Kong, China | 852-2358-7044 | eermurch@ece.ust.hk |
| Khaled Ben Letaief | HKUST | Hong Kong, China | 852-2358-7064 | eekhaled@ece.ust.hk |
| Linjun Lu | Huawei Technologies | Shenzhen, China | 0086-755-28973119 | lvlinjun@huawei.com |
| Soo-Young Chang | Huawei Technologies | Davis, CA, U.S. | 1-916 278 6568 | sychang@ecs.csus.edu |
| Jianwei Zhang | Huawei Technologies | Shenzhen, China | 86-21-68644808 | zhangjianwei@huawei.com |
| Lai Qian | Huawei Technologies | Shenzhen, China | 86-755-28973118 | qlai@huawei.com |
| Jianhuan Wen | Huawei Technologies | Shenzhen, China | 86-755-28973121 | wenjh@huawei.com |

| Co-Author(s): |
| --- |
| Name | Company | Address | Phone | email |
| Terry T.Y. Wu | HKUST | Hong Kong, China | 852-2358-7086 | wuty@ust.hk |
| S. M. Mok | HKUST | Hong Kong, China | 852-2358-7086 | eebao@ust.hk |
| Edward K. S. Au | HKUST | Hong Kong, China | 852-2358-7086 | eeedward@ece.ust.hk |
| Zhou Wu | Huawei Technologies | Shenzhen, China | 86-755-28979499 | wuzhou@huawei.com |
| Jun Rong | Huawei Technologies | Shenzhen, China | 86-755-28979499 | rongjun@huawei.com |
| Jian Jiao | Huawei Technologies | Beijing, China | 86-10-82882751 | Jiao_jian@huawei.com |
| Meiwei Jie | Huawei Technologies | Shenzhen, China | 86-755-28972660 | jiemingwei@huawei.com |

Combined MCS, Mode and Precoder Design for Point to Point MIMO in WRAN with Limited CSI Feedback

## 1.  Introduction

We propose an integrated framework of optimizing the MCS (modulation and coding scheme), mode and precoding adaptation design for slow fading correlated MIMO channels with limited feedback. In the proposed design framework, the online adaptation algorithm is very simple while the offline mechanism to build the MCS, Mode Selection and Precoder table as well as the channel state information (CSI) partition at the receiver is modeled as a VQ (Vector Quantization) optimization problem where both the feedback strategy and the transmission adaptation strategy are jointly designed to maximize average system goodput. A design of 2 MAC management messages with the respective message flow in WRAN systems is also proposed.

## Existing Mechanism and the Drawbacks

The existing mechanism of the precoder design and rate adaption in point-to-point WRAN MIMO system is specified in specification Annex C.6 [1]. The design provides a beamforming solution that satisfies equal power/antenna in addition to the total power constraint while only a limited feedback bits are available. Although TDD and slow fading system are considered, the reason that the feedback bits for channel state information is assumed to be limited is because the US (Upstream) and DS (Downstream) subcarriers allocation may be different. Hence, the channel state information at the transmitter (CSIT) estimated though US may not be able to be applied on the DS channel. The existing mechanism uses ARQ to control the transmission rate.

However, there are a number of drawbacks related to the mechanism stated above.

- The number of data streams (the transmission mode) is not determined by CSIT.

- No power allocation is included in the precoder design algorithm.

- Control rate adaptation by simply relying on ARQ may lead to poor performance, as

  - The ARQ feedback may be outdated when the data traffic is bursting.

  - The user may not operate in a fixed channel. When the channel changes, the ARQ is unable to predict the CSI of the new channel.

- When the MIMO channel is spatially correlated, it is not sure about which transmission mode should be selected (Spatial Multiplexing or Spatial Diversity).

## Mechanism Design

In this section, we present the proposed integrated limited feedback design framework for MIMO system under the slowly fading and spatially correlated channel to maximize the MIMO system goodput through MCS, mode and precoder adaptation. In particular, we propose

1. 	An efficient combined MCS, Mode and Precoder Online Adaptation framework;

2. 	An offline mechanism to build the MCS, Mode Selection and Precoder table as well as the CSI partition at the receiver.

3.	MAC management messages and the respective message flow for the WRAN system as an application example.

The following shows the embodiment with reference to the system model illustrated in Figure 1, in which the perfect and noiseless channel state information at the MIMO receiver (CSIR) is assumed. In addition, the MCS, mode and precoder codebook is known to both both the transmitter and the receiver. On the other hand, the CSIR space is partitioned into 2Cfb non-overlapping regions, where Cfb is the number of bits available for feedback.

Figure 1. System block diagram for the proposed framework.

## 3.1.  Description of the Online Algorithm

The online adaptation algorithm is very simple and is summarized as follows. Upon receiving data, the receiver estimates the instantaneous CSIR H and determines the partition H belongs to. Suppose H belongs to i-th partition, the receiver will feedback the index i with Cfb feeback bits to the MIMO transmitter as the CSI. Once the transmitter receives the bits, the MCS, mode and precoder from the i-th entry of the codebook that will be used for data transmission can be obtained.

For example, suppose there are 3 transmit and receive antennas and there are 4 bits of CSI feedback available. At the transmitter, there is a table (with 16 entries) of Precoding Matrix V, MCS (R) and Spatial Multiplexing/Spatial Diversity Mode. At the receiver, there is a partition (with 16 regions) of the CSIR space. At a particular time slot, the receiver estimates the current CSI and determines which of the 16 regions it falls into. After that, it feeds back the region index (e.g. 3) to the transmitter via the 4-bit feedback link. The transmitter then utilizes the MCS, Mode and Precoder from the 3rd entry in the table.  The advantages of the online algorithm two-fold, namely are low overhead (4 bits) and low complexity.

## Description of the Offline Algorithm

The offline design is a mechanism to build the MCS, Mode Selection and Precoder table as well as the partition at the receiver. There are a number of literatures talking about codebook and partition design [2,3,4].  We propose to jointly optimize the table and the partition so as to maximize the total effective “goodput”.

The offline algorithm is equivalent to a VQ problem and can be solved by an iterative Lloyd’s algorithm. As an example, the optimal codebook designed for 2-by-2 system with 9dB SNR and 2 bits feedback is listed below.

Table 1—The Codebook of 2 by 2 MIMO system with SNR 9dB and 2 bits feedback

| Codebook Entry | MCS (R) | Mode (M) | Precoder (V) |
| --- | --- | --- | --- |
|  | Modulation | Encoding Rate |  |  |
| 1 | BPSK | 3/4 | 2 |  |
| 2 | 16QAM | 3/5 | 1 | [-0.7059 -0.6581+0.2620i]T |
| 3 | 16QAM | 7/8 | 1 | [-0.7048 -0.6556+0.2711i]T |
| 4 | 64QAM | 3/4 | 1 | [-0.7073 -0.6537+0.2690i]T |

The rule of determining the channel partition is as follows.

where, R is the transmission rate that MCS can provide, M is the transmission mode which denotes the number of data streams transmit simultaneously, is the right singular matrix of H and P is the power constraint.

## MAC Management Message Design

Suppose there are several feedback bits (e.g. 4) for a sub-channel in the WRAN system in which a CPE occupies several sub-channels (e.g. 2 discontinuous sub-channels). In this case,

two management messages and the respective message flow are needed to support the limited feedback framework.

The BS shall use a message to inform the CPE when feedback is needed on the 2 sub-channels occupied by the CPE. We define the message as CFB-REQ, which consists of the following elements:

•The starting feedback frame

•Number of feedback frames

•Index of the sub-channels requiring feedback

When the CPE received the feedback requesting message, it shall use a message to report limited feedback to the BS (4 bits per sub-channel). We define the message as CFB-RSP, which consists of the following elements:

•Index of the feedback sub-channels

•Limited feedback bits for these sub-channels.

Tables 2-5 show the designed control messages.

Table 2—CFB-REQ message format

Table 3: CFB-REQ message body

Table 4: CFB-RSP message format

Table 5—CFB-RSP message body

We shall note that the CFB-REQ/RSP can be applied to both downstream and upstream transmission.

In Table 5, the maximum number of bits for each sub-channel is 8. However, it is woth noting that this is not compulsory. If the codebook is smaller, the actual feedback bits can be smaller than 8. It is because for larger codebook, the online algorithm will be more time consuming.

Additionally, we shall add these 2 messages to the Table 24 of [1] as well.

Table 24—Management messages

Figure 2.  An illustration of the message flow.

## 5. Simulation

The simulation configurations are as follows.

- Antenna spacing / wavelength = 1

Remarks: Since the TV operating band is 47-910 MHz, the WRAN system can work on ~100MHz band with a wavelength 3m. Hence, the unit ratio is a reasonable setting. Note that the calculation of correlation matrix only needs the ratio [5], and the corresponding channel correlation coefficient is 0.94.

- Number of scatters = 100

- Angular spread (transmit correlation) = 20 (in degree)

- Feasible mode = 1 to Nr (assuming Nt > = Nr), where Nt and Nr are the numbers of transmit and receive antennas, respectively.

- FER constraint is ( = 0.01

Figure 3. Goodput comparison in a 2-by-1 system with transmit correlation coefficient = 0.94.

Figure 4. Goodput comparison in a 2-by-2 system with transmit correlation coefficient = 0.94.

From Figure 3 and Figure 4, we can find that the SNR gain of the proposed design with respect to the current design of [1] is around 12dB and 8dB for 2-by-1 and 2-by-2 systems, respectively. The significant SNR gain illustrates the importance of rate and mode adaptation in the slow fading spatial correlated channels of WRAN system. In addition, the online algorithm of the proposed design is quite simple hence the proposed design is very practical.

Reference:

[1]	IEEE 802.22/D0.1, Draft Standard for Wireless Regional Area Networks Part22: Cognitive Wireless RAN Medium Access Control (MAC) and Physical Layer (PHY) specifications: Policies and procedures for operation in the TV Bands, IEEE Standard, May 2006.

[2] 	R. W. Heath, Jr. and A. J. Paulraj, “Switching between diversity and multiplexing in MIMO systems,” IEEE Transactions on Communications, vol. 53, pp. 962-968, June 2005.

[3] V. K. N. Lau, Y. Liu and T. A. Chen, “On the design of MIMO block-fading channels with feedback-link capacity constraint,” IEEE Transactions on Communications, vol. 52, pp. 62-70, January 2004.

[4] D. J. Love, R. W. Heath, Jr. and T. Strohmer, “Grassmannian beamforming for multiple-input multiple-output wireless systems,” IEEE Transactions on Information Theory, vol. 49, pp. 2735-2747, October 2003.

[5] H. Zhang, H. Dai, “Fast transmit antenna selection algorithms for MIMO systems with fading correlation,” in Proceedings of IEEE Vehicular Technology Conference Fall, 2004.

# Text boxes

Notice: This document has been prepared to assist IEEE 802.22. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.22.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures

<http://standards.ieee.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <Carl R. Stevenson> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.22 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

We propose an integrated framework of joint optimizing the MCS (modulation and coding scheme), mode and precoding adaptation design for slow fading correlated MIMO channels with limited feedback. A design of 2 MAC management messages and the respective message flow in WRAN system shll also be presented.

CFB-RSP

61

Basic

MIMO Channel Feedback Request

CFB-REQ

60

…

…

…

0-59

Connection

Description

Message

Type

}

}

The index of the partition that the CSI belongs to. Shall be Feedback to the transmitter through the reverse link. The transmitter will use the parameters (rate, mode and precoder) within the corresponding codebook on the forward link.

8 bits

Feedback for the sub-channels

The index of the sub-channels requested to estimate and feedback.

8 bits

Sub-channel index

For i= 1:c {

The number of sub-channels requested to estimate and feedback.

8 bits

Number of sub-channels, c

CFB-RSP_Message_Body() {

Notes

Size

Syntax

}

Table 4

Variable

Message Body

8 bits

Management Message Type = 61

CFB-RSP_Message_Format() {

Notes

Size

Syntax

}

Shall be set to zero

8 bits

reserved

}

The index of the sub-channels requested to estimate and feedback

8 bits

sub-channel index

For i = 1:c {

The number of sub-channels requested to estimate and feedback

8 bits

Number of sub-channels, c

The number of frames over which to measure

7 bits

Number of Frames

The least significant 8 bits of the frame to start the measurement

8 bits

Frame Number

CFB-REQ_Message_Body() {

Notes

Size

Syntax

}

Table 3

Variable

Message Body

8 bits

Management Message Type = 60

CFB-REQ_Message_Format() {

Notes

Size

Syntax

MIMO Channel Feedback Response

Basic