IEEE P802.22
Wireless RANs

| Proposed Changes to Section 6.16.8 of Draft v1.0 |
| --- |
| Date: 2008-05-06 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Winston Caldwell | Fox | 10201 W. Pico Blvd. Los Angeles, CA 90064 | 310-369-4367 | Winston.caldwell@fox.com |

6.16.8	BS Transmit Channel Sets and Maximum Allowed EIRP Array to CPE

The BS shall send the channel sets to the new CPE.  The channel sets are described in Section 9.2.2.  The channel sets that are sent to the initializing CPE are the backup channels and the candidate channels.  The channel sets are sent in a DCD message, as described in Section 6.9.1 and in Tables 44 – 46.  The BS shall send DCD channel information elements 11 and 12.  Table 46 describes information element 12 as the backup and candidate channel list.  It is a prioritized list of the channels with the backup channel set higher in priority than the candidate channel set.  The two sets are identified by sending information element 11 which provides the number of the higher prioritized backup channel set.  Each channel in DCD information element 12 is characterized by both the channel number and the maximum allowed EIRP.

References:

# Text boxes

Notice: This document has been prepared to assist IEEE 802.22. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.22.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures

<http://standards.ieee.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <Carl R. Stevenson> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.22 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This document contains the proposed changes to Section 6.16.8 titled, “BS Transmit Channel Sets and Maximum EIRP Array to CPE” of Draft v1.0.