IEEE P802.22 Wireless RANs

| Minutes from PHY Conference Call Held on Aug 27, 2009 |
| --- |
| Date: 2009-08-28 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Zander Zhongding Lei | Institute for Infocomm Research, Singapore | 1 Fusionopolis Way #21-01 Connexis, Singapore 138632 | 65-6408-2436 | leizd@i2r.a-star.edu.sg |

## Agenda

### Attendance

### IEEE patent policy located at: http://standards.ieee.org/board/pat/pat-slideset.pdf

### Approval of Minutes of last call

### Agenda Approval

### Comments Review (might not review all due to time constraint)

ID: 830/859/864/867     		Jungsun

ID: 951             			Robert

ID: 952/971/973     		Stephen Kuffner

ID: 953                 		Steve Shellhammer

Redirected from MAC

ID: 322				Winston

ID: 330/332/338/342/353	Gerald

ID: 331/352/			Robert

ID: 343

### AOB

## Attendance

| Attendee | Affiliation | July 30 | Aug 6 | Aug 13 | Aug 20 | Aug 27 |
| --- | --- | --- | --- | --- | --- | --- |
| Sung Hyun Hwang | ETRI |  | x |  | x |  |
| Jung Sun Um | ETRI | x | x | x |  | x |
| Zander Zhongding Lei | I2R | x | x | x | x | x |
| Gerald Chouinard | CRC | x | x |  | x | x |
| Robert Wu | Wi-LAN |  |  | x | x | x |
| Jason Li | Wi-LAN |  |  | x |  | x |
| Vajira Samarasooriya | Wi-LAN |  |  | x |  | x |
| Wendong Hu | STM |  |  | x | x |  |
| Apurva Mody | BAE |  |  | x |  | x |
| Steve Kuffner | Motorola |  |  |  | x |  |
| Ivan Reede | Amerisys |  |  |  | x |  |

## Notes

- The meeting started at 9:00 pm and ended at 10: 40 pm ET

- All attendees were aware of the IEEE patent policy

- The minutes of last call on Aug 20 was approved.

- The agenda was approved.

Comments Review

PHY team reviewed and discussed 5 Technical comments the discussion/resolution was summarized below. More information may be found in the spreadsheet DCN09-120, updated regularly on Mentor.

- ID 830 (Jung Sun)	Withdrawn as it is addressed in ID 829

- ID 859 (Jung Sun)	Defer and action for John Benko to provide interleaver parameter for 			block size 836 for CBP transmission

- ID 864 (Jung Sun)	Pending for resolution in 867

- ID 867 (Jung Sun)	Defer with action for John Benko/Zander

Discussions: The comment pointed out that the block size given in Table 232 may not consider tail bits, i.e., assuming tailbiting for PSDU. However, the tail bits are used for PSDU as stated in the draft.

Jung Sun proposed to either modify the draft so that tailbiting is used for PSDU or provide consistent block size in table 232 (advanced coding schemes are using tailbiting. In simulations performed by Coding Tiger team also assumed tailbiting for PSDU)

Zander: Using tail bits initializing the encoder incurs some overhead compared to tailbiting, so tailbiting is used for the control signals which are usually short. Whereas for PSDU, the overhead might not be a big deal as it is usually long. It seems there is a trade-off here. To achieve same performance, the decoder in tailbiting may need a bit more complexity than that in using tail bits.

Action: Zander to contact John Benko to see the possibility of adding these new block sizes to match the 6 tail bits and see the relative increase in complexity if using tailbiting for PSDU.

- ID 951 (Robert)		Accepted with rephrased text agreed

Discussions: The comment suggested decoupling the requirement for carrier frequency and symbol clock frequency with separate sentences.

A good discussion was on clarification or definition of the requirement and effect to the implementation.

Robert agreed the requirement that maximum tolerance is 2% of the subcarrier spacing for each at the time being, feeling the number 2% might not be tight enough though.

## Next Call

Next meeting will be on 3rd Sept 09 (9pm ET).

# Text boxes

Notice: This document has been prepared to assist IEEE 802.22. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.22.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures

<http://standards.ieee.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <Wendong Hu> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.22 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This document contains the minutes from the PHY conference call on Aug. 28, 2009