IEEE P802.22
Wireless RANs

| Proposed Text of MAC technical items related to 7.14 Initialization and network association |
| --- |
| Date: 2013-11-13 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Keat Beng Toh | Hitachi Kokusai Electric Inc. | 32,Miyuki-cho,Kodaira-shi, Tokyo, 187-8511, Japan | +81-42-322-3111 | toh.keatbeng@h-kokusai.com |
| Keigo Hasegawa | Hitachi Kokusai Electric Inc. | 32,Miyuki-cho,Kodaira-shi, Tokyo, 187-8511, Japan | +81-42-322-3111 | hasegawa.keigo@h-kokusai.com |
| Masayuki Takekawa | Hitachi Kokusai Electric Inc. | 32,Miyuki-cho,Kodaira-shi, Tokyo, 187-8511, Japan | +81-42-322-3111 | takekawa.masayuki@h-kokusai.com |
| Kei Yanagisawa | Hitachi Kokusai Electric Inc. | 32,Miyuki-cho,Kodaira-shi, Tokyo, 187-8511, Japan | +81-42-322-3111 | yanagisawa.kei@h-kokusai.com |
| Seishi Sasaki | Hitachi Kokusai Electric Inc. | 32,Miyuki-cho,Kodaira-shi, Tokyo, 187-8511, Japan | +81-42-322-3111 | sasaki.seishi@h-kokusai.com |
| Masahiro Asano | Hitachi Kokusai Electric Inc. | 32,Miyuki-cho,Kodaira-shi, Tokyo, 187-8511, Japan | +81-42-322-3111 | asano.masahiro@h-kokusai.com |

Summary of this document

In this document, Initialization and network association for IEEE 802.22b is proposed to support multi-channel operation which provide higher data throughput than the IEEE Std. 802.22-2011.The subclause structure in the proposed text is shown as follows.

7.14.1 BS Initialization

7.14.2 CPE Initilaization

In this proposal, all the texts are described as revision texts to the 802.22 standard.

7.14.1 BS Initialization

The WRAN BS initialization procedure shall consist of the following steps:

- BS is professionally installed.

- BS acquires the antenna gain information

- Determine the BS geographic location.

- If a database service exists for BS area of service, Spectrum Manager at the BS receives an initial list of available channels from the database service. If there is no database service, Spectrum Manager initially considers all channels available.

- Operator disallows channels on the available channel list as needed.

- Perform incumbent detection in all usable channels and synchronize network to neighboring BSs.

- Presentation of the available channel list to the higher layers for selection of an operating channel or operating channels.

- Commence single channel operation or multi-channel operation on the selected operating channel(s).

This BS initialization procedure is depicted in Figure 3X.

Figure 32 — BS initialization procedure

Subclauses 7.14.1.1 to 7.14.1.6 are remains the same as described in the IEEE 802.22-2011 standard.

7.14.1.7 Present the Available Channel List to the Higher Layers

After incumbent detection during which channels may have been identified as protected or occupied, the resulting list shall be presented to the higher layers using an M-AVAIL-TV-CH-REPORT primitive with the mode set equal to 2 for selection of and operating channel or using an M-AVAIL-TV-CH-REPORT primitive with the mode set equal to 3 for selection of operating channels.  The required information presented shall be each channel number that is available for the BS to commence WRAN service and the maximum allowed EIRP for each channel.  Additional information can be provided to the higher layers to help with the selection of an optimal channel or optimal channels, such as a list of channels where other wireless services were detected during the incumbent detection stage.  As a result of the selection from the higher layer, the SM shall receive an M-OPERATING-TV-CH or M-OPERATING-TV-CHS primitive from the NCMS.

7.14.1.8 Commence Single channel Operation or Multi-channel Operation

The BS may now commence single channel operation on any one channel listed on the available channel list or multi-channel operation on any channel listed on the available channel list.

7.14.2 CPE Initialization

The procedure carried out by the BS and the CPE to perform CPE network entry and initialization shall be as follows:

- CPE performs self test.

- CPE acquires the antenna gain information

- CPE senses for and synchronizes to WRAN services.  The sensing thread also begins during this step to detect broadcasting incumbents.

- CPE presents sensing results to the higher layers.

- CPE chooses a WRAN service for single channel operation or multiple WRAN services for multi-channel operation.

- CPE acquires valid geolocation data from the satellites.  If the data acquisition is unsuccessful, CPE initialization shall not continue.

- CPE acquires the downstream and upstream parameters from the selected WRAN service.

- CPE directional antenna azimuth adjustment.

- If channels N and N±1 pass the sensing and timing requirements, BS and CPE perform initial ranging (see 749H7.15.2.1).

- CPE transmits basic capabilities.

- If all required basic capabilities are present in the CPE, the AAA authenticates the CPE and key exchange is performed; otherwise, the CPE does not proceed to registration and the BS de-registers the CPE.

- Perform Registration (REG-REQ/RSP). Registration entails the following:

  - Exchange and verification of CPE NMEA string

  - Configuration of CPE operational parameters including configuration of IP version to be used by the CPE.

- Upon completing registration, BS transmits channel sets to CPE.

- Establish IP connectivity.

- Establish time of day.

- Transfer operational parameters.

- Establish dynamic service flows.

- CPE reports sensing results and discovered neighboring networks.

Figure 34 summarizes the network entry of the CPE and its initialization procedure. Note that these steps taken by the CPE consist of a set of actions and error verification. In the following subclauses, we provide a more detailed description of these steps and their individual responsibilities.

— CPE initialization procedure

Subclauses 7.14.2.1 to 7.14.2.4 are remains the same as described in the IEEE 802.22-2011 standard.

7.14.2.5 CPE Chooses a WRAN Service for single channel operation or multiple WRAN services for multi-channel operation

A WRAN service is selected at the higher layers of the CPE after preliminary sensing and identification of available BSs and the presence of incumbents in the area as the above subclauses describe.  The CPE SSA shall issue an M-WRAN-SERVICE-REPORT primitive to request the higher layers through the NCMS to select a channel from the available WRAN service list that is included in the primitive, as described in 10.7.3.1.  The SSA shall receive an M-WRAN-SERVICE-RESPONSE primitive with the selected channel from the NCMS, as described in 10.7.3.3.  Once the channel is selected, it and its adjacent channels are more rigorously sensed in order to detect the presence of a weak incumbent service that might be masked by the selected WRAN service.  This procedure is described in more detail in 10.3.2.

Multiple WRAN services are selected at the higher layers of the CPE after preliminary sensing and identification of available BSs and the presence of incumbents in the area as the above subclauses describe.  The CPE SSA shall issue an M-WRAN-SERVICE-REPORT primitive to request the higher layers through the NCMS to select channels from the available WRAN service list that is included in the primitive, as described in 10.7.3.1.  The SSA shall receive an M-WRAN-SERVICES-RESPONSE primitive with the selected channels from the NCMS, as described in 10.7.3.4.  Once the channels are selected, it and its adjacent channels are more rigorously sensed in order to detect the presence of a weak incumbent service that might be masked by the selected WRAN service.  This procedure is described in more detail in 10.3.2.

Subclauses 7.14.2.6 to 7.14.2.17 are remains the same as described in the IEEE 802.22-2011 standard.

# Text boxes

Abstract

This document contains the proposed text of MAC technical items related to Initialization and network association.

Notice: This document has been prepared to assist IEEE 802.22. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.22.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures

<http://standards.ieee.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair Apurva N. Mody <apurva.mody@ieee.org> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.22 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

No

Yes

Professional

installation

Determine

Geographic Location

Incumbent

Database exists for BS

area of service

?

Spectrum Manager builds an initial

list of available TV channels using

inputs from the geolocator

&

the

incumbent databases

Spectrum Manager

initially considers all

channels available

Operator disallows channels

on the available TV channel

list from usage as needed

Perform Incumbent Detection

in all usable TV channels and

Synchronize Network to

Neighboring BSs

Present the available TV

channel list to the Higher

Layers for Selection of an

Operating Channel or

Commence single channel

operation or multi-channel

TV channels

Acquire BS antenna

gain information

BS not

operational

Operating Channels

operation on the selected

Perform key exchange

Yes

BS transmits channel sets to CPE

No

Establish IP connectivity

CPE

operational

CPE initial turn

-

on

CPE self test

Initial sweep of TV Channels to

discover WRAN services

,

synchronize with WRAN

,

and

start sensing thread

Presentation of

WRAN services

advertising

,

RSSI levels

,

and

sensing results to higher layer

Selection of WRAN service or WRAN

services by installer or by local routine

Do channels N

,

N

+/

-

1

pass sensing criteria

?

WRAN antenna azimuth

adjustment

if needed

Yes

No

Valid NMEA

string at the BS Spectrum

Manager

?

Yes

CPE loca

l

Configuration

allowed

?

No

Registration

-

Transmit encrypted CPE NMEA string

-

Negotiate IP version

-

Configure CPE operational parameters

Acquire downstream and

upstream parameters

AAA

authorizes the CPE

?

Yes

No

Log authentication

denial and remove

BS from immediate

consideration

Perform initial ranging process

No

Yes

Is satellite geolocation

acquired

?

Yes

Transmit basic capabilities

Report sensing results and

discovered neighboring networks

Establish time of day

Transfer operational parameters

Establish dynamic service flows

CPE

initialization

failed

Acquire CPE antenna gain

information

for single or multi-channel operation