## Slide 1: Comment Resolution related to MAC
IEEE P802.22 Wireless RANs Date: 2014-2-12
Authors:
Notice: This document has been prepared to assist IEEE 802.22. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.22.
Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures
<http://standards.ieee.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard." Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication. Please notify the Chair Apurva Mody <apurva.mody@ieee.org> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.22 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

## Slide 2: Comment Resolution related to MAC Frame (CID 87)
87 | "If indicated, the Bandwidth Request subheader … the Generic MAC header" If both Bandwidth request subheader and Extended bandwidth request subheader appear at the same time, how to know which is first or later. | Add the following rule. "the Generic MAC header, the Bandwidth Request subheader shall come first."
ID | Comment | Suggested Remedy
Proposed Resolution
: Accept in principle.
Subheader format is modified as described in 22-13-0182-00

## Slide 3: Comment Resolution related to MAC Frame (CID 215)
215 | There may be a problem with the way the ranging/BW request/UCS notification control region is depicted in the Figure B1 (and all other frame structure figures for that matter). According to step 2 in section 9.6.4 on page 327 of IEEE Std 802.22-2011, the indices that correspond to the control region span from {-840 -830 -820 ... -10 10 ... 820 830 840}. This seems to indicate that subchannels allocated for the US control region actually cover subchannels at both the upper and lower band-edges of the channel. | If the intention is to properly depict where the time frequency resource allocated to the control region in these frame structure diagrams, then update the frame structure diagrams (starting with B1) to indicate a portion of the US control region at each band edge.
ID | Comment | Suggested Remedy
Proposed Resolution
: Reject
Modification of figure makes a confusion, then the figure keeps as it is.

## Slide 4: Comment Resolution related to MAC Frame (CID 216)
216 | Here the OFDM slot is defined as 4 symbols by 1 subchannel. If a slot is constructed this way, it breaks compatibility with legacy CPEs. Future deployments may have to consider legacy/1st generation CPEs connecting to R-CPEs or MR-BS directly. MAPs/MAP IEs define allocations in terms of slots. A legacy CPE will not be able to process MAPs issued by a R-CPE or MR-BS | Use original definition of OFDM slot to ensure compatiblity with base std IEEE 802.22-2011.
ID | Comment | Suggested Remedy
802.22b Draft defines two modes of PHY such as Mode 1 and Mode 2. Mode 1 is fully compatible with IEEE Std. 802.22-2011, then 802.22b Draft is still compatible with IEEE Std. 802.22-2011 on PHY mode 1. Also, the legacy CPE can communicate R-CPE or MR-BS on PHY Mode 1.
Proposed Resolution
: Reject

## Slide 5: Comment Resolution related to MAC Frame (CID 217)
217 | Much of the text in 7.4a3 on pg 18-19, through top of page 20, is almost verbatim copied from the corresponding sections in the base Std. | Only provide text modifications (additions/deletions/modifications) being made on top of the corresponding text in this section from the base standard. If there is text that is not being modified, it is not required to be included in the amendment (as per the IEEE 802 Style Guide)
ID | Comment | Suggested Remedy
A lot of text on 802.22b Draft are copied from IEEE Std. 802.22-2011, but the copied text is help to understand the new operations of PHY mode 2 which is a new PHY for 802.22b.
Proposed Resolution
: Reject

## Slide 6: Comment Resolution related to MAC Frame (CID 220)
220 | There may be a couple of issues with regard to definition of the extended BR subheader: 1) Inclusion of each CPE's MAC address is not necessary and will introduce too much overhead. 2) A "Directions" field is not needed. The BR function is for the purpose of requesting US bandwidth. DS bandwidth, in the case of a centralized R-CPE, is granted in DS-MAP IEs in the DS relay/access zones. 3) Indication of the FID is not necessary, as we are granting bandwidth to the CPE/station ID itself | Remove reference to CPE MAC ADDRESS, remove indication of request for DS allocation, remove indication of specific FID.
ID | Comment | Suggested Remedy
Proposed Resolution
: Accept

## Slide 7: Comment Resolution related to MAC Frame (CID 227)
227 | In Table 31 we have distinct UCD Ies for the BR opportunity and UCS Notification opportunity size for the US DRZ. If a Distributed R-CPE is transmitting its own MAPs and configuration descriptor messages, wouldn't the R-CPE use the same Ies for theses fucntions as the MR-BS? | Remove specificate of DRZ Bandwidth Request Opportunity Size, and DRZ UCS Notification Opportunity Size form Table 31. Updates entries for Bandwidth Request Opportunity Size and UCS Notification Opportunity Size in Table 31 to include reference that these UCD IEs can be used by Distributed R-CPE transmitting in US DRZ
ID | Comment | Suggested Remedy
Proposed Resolution
: Accept

## Slide 8: Comment Resolution related to MAC Frame (CID 228)
228 | See previous comments regarding managing of DIUCs/UIUCs. 1 byte here is not sufficient to specifiy the all the modes a R-CPE supports. | This field needs to be an array of values or a bitmap of some kind. This is a problem that exists in the base standard and needs to be corrected. Make appropriate specification of CPE Modulator in 7.7.11.3.2.2.4
ID | Comment | Suggested Remedy
Proposed Resolution
: Accept
In order to indicate the capability of modulation and coding, 8 bits bitmap for modulations and 8 bits bitmap for coding rates are extended from 8 bits.

## Slide 9: Bitmap Usage for Modulation and Coding Rates
b8 | b7 | b6 | b5 | b4 | b3 | b2 | b1
Reserved | Reserved | Reserved | Reserved | MD-TCM | 256QAM | 64QAM | 16QAM
Supported Modulation
  BPSK and QPSK shall be implemented
Supported Coding Rate
  1/2 shall be implemented
b8 | b7 | b6 | b5 | b4 | b3 | b2 | b1
Reserved | Reserved | 14/15 for MD-TCM | 10/11 for MD-TCM | 7/8 for 256QAM | 5/6 | 3/4 | 2/3

## Slide 10: Comment Resolution related to MAC Frame (CID 229)
229 | Can't R-CPEs request bandwidth from MR-BS and transmit MAC management messages to the MR-BS directly? What added funcitonality does the Container Message provided | If there is not added functionality provide with this message that can't be accomplished with messaging scheme, then it's suggested this section be removed.
ID | Comment | Suggested Remedy
R-CPE can send request messages to MR-BS.
In particular, a container message contains more than one requests (Bandwidth request, basic capability request, registration request) or other messages received from S-CPEs, and R-CPE sends the container message grouped by messages to BS that may reduce the overhead to transmit an individual message.
Proposed Resolution
: Reject

## Slide 11: Comment Resolution related to MAC Frame (CID 231)
231 | There is no description here as to what modifications/updates are needed to security sublayer, if needed to support new R-CPEs | Provided description and technical required for security sublayer concerning R-CPEs and MR-BS operation.
ID | Comment | Suggested Remedy
Proposed Resolution
: Reject since no extension of security layer is needed.