IEEE 802.24 Smart Grid TAG
July 2013 working document

---
ITU-R (18-13-0085-00)
- Rolfe and Kunal to fill out 6.1 for frequencies.
- First mile will be edited on Tuesday
- Middle mile edits on Tuesday
- Mody will review questions 7 and 8 and bring changes to the group on Wednesday. Mention 802.3 in these two questions.

---
Section 6
- Start with architectural diagram.
- Replace 6.2-6.4 with later slides

---
More introduction
- There are overlapping areas of applicability of wireless and wired standards.
- Wireless is an important part of the Smart Grid Management system because:
  - Supports communications during power failures, particularly damaged transmission paths.
  - Provides independent infrastructure for communications.
  - Not practical to provide physical connection to some endpoints.
  - Easy and low cost network deployment and configuration for a large number of terminals
  - Can provide greater reliability through redundant paths, e.g. provision multiple radios, and fast reconfiguration.

---
New figure to be provided by Gillmore

---
Replacement for 6.2, 6.3 and 6.4
- There are multiple wireless standards that can provide solutions for first mile, middle mile and backhaul. The appropriate standard depends on the application and deployment scenario. In some instances, wired options can be used for some of the links in the network. The IEEE 802 LMSC has prepared a package of standards that lists IEEE 802 standards appropriate for use in Power Grid Management Systems.

---
Replacement for 6.2, 6.3 and 6.4 (cont)
- Characteristics
  - Wireless link data rates
    - First and middle mile: from 2.4 kb/s to 2 Mb/s, depending on the application
    - Backhaul from 50 kb/s to 100 Mb/s, depending on the application. Lower rates for long range coverage in sparse areas. Higher data rates are used in dense environment.
  - Bandwidths: As required for the modulation, but typically 0.5 to 5 bits/s/Hz
  - Transmit power levels: Most applications are range limited due to regulations
    - First and middle mile: Typically near the regulatory limits. However, in dense urban environments, the links may be interference limited.
    - Backhaul: For licensed spectrum power levels are typically higher.
  - Spectrum: Multiple available channels improve the reliability of the wireless networks. The frequency of the spectrum allocation is important because it is an outdoor application that benefits from the propagation characteristics in lower frequency bands.
  - Topology: mesh, point-to-point, point-to-multipoint

---
Possible picture needs work.
Server
Backhaul
WAN
Gateway
Gateway
Distribution
HAN
FAN
Tim Godfrey will work on the picture Ramasastry to provide chart based on earlier presentation

---
Backhaul
- Data rates, bandwidths, and spectrum requirements needed to support the needs of power grid management systems
  - Wireless link data rates: from 50 kb/s to 100 Mb/s, depending on the application. Lower rates for long range coverage in sparse areas. Higher data rates are used in dense environment.
  - Bandwidths: As required for the modulation, but typically from 0.5 to 5 bits/s/Hz
  - Transmit power levels: Typically near the regulatory limits. Most applications are range limited due to regulations. For licensed spectrum power levels are typically higher.
  - Spectrum: Multiple available channels improve the reliability of the wireless networks. The frequency of the spectrum allocation is important because it is an outdoor application that benefits from the propagation characteristics in lower frequency bands.
  - Topology: point-to-point, point-to-multipoint, mesh

---
Whitepaper notes
- Discusses IEEE 802 technologies only.
- Outline
  - Introduction, value and history of 802
  - Reference package of standards
  - Subsection for each applications, input from each group.
  - Conclusions and pretty pictures
- Build on Greencomm paper as basis?

---
Tasks
- Develop list of application (not exhaustive)
  - AMI/AMR (802.15.4, 802.11, backhaul: 802.16, 802.3, 802.22 [metro Ethernet?])
  - Demand response ( 802.15.4, 802.11, backhaul: 802.16, 802.3, 802.22 [metro Ethernet?])
  - Distribution automation (same as above)
  - Protection/substation control 802.3,
  - Outage restoration management
  - Load control
- Delegate rough cut to Gillmore