## Slide 1
IEEE 802 Scope of OmniRAN |  |  | 
Date: 2013-05-13 |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Max Riegel | NSN | +49 173 293 8240 | maximilian.riegel@nsn.com
Notice: This document does not represent the agreed view of the OmniRAN EC SG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
Access networks comprise functions which extend beyond the scope of IEEE 802.
The contribution provides different architectural views on access networks to define the functional pieces of access networks which fall into the scope of IEEE 802.

## Slide 2: IEEE 802 Scope of OmniRAN
Architectural models and functional views of OmniRAN in the scope of IEEE 802

## Slide 3: Motivation
IEEE 802 Scope of OmniRAN

## Slide 4: How and where does OmniRAN fit? (Informative figure IEEE 802-2001)
OmniRAN comprises the functions of access networks based on IEEE 802 technologies
As IEEE 802 access networks consist of the cooperation of multiple instances of IEEE 802 technologies with a single higher layer control and traffic forwarding function, there is no obvious place for OmniRAN in the IEEE 802-2001 informative figure.
  Like for other IEEE 802 standards, e.g. IEEE 802.21, IEEE 802.1X, …

## Slide 5: Really helpful to describe and define OmniRAN scope within IEEE 802?
The amended figure 5 of 802rev-D1.6 puts OmniRAN into a single box of the higher layer end-point stack aside of the data path
  discussed in the Mar ‘13 Orlando session
The figure may not be completely wrong, however it provides not much guidance of functional pieces in scope of OmniRAN and relation to IP based protocols
OmniRAN
R2, R3 R4

## Slide 6: ACCESS NETWORK ArchitecturAL VIEWS
IEEE 802 Scope of OmniRAN

## Slide 7: OmniRAN Architecture Partitioning for dynamic attachment of terminals to networks
Communication networks supporting dynamic attachment of terminals are usually structured into
  Access Network
    Distributed infrastructure for aggregation of multiple network access interfaces into a common interface
  Core Network
    Infrastructure for control and management of network access and end-to-end IP connectivity
  Services
    Infrastructure for providing services on top of established IP connectivity
Internet
Terminal
Access Network
Services
Core Network

## Slide 8: Functions for establishment of end-to-end Connectivity
Access Network
Network advertisement
IEEE 802.xx PHY and MAC
Authentication, authorization and accounting client
L2 session establishment
  w/ QoS and Policy Enforcement
L2 mobility management inside and across access networks
Mobility Gateway
Traffic forwarding to core based on L2 addresses
Core Network
Authentication, authorization and accounting server
IP address management
Policy & QoS management based on a SLA
Mobility among multiple access networks
IP connectivity establishment to Internet and services
Roaming via other core networks

## Slide 9: Access Network Architectual Views
Medium
Medium
Data Link
Physical
Network
Transport
Application
Data Link
Physical
Access Network
Terminal
Data Link
Physical
Data Link
Physical
Network
Transport
Application
Network
Network
Medium
Medium
Core
Service
Data Link
Physical
Data Link
Physical
Data Link
Physical
Data Link
Physical
R2
R1
R3
R5
Scanning
Network Selection
Association
Authentication
Host Configuration
Application
Layered Protocol View
Procedural View
Topology View

## Slide 10: Topology View on OmniRAN Architecture and Reference Points
Access
Core
Internet
R1
R3
R4
Access
Core
Internet
R3
R5
Terminal
R3
Authentication
Authorization
Accounting
Location
CoA
Mobility
Encapsulation
Authentication
Authorization
Accounting
Location
CoA
Mobility
Encapsulation
DataPath
Access
Core
Transport
Reference Points represent a bundle of protocols between peer entities
  - Similar to real network interfaces
R2
Access
R3

## Slide 11: OmniRAN Reference Points
R1: Access link, technology specific
R2: User & terminal authentication, subscription & terminal management
R3: Authorization, service management, user data connection, mobility support, accounting, location
R4: Inter-access network coordination and cooperation, fast inter-technology handover
R5: Inter-operator roaming control interface
All reference points may comprise a number of different protocols. However, only the protocols related to required functionality have to be present on the reference point.

## Slide 12: Access Network Protocol Layer Model
Current scope of IEEE 802
Terminal
Access Network
Core Network
Medium
Medium
Medium
IEEE 802 is dealing with communication functions in the Data Link and Physical layers.
More fine-grain layering models are used by IEEE 802 to describe the architecture of its work.
Data Link
Physical
Network
Transport
Application
Data Link
Physical
Network
Transport
Application
Data Link
Physical
Data Link
Physical
Data Link
Physical
Data Link
Physical

## Slide 13: IEEE 802 Architecture
IEEE 802 Scope of OmniRAN

## Slide 14: IEEE 802 Reference Model for End-Stations (802rev-D1.6)
Reference Model within the 7 layer ISO-OSI model
IEEE 802 provides link layer connectivity to the overall communication architecture
It covers the Physical and the Data link layer of the ISO-OSI 7 layer model
Data link layer is represented in IEEE 802 by MAC and LLC sub-layers
Functionality above Data link layer is considered as ‘higher layer’.
Reference Model exposing specific IEEE 802 functions
The IEEE 802 connectivity stack is supplemented by a management plane and a plane representing IEEE 802.21 MIH.
MIH comprises a number of control SAPs into each of the layer of the IEEE 802 reference model
The network management model of IEEE 802 is aligned with the ITU TMN framework and provides the definition of managed objects for each of the layers of the IEEE 802 architecture
IEEE 802 allows for special purpose network management protocols when the usual network management approach with managed objects is not sufficient.

## Slide 15: IEEE 802 Reference Model for Bridges
IEEE 802 provides a bridging model for interconnection of multiple network segments based on data link layer functionality
Different bridging protocols can handle the issues of various topologies including avoidance of data loops and establishment of ‘optimized’ filtering and forwarding decisions.
Bridging protocols have been extended to cope with multiple operational domains of an hierarchical provider structure.

## Slide 16: OmniRAN Architecture WITHIN SCOPE of IEEE 802
IEEE 802 Scope of OmniRAN

## Slide 17: Mapping of OmniRAN Reference Points to IEEE 802 Reference Model
Current scope of IEEE 802
Medium
Medium
Medium
R1, R2, R3 Reference Points can be easily mapped into IEEE 802 Reference Model
  However IP based protocols to carry control information elements are out of scope of IEEE 802
  ‘R3 Data’ may define a special kind of Data Link SAP
  ‘R2’ and ‘R3 Control’ may comprise only definitions of attributes
Data Link
Physical
Higher Layers
Data Link
Physical
Data Link
Physical
Data Link
Physical
Data Link
Physical
Data Link
Physical
Higher Layers Control
Higher Layers Control
Higher Layers
R3 Data
R3 Control
R2/R3 Control
R1
R1

## Slide 18: Conclusion
IEEE 802 Scope of OmniRAN

## Slide 19: Conclusion
OmniRAN Reference Points can be mapped into the IEEE 802 Reference Model
  R1 is completely covered by IEEE 802 specifications
  R2 and R3 are related to attributes for control of IEEE 802 functions and the definition of a DL SAP for the transport of user payload
  R4 is not considered by this contribution
    IEEE 802.21 may provide the solution for this OmniRAN reference point?
  R5 may be completely out of scope of IEEE 802
    However attributes of R3 may be copied over to R5
IP protocols used for OmniRAN are out of scope of IEEE 802
OmniRAN Specification in the scope of IEEE 802 would consist of
  an normative part defining control attributes and a DL SAP for the user payload
  an informative part outlining the overall architecture
  an informative part proposing the usage of particular IP protocols and the mapping of the IEEE 802 attributes into the IP protocols.
BTW: Approach seems to capture well the proposals on SDN