## Slide 1
IEEE 802 Scope of OmniRAN |  |  | 
Date: 2013-05-13 |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Max Riegel | NSN | +49 173 293 8240 | maximilian.riegel@nsn.com
Notice: This document does not represent the agreed view of the OmniRAN EC SG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
Access networks comprise functions which extend beyond the scope of IEEE 802.
The contribution provides different architectural views on access networks to define the functional pieces of access networks which fall into the scope of IEEE 802.

## Slide 2: IEEE 802 Scope of OmniRAN
Architectural models and functional views of OmniRAN in the scope of IEEE 802

## Slide 3: Motivation
IEEE 802 Scope of OmniRAN

## Slide 4: How and where does OmniRAN fit? (Informative figure IEEE 802-2001)
OmniRAN comprises the functions of access networks based on IEEE 802 technologies
As IEEE 802 access networks consist of the cooperation of multiple instances of IEEE 802 technologies with a single higher layer control and traffic forwarding function, there is no obvious place for OmniRAN in the IEEE 802-2001 informative figure.
  Like for other IEEE 802 standards, e.g. IEEE 802.21, IEEE 802.1X, …

## Slide 5: Really helpful to describe and define OmniRAN scope within IEEE 802?
The amended figure 5 of 802rev-D1.6 puts OmniRAN into a single box of the higher layer end-point stack aside of the data path
  discussed in the Mar ‘13 Orlando session
The figure may not be completely wrong, however it provides not much guidance on which functional pieces are in scope of OmniRAN and their relation to IP based protocols.
OmniRAN
R2, R3 R4

## Slide 6: ACCESS NETWORK ArchitecturAL VIEWS
IEEE 802 Scope of OmniRAN

## Slide 7: OmniRAN architecture partitioning for dynamic attachment of terminals to networks
Communication networks supporting dynamic attachment of terminals are usually structured into
  Access Network
    Distributed infrastructure for aggregation of multiple network access interfaces into a common interface
  Core Network
    Infrastructure for control and management of network access and end-to-end IP connectivity
  Services
    Infrastructure for providing services on top of established IP connectivity
Internet
Terminal
Access Network
Services
Core Network

## Slide 8: Functions for establishment of end-to-end Connectivity
Access Network
Network advertisement
Pre-association signalling
IEEE 802.xx PHY and MAC
Authentication, authorization and accounting client
L2 session establishment
  w/ QoS and Policy Enforcement
L2 mobility management inside and across access networks
Mobility Gateway
Traffic forwarding to core based on L2 addresses
Core Network
Authentication, authorization and accounting server
IP address management
Policy & QoS management based on a SLA
Mobility among multiple access networks
IP connectivity establishment to Internet and services
Roaming via other core networks

## Slide 9: Access Network Architectual Views
Medium
Medium
Data Link
Physical
Network
Transport
Application
Data Link
Physical
Access Network
Terminal
Data Link
Physical
Data Link
Physical
Network
Transport
Application
Network
Network
Medium
Medium
Core
Service
Data Link
Physical
Data Link
Physical
Data Link
Physical
Data Link
Physical
R2
R1
R3
R5
Scanning
Network Selection
Association
Authentication
Host Configuration
Application
Layered Protocol View
Procedural View
Topology View

## Slide 10: Topology view on OmniRAN architecture and reference points
Access
Core
Internet
R1
R3
R4
Access
Core
Internet
R3
R5
Terminal
R3
Authentication
Authorization
Accounting
Location
CoA
Mobility
Encapsulation
Authentication
Authorization
Accounting
Location
CoA
Mobility
Encapsulation
DataPath
Access
Core
Transport
Reference Points represent a bundle of protocols between peer entities
  - Similar to real network interfaces
R2
Access
R3

## Slide 11: The benefits of the topology view: Reference points
Reference points denote the interconnections between functional entities in the access network, e.g.
  R1 between terminal and base station:
    Access link, technology specific
  R2 between terminal and core network:
    User & terminal authentication, subscription & terminal management
  R3 between access network and core network:
    Authorization, service management, user data connection, mobility support, accounting, location
  R4 between access networks:
    Inter-access network coordination and cooperation, fast inter-technology handover
  R5 between core networks:
    Inter-operator roaming control interface
Reference points build an excellent foundation for realizing interoperability between real world network equipment.
However reference points usually do not reflect nor match the scope of IEEE 802.

## Slide 12: Procedural view on OmniRAN
Accounting
Disassociation
Host Configuration
Application
Policy Control
Application
Host Config Release
Accounting
Authentication
Authorization
Association
Network Selection
Scanning
AAA
DHCP
Application
ANQP
L2 Protocol
L2 Attributes
L3+ Protocol
L2 Attributes
L3+ Protocol
L3+ Attributes
Legend:
L2 Protocol
L3+ Attributes

## Slide 13: The benefit of the procedural view: Getting insights into protocols
Scanning: Finding out about the existence of potential communication peers
  Scope of individual IEEE 802.xx specifications
Network selection: Finding the most appropriate network access
  IEEE 802.xx protocol for higher layer information
Association: Setting up the access link
  Scope of individual IEEE 802.xx specifications
Authentication
  Security framework, based on IEEE 802.1X
Authorization: Setting up the IEEE 802 communication link
  Attributes and functions depending on particular IEEE 802.xx technologies
Accounting: Usage and inventory reporting
  Attributes depending on particular IEEE 802.xx technologies
Policy Control: Adjustment of the user data connection
  Attributes depending on particular IEEE 802.xx technologies
Host Configuration: Getting the IP communication parameters
  IP protocol for IP configuration parameters
Application: Making productive use of the communication infrastructure
  IP protocol for application parameters
Host Config Release: Releasing the IP communication parameters
  IP protocol for IP configuration parameters
Disassociation: Releasing the access link
  Scope of individual IEEE 802.xx specifications

## Slide 14: The benefit of the layered protocol view: Detailed representation of the data path
Current scope of IEEE 802
Medium
Medium
Medium
IEEE 802 is dealing with packet transport functions in the Data Link and Physical layers.
More fine-grain layering models are used by IEEE 802 to describe the architecture of its work.
Data Link
Physical
Network
Transport
Application
Data Link
Physical
Network
Transport
Application
Data Link
Physical
Data Link
Physical
Data Link
Physical
Data Link
Physical
Access Network
Terminal
Core

## Slide 15: IEEE 802 Architecture
IEEE 802 Scope of OmniRAN

## Slide 16: IEEE 802 Reference Model for End-Stations (802rev-D1.6)
Reference Model within the 7 layer ISO-OSI model
IEEE 802 provides link layer connectivity to the overall communication architecture
It covers the Physical and the Data link layer of the ISO-OSI 7 layer model
Data link layer is represented in IEEE 802 by MAC and LLC sub-layers
Functionality above Data link layer is considered as ‘higher layer’.
Reference Model exposing specific IEEE 802 functions
The IEEE 802 connectivity stack is supplemented by a management plane and a plane representing IEEE 802.21 MIH.
MIH comprises a number of control SAPs into each of the layer of the IEEE 802 reference model
The network management model of IEEE 802 is aligned with the ITU TMN framework and provides the definition of managed objects for each of the layers of the IEEE 802 architecture
IEEE 802 allows for special purpose network management protocols when the usual network management approach with managed objects is not sufficient.

## Slide 17: IEEE 802 Reference Model for Bridges
IEEE 802 provides a bridging model for interconnection of multiple network segments based on data link layer functionality
Different bridging protocols can handle the issues of various topologies including avoidance of data loops and establishment of ‘optimized’ filtering and forwarding decisions.
Bridging protocols have been extended to cope with multiple operational domains of an hierarchical provider structure.

## Slide 18: OmniRAN Architecture WITHIN SCOPE of IEEE 802
IEEE 802 Scope of OmniRAN

## Slide 19: OmniRAN Reference Points in the layered protocol view
Current scope of IEEE 802
Medium
Medium
Medium
OmniRAN reference points describe interfaces into IEEE 802 network functions.
  Most of the Reference Points mainly comprise signaling information.
Signaling information configures functionalities in the PHY and DataLink layer of IEEE 802 functions.
The signaling information is carried by IP protocols from a central database server to the IEEE 802 functions
  Similar to the definition and processing of network management information in IEEE 802
Effectively each of IEEE 802 network elements contains an IP communication stack on top of the IEEE 802 data path for the exchange of the control information.
Data Link
Physical
Network
Transport
Application
Data Link
Physical
Network
Transport
Application
Data Link
Physical
Data Link
Physical
Data Link
Physical
Data Link
Physical
Network
Transport
Application
Network
Transport
Application

## Slide 20: Mapping of OmniRAN Reference Points to IEEE 802 Reference Model
Current scope of IEEE 802
Medium
Medium
Medium
R1, R2, R3 Reference Points can be mapped onto the IEEE 802 Reference Model
  R1 represents the PHY and MAC layer functions between terminal and base station
    Completely covered by IEEE 802 specifications
  R2 represents the L2 control protocol functions between terminal and central entities for control and AAA.
  R3 represents the L1 & L2 control interface from a central control entity into the network elements
  ‘R2’ and ‘R3 Control’ may comprise only definitions of attributes
    However IP based protocols to carry control information elements are out of scope of IEEE 802
  ‘R3 Data’ may define a special kind of Data Link SAP
Data Link
Physical
Higher Layers
Data Link
Physical
Data Link
Physical
Data Link
Physical
Data Link
Physical
Data Link
Physical
Higher Layers Control
Higher Layers Control
Higher Layers
R3 Data
R3 Control
R2/R3 Control
R1

## Slide 21: Further considerations
Key issue is the handling of IEEE 802 specific attributes of IP protocols within the activities of IEEE P802
IEEE P802 has an established routine for defining the MIBs of IEEE 802 technologies
  Partly done by itself and partly within the IETF
Processes for defining other IEEE 802 related attributes in IETF vary depending of protocol
  e.g. AAA attributes are mainly done by IETF with some informal review by IEEE 802 WGs
Cooperation between IEEE 802 and IETF is currently reviewed and refined in [draft-iab-rfc4441rev-04.txt]
  More details on next slide.

## Slide 22: [draft-iab-rfc4441rev-04.txt] Appendix A. Current examples of IEEE 802 and IETF Work Item Collaboration
A.1. MIB Review
Historically the MIB modules for IEEE 802.1 and IEEE 802.3 were
developed in the IETF Bridge MIB and Hub MIB Working Groups
respectively. With travel budgets under pressure, it has become
increasingly difficult for companies to fund employees to attend both
IEEE 802 and IETF meetings. As a result, an alternative was found to
past arrangements that involved chartering MIB work items within an
IETF WG by transferring the work to IEEE 802 with expert support for
MIB review from the IETF. In order to encourage wider review of MIBs
developed by IEEE 802 WGs, it is recommended that MIB modules
developed in IEEE 802 follow the MIB guidelines [RFC4181]. An IEEE
802 group may request assignment of a 'MIB Doctor' to assist in a MIB
review by contacting the IETF Operations and Management Area
Director.
By standardizing IEEE 802 MIBs only within IEEE 802 while utilizing
the SNMP quality control process, the IETF and IEEE 802 seek to
ensure quality while decreasing overhead. The process of transfer of
the MIB work from the IETF Bridge MIB WG to IEEE 802.1 WG is
documented in [RFC4663].

## Slide 23: [draft-iab-rfc4441rev-04.txt] Appendix A. Current examples of IEEE 802 and IETF Work Item Collaboration
A.2. AAA Review
IEEE 802 WGs requiring new AAA applications should send a liaison
request to the IETF. Where merely new attributes definitions are
sufficient rather than defining a new authentication, authorization
and accounting logic/procedures, an Internet-Draft can be submitted
and review can be requested from AAA-related WGs such as the RADEXT
or DIME WGs. For attributes of general utility, and particularly
those useful in multiple potential applications, allocation from the
IETF standard attribute space is preferred to creation of IEEE 802
Vendor-Specific Attributes (VSAs). As noted in [RFC3575]: "RADIUS
defines a mechanism for Vendor-Specific extensions and the use of
that should be encouraged instead of allocation of global attribute
types, for functions specific only to one vendor's implementation of
RADIUS, where no interoperability is deemed useful".
Where allocation of VSAs are required, it is recommended that IEEE
802 create a uniform format for all of IEEE 802, rather than having
each IEEE 802 group create their own VSA format. The VSA format
defined in [IEEE80211F] is inappropriate for this, since the Type
field is only a single octet, allowing for only 255 attributes. It
is recommended that IEEE groups read and follow the recommendations
in "RADIUS Design Guidelines" [BCP158] and the "Protocol Extensions"
ID [RADEXT] when designing and reviewing new extensions and
attributes.

## Slide 24: Conclusion
IEEE 802 Scope of OmniRAN

## Slide 25: Conclusion
OmniRAN Reference Points can be mapped into the IEEE 802 Reference Model
  R1 is completely covered by IEEE 802 specifications
  R2 and R3 are related to attributes for control of IEEE 802 functions and the definition of a DL SAP for the transport of user payload
  R4 is not considered by this contribution
    IEEE 802.21 may provide some ideas for its representation in the IEEE 802 views.
  R5 may be completely out of scope of IEEE 802
    However attributes of R3 may be copied over to R5
IP protocols used for OmniRAN are out of scope of IEEE 802
OmniRAN Specification in the scope of IEEE 802 would consist of
  an normative part defining control attributes and a DL SAP for the user payload
  an informative part outlining the overall architecture
  an informative part proposing the usage of particular IP protocols and the mapping of the IEEE 802 attributes into the IP protocols.
BTW: The approach seems to be aligned as well with the SDN use cases.