## Slide 1
P802.1CF NRM Backhaul Considerations |  |  | 
Date: 2014-11-05 |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Max Riegel | Nokia Networks | +49 173 293 8240 | maximilian.riegel@nsn.com
Notice: This document does not represent the agreed view of the IEEE 802.1 OmniRAN TG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
The presentation addresses the representation of backhaul within the P802.1CF NRM.

## Slide 2: P802.1CF NRM Backhaul Considerations
Max Riegel
(Nokia Networks)

## Slide 3: Terminology
AN Access Network
PoA Point of Attachment (e.g. AP)
SS Subscription Service
CNS Core Network Service
CIS Coordination and Information Service
TE Terminal

## Slide 4: Backhaul is part of Access Network
Scope of IEEE 802
Medium
Medium
Data Link
Physical
Network
Transport
Application
DL
Phy
DL
Phy
Data Link
Physical
Network
Transport
Application
Network
Network
Medium
Medium
Data Link
Physical
Data Link
Physical
OmniRAN provides a generic model of an access network based on IEEE 802 technologies
Access Network
Terminal
Core
Service
Core
R2
R1
R3
OmniRAN Network Reference Model
Access Network
Terminal
DL
Phy
DL
Phy
DL
Phy
DL
Phy
Medium
Backhaul
Backhaul

## Slide 5: Backhaul Characteristics
Part of the Access Network
Transport of the user plane between PoA and CNS
Consists of bridges and links between bridges
Mix of wired or wireless medium possible within a backhaul
Isolation of user plane from transport network through VLANs
  User plane is ‘tunneled’ through
  Backhaul does not modify payload
Multiple operational domains possible within backhaul
  Bridges and links may belong to multiple operators.
  However a brigde device has a single owner?

## Slide 6: Virtual LANs
802.1Q provides the functionality to enable multiple independent LANs (Broadcast Domains) within the same infrastructure
  Making use of a VLAN Tag in each ETH frame to identify the membership to particular LANs
VLAN Tags can be stacked to allow for multiple operational domains
  Customer VLAN
  Service Provider VLAN
  Backbone Provider VLAN
IEEE 802 based backhaul deploys stacked VLANs for distinction of operational domains

## Slide 7: VLAN Deployment Example for Backhaul Realization
Core
Internet
R1
Terminal
Access
R1
Terminal
Access
R1
Terminal
Access
R1
Terminal
Access
Core
Internet
Core
Internet
Core
Internet
R3
R3
R3
R3
ETH Service Provider ##A##
ETH Service Provider ##B##
ETH Backbone Provider
ETH Service Provider ##A##
ETH Service Provider ##C##
Backhaul

## Slide 8: NRM with R8c and CIS over R9c
Access Network
Terminal
R1
Coordination and Information Service
R2
R9c
R8c
AN Ctrl
TE Ctrl
Subscription
Service
Core Network Service
R3d
R3s
CNS Ctrl
R3c

## Slide 9: The issues of representing backhaul in the NRM
In IEEE 802 backhaul is more than tunneling
  ‘Switches’ may concurrently handle both user plane forwarding and service provider VLAN processing (transport network)
Missing separation of user plane and transport network
  Unlike other access network technologies
‘Transport’ may belong to multiple operational domains
No obvious way to split between user plan attributes and transport network attributes within the configuration of a provider bridge
  Provider backbone bridges may facilitate easier separation

## Slide 10: Conclusion
Exposing Backhaul in NRM creates much more complexity than just adding some reference points
  Model for separation of user plane and transport network required
  Transport model must support multiple operational domains and hierarchies
Further thoughts needed on modeling and representation of provider bridges and provider backbone bridges.