## Slide 1
P802.1CF NRM Ambiguities |  |  | 
Date: 2015-01-12 |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Max Riegel | Nokia Networks | +49 173 293 8240 | maximilian.riegel@nsn.com
Notice: This document does not represent the agreed view of the IEEE 802.1 OmniRAN TG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
Document ‘omniran-14-0083-00-00TG-p802-1cf-network-reference-model.docx’ specifies the Network Reference Model of P802.1CF. This presentation reviews the definitions and brings up some ambiguities in the definition of the P802.1CF.

## Slide 2: P802.1CF NRM Ambiguities
2015-01-13
Max Riegel
(Nokia Networks)

## Slide 3: Terminology
AN: Access Network
SS: Subscription Service
CNS: Core Network Service
CIS: Coordination and Information Service
TE: Terminal
NA: Node of Attachment

## Slide 4: From omniran-14-0083-00-00TG-p802-1cf-network-reference-model.docx Basic Network Reference Model
Access Network
Terminal
R1
Subscription
Service
Core Network Service
R3d
R3s
R2
CNS Ctrl
AN Ctrl
TE Ctrl
R3c
Figure 1: Basic Network Reference Model

## Slide 5: From omniran-14-0083-00-00TG-p802-1cf-network-reference-model.docx NRM Description
Figure 1 presents the Basic Network Reference Model (NRM). This NRM is the basis of further models and includes the basic differentiation between services and the reference points for their communication. This NRM is composed of three main elements; i) the terminal, ii) the Access Network and iii) the Core Network, consisting of Core Network Service (CNS), CNS Control and Subscription Service. The basic NRM differentiates two service types: i) Subscription service and ii) Core Network service. Please note that currently no assumption on the service providers is made.
In the NRM depicted in Figure 1, for each element we assume a control entity which we will call Controller (Ctrl). Each of the elements has a specific Controller.

## Slide 6: The issue: How do we denote the red entities?
Access Network
Terminal
R1
Subscription
Service
Core Network Service
R3d
R3s
R2
CNS Ctrl
AN Ctrl
TE Ctrl
R3c
Core Network
Access Network ??
Terminal ??

## Slide 7: The issue in the comprehenisve NRM
Core Network
Access Network ??
Terminal ??
Access Network
Terminal
R1
Coordination and Information Service
R2
R9c
R8c
AN Ctrl
TE Ctrl
Subscription
Service
Core Network Service
R3d
R3s
CNS Ctrl
R3c
NA
Backhaul
R6d
R6c
R7c

## Slide 8: Potential approaches
Show controller internal to Terminal and Access Network - 
Introduce additional names for Terminal+TE Ctrl, as well as Access Network + AN Ctrl - 
Rename Terminal (TE) -> Terminal Service (TES) and Access Network (AN) -> Access Network Service (ANS) in correspondence to Core Network (CN) and Core Network Service (CNS)

## Slide 9: Proposal #1
Core Network
Access Network
Terminal
Access Network Service
Terminal Service
R1
Coordination and Information Service
R2
R9c
R8c
AN Ctrl
TE Ctrl
Subscription
Service
Core Network Service
R3d
R3s
CNS Ctrl
R3c
NA
Backhaul
R6d
R6c
R7c

## Slide 10: Other proposal ?
Core Network
Access Network
Terminal
Terminal Interface
R1
Coordination and Information Service
R2
R9c
R8c
AN Ctrl
TE Ctrl
Subscription
Service
Core Network Service
R3d
R3s
CNS Ctrl
R3c
NA
Backhaul
R6d
R6c
R7c