## Slide 1
Radio Interface Component from an OmniRAN perspective |  |  | 
Date: 2015-09-14 |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Max Riegel | Nokia Networks | +491732938240 | maximilian.riegel@nokia.com
Notice: This document does not represent the agreed view of the OmniRAN EC SG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
This contribution introduces the idea of ‘802.11 as a component’ to OmniRAN and brings up a couple of questions and approaches for further discussion in OmniRAN.

## Slide 2: Radio Interface Component from an OmniRAN perspective
Max Riegel
Nokia Networks

## Slide 3: Problem Statement
Radio Interface Component

## Slide 4: What is a component? From 11-15-0757-01-0000-802-11-as-a-component-tutorial.pptx
For the purpose of this submission, a component has a defined function and defined external interfaces.
The component doesn’t care how it is used, provided that the use of the component matches the constraints of its defined external interfaces.
It should be possible to swap implementations of the component from different sources provided those implementations are compliant to the defined functions and external interfaces.

## Slide 5: Is 802.11 a component now? From 11-15-0757-01-0000-802-11-as-a-component-tutorial.pptx
Answer: No
We have these main impediments:
  No concrete definition of our management interface, defined by various SAP primitives
  A “theoretical” MIB of which there is no compliant implementation.
  Lack of clarity as to whether the SME is part of the STA or not. There are “shall statements” for it, but no adequate interface to control it.

## Slide 6: Schematic 802.11 Protocol Architecture
802.1X
  Port Access Entity
  Authenticator/Supplicant
RSNA Key Management
  Generation of Pair-wise and Group Keys
Station Management Entity (SME)
  interacts with both MAC and PHY Management
MAC Layer Management Entity (MLME)
  synchronization
  power management
  scanning
  authentication
  association
  MAC configuration and monitoring
MAC Layer
  basic access mechanism
  fragmentation
  encryption
PHY Layer Management Entity (PLME)
  channel tuning
  PHY configuration and monitoring
Physical Layer Convergence Protocol (PLCP)
  PHY-specific, supports common PHY SAP
  provides Clear Channel Assessment signal (carrier sense)
Physical Medium Dependent Sublayer (PMD)
  modulation and encoding
Notes: 8

## Slide 7: Value of an abstract management API From 11-15-0757-01-0000-802-11-as-a-component-tutorial.pptx
An abstract API allows an architectural partition to be specified, in terms of entities, interfaces between entities, and the behaviour of those entities
This partition is not necessarily at the same level of granularity that would be chosen for a practical management API
Because this choice of granularity is left to the implementer, a higher layer network management entity cannot depend on any uniform behaviour to manage.

## Slide 8: State of the Art
Radio Interface Component

## Slide 9: OAM in the IEEE 802.11 Standards Environment
IEEE 802.11 defines a radio interface
Wi-Fi Alliance ensures compliance of the radio interface by certification
OAM of the 802.11 radio interface is described by a comprehensive 802.11 MIB
A couple of organizations developed special variants of OAM interfaces for 802.11 to enable interoperability.
RADIUS is used for AAA messaging.
IEEE 802.11
Network
802.11 OAM
?
AAA
RADIUS

## Slide 10: BroadBand Forum CWMP
CWMP: CPE WAN Management Protocol aka TR-069
  https://www.broadband-forum.org/cwmp.php
        Broadband Forum, MR230, TR-069 deployment scenarios
  TR-069 is an soap/HTTP based protocol for transmission of XMLbased descriptions of management models between CPE and ACS
  TR-069 Data Models are xml documents that are “schema-like”, that describe the management objects and parameters used for particular use cases.
The CWMP Data Model Schema is specified in TR-106.
TR-181 defines version 2 of the TR-069 Device data model (Device:2) and is applicable to all types of TR-069-enabled devices. It obsoletes both Device:1 and InternetGatewayDevice:1 specifications

## Slide 11: TR-181 Wi-Fi Model
Device.WiFi
Device.WiFi.Radio.{i}
Device.WiFi.Radio.{i}.Stats
Device.WiFi.NeighboringWiFiDiagnostic
Device.WiFi.NeighboringWiFiDiagnostic.Results.{i}
WiFi.SSID.{i}
WiFi.SSID.{i}.Stats
WiFi.EndPoint.{i}.
WiFi.EndPoint.{i}.Stats
WiFi.EndPoint.{i}.Securtiy
WiFi.EndPoint.{i}.Profile.{i}
WiFi.EndPoint.{i}.Profile.{i}.Security
WiFi.EndPoint.{i}.WPS
WiFi.EndPoint.{i}.AC.{i}
WiFi.EndPoint.{i}.AC.{i}.Stats
WiFi.AccessPoint.{i}
WiFi.AccessPoint.{i}. Security
WiFi.AccessPoint.{i}. Accounting
WiFi.AccessPoint.{i}.WPS
WiFi.AccessPoint.{i}. AssociatedDevises.{i}
WiFi.AccessPoint.{i}. AssociatedDevises.{i}.Stats
WiFi.AccessPoint.{i}.AC.{i}
WiFi.AccessPoint.{i}.AC.{i}.Stats

## Slide 12: LINUX Wireless

## Slide 13: LINUX Wi-Fi driver architecture
nl80211 has become defacto standard for Wi-Fi configuration in LINUX
  Defines a comprehensive list of controls, commands and attributes for Wi-Fi
  Communicates by netlink (RFC3549) with kernel
cfg80211 provides unified interface into kernel drivers
mac80211 and future fullmac drivers
cfg80211
nl80211
Wi-Fi ‘hardware’
userspace
kernel
iw
hostapd
wpa_suplicant
…

## Slide 14: Wi-Fi OAM specification ‘nl80211.h’ http://git.kernel.org/cgit/linux/kernel/git/linville/wireless.git/tree/include/uapi/linux/nl80211.h?id=HEAD
#ifndef __LINUX_NL80211_H
#define __LINUX_NL80211_H
/*
* 802.11 netlink interface public header
*
* Copyright 2006-2010 Johannes Berg <johannes@sipsolutions.net>
* Copyright 2008 Michael Wu <flamingice@sourmilk.net>
* Copyright 2008 Luis Carlos Cobo <luisca@cozybit.com>
* Copyright 2008 Michael Buesch <m@bues.ch>
* Copyright 2008, 2009 Luis R. Rodriguez <lrodriguez@atheros.com>
* Copyright 2008 Jouni Malinen <jouni.malinen@atheros.com>
* Copyright 2008 Colin McCabe <colin@cozybit.com>
*
* Permission to use, copy, modify, and/or distribute this software for any
* purpose with or without fee is hereby granted, provided that the above
* copyright notice and this permission notice appear in all copies.
*
* THE SOFTWARE IS PROVIDED "AS IS" AND THE AUTHOR DISCLAIMS ALL WARRANTIES
* WITH REGARD TO THIS SOFTWARE INCLUDING ALL IMPLIED WARRANTIES OF
* MERCHANTABILITY AND FITNESS. IN NO EVENT SHALL THE AUTHOR BE LIABLE FOR
* ANY SPECIAL, DIRECT, INDIRECT, OR CONSEQUENTIAL DAMAGES OR ANY DAMAGES
* WHATSOEVER RESULTING FROM LOSS OF USE, DATA OR PROFITS, WHETHER IN AN
* ACTION OF CONTRACT, NEGLIGENCE OR OTHER TORTIOUS ACTION, ARISING OUT OF
* OR IN CONNECTION WITH THE USE OR PERFORMANCE OF THIS SOFTWARE.
*
*/
#include <linux/types.h>
#define NL80211_GENL_NAME "nl80211"
/**
* DOC: Station handling
*
* Stations are added per interface, but a special case exists with VLAN
* interfaces. When a station is bound to an AP interface, it may be moved
* into a VLAN identified by a VLAN interface index (%NL80211_ATTR_STA_VLAN).
* The station is still assumed to belong to the AP interface it was added
* to.
*
* Station handling varies per interface type and depending on the driver's
* capabilities.
*
nl80211.h defines
  120 commands
  about 600 attributes and controls
Potentially nl80211.h is the most comprehensive open OAM interface for 802.11
  next to the 802.11 MIB

## Slide 15: OmnirAN Perspective
Radio Interface Component

## Slide 16: Access network architecture
Medium
Medium
Data Link
Physical
Network
Transport
Application
DL
Phy
DL
Phy
Data Link
Physical
Network
Transport
Application
Network
Network
Medium
Medium
Data Link
Physical
Data Link
Physical
Access Network
Terminal
Access Router
Information Server
DL
Phy
DL
Phy
DL
Phy
DL
Phy
Medium
Backhaul
Backhaul
The physical view of an access network
Subscription Service
Protocol layer architecture of an access network
Node of Attachment
Terminal Interface
Access Router Interface
Scope of P802.1CF
STA
AP

## Slide 17: P802.1CF Network Reference Model
Access Router
Access Network
Terminal
Terminal Interface
R1
Coordination and Information Service
R2
R10
R8
AN Ctrl
TE Ctrl
Subscription
Service
Access Router Interface
R3
R4
AR Ctrl
R9
NA
Backhaul
R6
R5
R7
R11
STA
AP
NA = Node of Attachment {AP, BS}
Radio interface components

## Slide 18: Attributes of the generic network model
Application view
  Guides deployment of IEEE 802 technologies
Components
  Defines abstract functional entities of IEEE 802 technologies
    E.g. Node of Attachment, Backhaul, TE/AR Interface
Generic
  Emphasizes commonalities among IEEE 802 technologies
    E.g. MAC Service, EAPoL, LMI
Software oriented
  Creates data models for IEEE 802 access network and components.
  In OO terms: Definition of classes for ‘access network’, ‘na’, ‘backhaul’
Extensible
  Provides basic/generic data structures for extension by technology specifics

## Slide 19: Reference point variations
IEEE 802 knows about 2 kind of interfaces:
User data as well as peer-to-peer control is conveyed via ports
Control and management is represented by Layer Management Information as currently specified by the MIB
Control
Port

## Slide 20: Lifecycle of a WLAN session
Network Selection
Accounting
Disassociation
Host Configuration
Application
QoS Control
Application
Host Cfg Release
Accounting Start
Authentication
Authorization
Association
Scanning
AAA Policy
Configuration
DHCP
Application
STA
AP
ANQP

## Slide 21: Specification of a component
Describing a network element as a ‘component’ would require:
  Deployment models
  A control architecture, i.e. definition of entities exchanging control information with the ‘component’
  An outline for the specification of the functional behavior from an application perspective
  Structuring the control attributes from an application perspective

## Slide 22: What 802.1CF could do for IEEE 802.11 as a ‘component’
802.1CF would provide the solution for
  Defining the deployment models (STA, AP)
  A control architecture, i.e. definition of entities exchanging control information with the ‘component’
  A generic structure for the management object model aligned to the functional behavior
Out of scope of 802.1CF
  Restructuring/redefining the IEEE 802.11 control attributes
  It would be left to 802.11 to develop an appropriate format of its LMI (Layer Management Information (MIB))

## Slide 23: Discussion
Radio Interface Component