## Slide 1
P802.1CF within the scope of 5G |  |  | 
Date: 2015-11-09 |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Max Riegel | Nokia Networks | +491732938240 | maximilian.riegel@nokia.com
Yonggang Fang | ZTE |  | yfang@ztetx.com
Notice: This document does not represent the agreed view of the IEEE 802.1 OmniRAN TG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
Initial considerations about Wi-Fi as component of 5G indicate that deployment of IEEE 802 radio access technologies would require not only the PHY and MAC of the radio interface but a comprehensive model of a Radio Access Network
This presentation provide further observations on deploying IEEE 802 access network as part of a 5G cellular system.

## Slide 2: P802.1CF within the scope of 5G
Max Riegel, Nokia Networks
Yonggang Fang, ZTE

## Slide 3: Outline
IEEE 802 radio technologies and 5G requirements
Results of Bangkok OmniRAN discussions
IEEE 802.11 in public communication networks
Interfacing options of P802.1CF with 5G core
Introduction of 5G network requirements

## Slide 4: Radio Requirements
P802.1CF within the scope of 5G

## Slide 5: IEEE 802 matches 5G requirements
5G Technology Directions
IEEE 802 technologies
Extreme broadband
  802.11ac, 802.11ad
  Upcoming: .11ax & .11ay
M2M
  802.11ah
  Various 802.15 radios
  Upcoming: ‘LRLP@2.4G’
Critical communication
  802.11e
  802.11p
5G Radio Requirements
Extreme Broadband
High throughput, consistent QoE
M2M
Low cost, low battery consumption
Critical communication
Low latency, high reliability

## Slide 6: 5G Radio Requirements
IEEE 802 has technologies fitting into the scope of 5G
IEEE 802.11 already today has solutions fitting well 5G requirements
  Ultra broadband with up to 6.9 Gbps
  M2M with multiple years of single battery operation
  Critical communication support for V2V communication
IEEE 802.11 is evolving its technology in all directions
Other IEEE 802 technologies match 5G requirements as well
  E.g. IEEE 802.15 has multiple radio interfaces optimized for M2M deployments

## Slide 7: Initial discussions in Bangkok, TH
P802.1CF within the scope of 5G

## Slide 8: OmniRAN TG Discussions ‘802.11 as a component’
Special 2hrs session on Sept. 16th
  Well attended by industry (14 organizations)
2 presentations
  WLAN as a Component (WaaC)
    Yonggang Fang (ZTETX)
    https://mentor.ieee.org/omniran/dcn/15/omniran-15-0043-01-CF00-wlan-as-a-component.pptx
    Introduces a new perspective on discussion that essentially a WLAN RAN may be required to successfully introduce 802.11 to 5G
  Radio Interface Component from an OmniRAN perspective
    Max Riegel (Nokia Networks)
    https://mentor.ieee.org/omniran/dcn/15/omniran-15-0044-01-CF00-radio-interface-component.pptx
    Showed that OmniRAN approach provides both, a model for a 802.11 radio component as well as a 802.11 Radio Access Network.
    No consensus on how to treat terminals in the component discussions.

## Slide 9: OmniRAN TG Discussions ‘802.11 as a component’
Conclusion of the discussions
  Agreement that there is an opportunity to define a new set of interfaces to address the 5G requirements for inclusion of IEEE 802.11
  This work would result in an 802.11 Radio Access Network (RAN).
  OmniRAN P802.1CF could potentially provide the network architecture (Stage 2) for this RAN.

## Slide 10: IEEE 802.11 in Public Communication Networks
P802.1CF within the scope of 5G

## Slide 11: Currently IEEE 802.11 is mainly used as wireless access technology in fixed networks … but consumers perceive it as ‘mobile’
CSP Backbone
Internet
2G/3G
4G
Mobile Core
xDSL
FTTH
Cable
Leased
Line
LAN
CSP Backbone
CSP Backbone
GSM/WCDMA/LTE
Wi-Fi

## Slide 12: IEEE 802.11 in mobile networks
Integration of IEEE 802.11 with mobile networks
  Control plane is connected through TWAP to AAA server in 3GPP Core.
  User plane is connected to PDN GW over TWAG.
Mainly used as stationary offload of bulk data, not as primary connection to serve Wi-Fi terminals
3GPP CORE
BSS1
BSS2
(TWAG)
NA2
NA1
AAA Server
PDN GW
STa
S2a
Trusted Non-3GPP WLAN
HSS
(TWAP)

## Slide 13: Current usage of IEEE 802.11 in public communication networks
Mobile operators currently consider IEEE 802.11 as a kind of ‘fixed’ wireless access technology
  Despite customers using their Wi-Fi terminals in a mobile fashion
  Not considering Wi-Fi as a primary mean to provide service
3GPP specifications currently treat Wi-Fi only as a secondary radio technology for ‘offload’
  Trying to squeeze IEEE 802.11 into a radio access network following completely different design approaches
    3GPP cellular radio interfaces are fully centrally controlled, while IEEE 802.11 vastly relies on terminal intelligence and local decisions
  Leading to requests to IEEE 802.11 to make the technology controllable like a 3GPP technology
  Leveraging full potential of IEEE 802.11 might require other integration approaches.
    Full potential of IEEE 802.11 as managed technology fulfilling highest requirements can be experienced today in Enterprise Wi-Fi networks.
Fixed network specification groups have done more comprehensive work to fully leverage IEEE 802.11 potentials
  E.g. BBF (TR069/TR181), CableLabs (WR-SP-WiFi-MGMT)

## Slide 14: Interface Options to 5G
P802.1CF within the scope of 5G

## Slide 15: Assumptions about network integration of the various Radio Access Technologies
From the NGMN Alliance 5G whitepaper:

## Slide 16: NGMN Alliance thoughts on 5G interface options
NGMN currently considers 3 options
  Option 1 has minimal impact to exisiting RATs but limitations to introduce full 5G performance services
  Option 2 allows for full evolution of network services for 5G but requires new interfacing with EPC and Fixed/Wi-Fi
  Option 3 would be the most comprehensive approach by integrating LTE, 5G and Fixed/Wi-Fi but has manifold implications.
    NGMN mandates further research into Option 3 before drawing conclusions.
Option 3 allows to fully leverage IEEE 802 technologies capabilities
  However option 3 would require that IEEE 802 provides an appropriate network interface to the 5G core

## Slide 17: P802.1CF Interface option to 5G
Access Router
Access Network
Terminal
Terminal Interface
R1
Coordination and Information Service
R2
R10
R8
AN Ctrl
TE Ctrl
Subscription
Service
Access Router Interface
R3
R4
AR Ctrl
R9
NA
Backhaul
R6
R5
R7
R11
IEEE 802 Access Network
5G NW Functions

## Slide 18: 5G Requirements
P802.1CF within the scope of 5G

## Slide 19: NGMN 5G White Paper Contents http://ngmn.org/fileadmin/ngmn/content/images/news/ngmn_news/NGMN_5G_White_Paper_V1_0.pdf
Table of Contents
  Executive Summary
  Introduction
  5G Vision
    Business Context
    Use Cases
    Business Models
  Requirements
  Technology and Architecture
  Spectrum
  IPR
  Way Forward
  Conclusions
  Annexes
Mainly spectrum and radio aspects were introduced to 802.11 by https://mentor.ieee.org/802.11/dcn/15/11-15-0547-00-0wng-ngmn-5g-white-paper-overview.pptx
This presentation focuses on networking aspects in relation to the scope of P802.1CF

## Slide 20: NGMN 5G Use Cases

## Slide 21: NGMN 5G Business Models

## Slide 22: Architectural implications by NGMN 5G Business Models
Network sharing
  Leverage network assets from multiple sources
  Provide networking functions to others
Enhanced connectivity
  Enable dynamically configured connectivity with differentiated feature sets
Enriched offers by partnership
  Allow for combination and integration of network services with other assets and information sources

## Slide 23: NGMN 5G Design Principles

## Slide 24: Design Principles
Core Network
Create common composable core
Minimize number of entities and functionalities
C/U-function split, lean protocol stack
No mandatory U-plane functions
Minimize legacy interworking
RAT-agnostic core
Fixed and mobile convergence
Operation & Management
Simplify operations and management
Automation and self-healing
Probeless monitoring
Collaborative management
Integrated OAM functionality
Carrier-grade network cloud orchestration

## Slide 25: NGMN 5G Architecture

## Slide 26: Network Slicing
A “5G slice” provides a particular connection service with specific C- and U-plane functionality
  Collection of 5G network functions and specific RAT settings for a particular service
  Can span all domains of the network
Not all slices contain the same functions
  Can be only subset of today’s mobile networks
  Provides only the traffic treatment that is necessary for the particular use case.
Flexibility of slicing is a key enabler for value creation.
Third-party entities can be given permission to control certain aspects of slicing.

## Slide 27: NGMN 5G Network Slicing

## Slide 28: Technology Building Blocks N1 – Network Flexibility
Software-Defined Networking
  Programmable network with centralized logically abstracted control, separated from a flow-based data/forwarding plane, like P-GW/S-GW and so on.
Virtualized Mobile Core Network
  Software based functionality abstracted from common pool of hardware. Enables mobile core network elements as virtualized functions decoupled from specialized hardware, managing function and resources more flexibly and intelligently
  Virtualization platform can provide open APIs to management functions utilizing shared resources.
State-disintegrated Core Node
  State of a core node is separated and kept in a remote database
Smart Edge Node
  A node at the edge of the network (e.g., base station, small cell or even terminal) can actively carry out some of the core network functionalities or additional services (example: context-aware dynamic caching)

## Slide 29: Technology Building Blocks N2 - Efficient/Adaptive Network Resource Usage
Traffic Optimization
  Adapting the transported traffic to the characteristics of the transmission path and/or the end-device using middleboxes in the network. Intelligently choosing the transmission path and last mile based on attributes of the end-device, available access technologies at the end-device’s location and status of network (paths and nodes)
Scalable service architecture
  Ability to adapt and scale to service needs based on the use case (and mapped resource allocation)
Big data
  To capture, analyze, make usable and leverage the vast amount of data available in many instances of content/service delivery. Additionally, along with behavior, context and proximity aspects, captured (or discovered & provided) by user devices, social media/networks, content/service delivery, user-data management, research and trial data, machine/sensors (including discovery) and IoT.
Content-optimization and adaptive streaming
  Use of client-side and server-side techniques to adapt content delivery to path characteristics and the attributes of the end-device.

## Slide 30: Technology Building Blocks N3 – Other Enablers
Technologies for massive connectivity
  There are a wide variety of small packets transmissions with different QoE (Quality of Experience) for both M2M and H2H, e.g. Periodic keep-alive packets, Bursty Instant Messages, or Real-time critical message delivery
  These small packet transmissions may cause frequent RRC transitions and contribute to network signaling congestion. Moreover, the current RRC transitions may introduce extra delay and thereby cannot satisfy the real-time requirement for some applications generating small packets transmissions. 3GPP is looking for signaling optimization of small packet transmission. Evolutional and some revolutionary mechanisms need to be devised to address this for 5G.
Privacy and Security Aspects
  There are different aspects related to security that will play an important role for 5G design, including:
  Radio link encryption of user traffic. Most applications that require security often implement it themselves, for instance using TLS/SSL, IPsec or some other application-specific security. Given this, how shall we handle link encryption of user traffic in 5G?
  Security-design for low-latency use cases. Some 5G use cases require extremely low latency – including the latency of initiating communications. This will be an important shaping factor for the security design.
  Location and identity privacy will require improvements with respect to current solutions used for 4G.

## Slide 31: Conclusion
P802.1CF within the scope of 5G

## Slide 32: Conclusion
IEEE 802 radio technologies fit well to NGMN 5G expectations
IEEE 802 radio technologies require an own version of radio access network to fully unleash their capabilities.
P802.1CF provides an generic approach to provide an IEEE 802 radio access network.
NGMN has demanding expectations on the upcoming mobile networks.
P802.1CF can fulfill NGMN expectations and requirements for the 5G radio access network.
  Except wide area high mobility, which is not in scope