## Slide 1
Network reference model for access network virtualization |  |  | 
Date: 2016-03-14 |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Max Riegel | Nokia | +49 173 293 8240 | maximilian.riegel@nokis.com
Notice: This document does not represent the agreed view of the IEEE 802.1 OmniRAN TG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
The presentation provides an introduction into the representation of virtualized access networks (network instances) by the 802.1CF network reference model and functional description. It also approaches the representation of fault diagnostic and maintenance in a virtualized network infrastructure.

## Slide 2: Network reference model for access network virtualization
Max Riegel
(Nokia)

## Slide 3: ToC
Problem description
Virtualized access network at a glance
Virtualized access network properties
Other forms of co-use of network resources
  Roaming
  Network sharing
Deployment examples:
  multi-SSID in Wi-Fi
  China Mobile iPCN
  5G network slicing
Network management aspects
Conclusion

## Slide 4: Problem description
802.1CF currently does not explain how to treat virtual access networks
  Multiple access network instances on a common resource pool
Virtualized access networks are an emerging aspect of access infrastructures
  Multi-SSID in Wi-Fi access networks
  China Mobile iPCN
  5G network slices
Following slides show the representation of virtual access networks in 802.1CF architecture

## Slide 5: NRM Overview
A Terminal is connected with a single AN, SS and AR at a time
An Access Network can have connections with multiple SSs and ARs at a time
Coordination and Information Service supports the management of resources, which are shared among multiple access networks
Access Router
Access Network
Terminal
TEI
R1
CIS
R2
R10
R8
ANC
TEC
SS
ARI
R3
R4
ARC
R9
NA
BH
R6
R5
R7
R11
CIS Coordination and Information Service
SS Subscription Service
TEC Terminal Control
TEI Terminal Interface
ANC Access Network Control
NA Node of Attachment
BH Backhaul
ARC Access Router Control
ARI Access Router Interface

## Slide 6: NRM describes single access network instance
Access Router
Access Network
Terminal
TEI
R1
CIS
R2
R10
R8
ANC
TEC
SS
ARI
R3
R4
ARC
R9
NA
BH
R6
R5
R7
R11

## Slide 7: Multiple instances of access network
TEI
R1
CIS
R10
R8
ANC
TEC
SS
ARI
R3
R4
ARC
R9
NA
BH
R6
R5
R7
R11
TEI
R1
R8
ANC
TEC
SS
ARI
R3
R4
ARC
R9
NA
BH
R6
R5
R7
R11
TEI
R1
R8
ANC
TEC
SS
ARI
R3
R4
ARC
R9
NA
BH
R6
R5
R7
R11
Virtualized access network is represented by multiple instances of NRM with a single CIS for resource management

## Slide 8: Virtualized Access Network Properties
The NRM represents one instance of an access network
  Not the physical infrastructure
Operation of virtualized access networks is isolated to the others
  Coordination is performed through CIS
  Multiple access networks may connect to the same pool of SSs and ARs
Virtualized access networks can configure and monitor themselves within the assigned resources.
The instantiation of further virtualized access networks is not performed by the virtual access network but by a meta-entity which has control over the available physical resources
  Orchestrator function may be associated with CIS
Control and management of an (virtual) access network is located in the ANC
  Management system of fault detection and maintenance may be considered as part of ANC as well

## Slide 9: Other forms of sharing access network resources
Roaming
  Relaying of AAA information through the SS of another operator
Network sharing
  An AN is concurrently used by multiple independent SSs

## Slide 10: Wi-Fi ‘multi SSID’ use case
Shared wireless access network
Infrastructure used for two different Wi-Fi services
  Two different SSIDs with its isolated security domains and aggregation separated by different VLAN IDs
Only radio efficiency impacts limit the number of virtual access networks of a Wi-Fi infrastructure

## Slide 11: Wi-Fi virtual access networks
For virtual networking Wi-Fi AP is decomposed into
  VAP (virtual AP, consisting of a MAC instance, security functions, MLME and SME)
  Radio transceiver (TRX, common PHY layer functions of all VAPs)
SSID defines an 802.11 Extended Service Set and relates to a VID on the bridging infrastructure
Wi-Fi virtual access network easily maps to the NRM layered concept presented before.
TE
AP
Switch
TE
TE
VAP
VID
AR
VAP
VID
AR
VAP
VID
AR
SS
SS
SS

## Slide 12: China Mobil iPCN

## Slide 13: NGMN 5G Network Slicing
A “5G slice” provides a particular connection service with specific C- and U-plane functionality
  Collection of 5G network functions and specific RAT settings for a particular service
  Can span all domains of the network
Not all slices contain the same functions
  Can be only subset of today’s mobile networks
  Provides only the traffic treatment that is necessary for the particular use case.
Flexibility of slicing is a key enabler for value creation.
Third-party entities can be given permission to control certain aspects of slicing.

## Slide 14: NGMN 5G Network Slicing

## Slide 15: Network Management Aspects
There are two dimensions of network management
  Managing each instance of the (virtual) access network independently by each tenant of the ANs
    The aspect, which is covered by the FDM section
  Managing the physical infrastructure providing the resources of AN instances
    A plethora of different solutions possible
    Anything in common, which we could describe?
Interlinking between the two dimensions can be achieved by CIS

## Slide 16: Conclusion
The NRM represents one instance of a virtual access network
  Completely consistent with dedicated physical implementations, except the limitations to the control of some PHY layer parameters
  Interception into PHY layer parameters should be performed by CSI interactions
    We may prepare our specification to easily relocate interactions into PHY layer parameters into CSI
    In which chapters do we reference PHY parameters?
    Are there cases of write actions to PHY parameters?
Network management aspects might focus on the management of virtual instances of the access network
  Effectively supporting the deployment of NaaS