## Slide 1
Measurement and Management in IEEE 802.11 and More |  |  | 
Date: [2016-03-16] |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Hao Wang | Fujitsu R&D Center | +86-10-59691000 | wangh@cn.fujitsu.com
Xiaojing Fan | Fujitsu R&D Center | +86-10-59691000 | fanxiaojing@cn.fujitsu.com
Su Yi | Fujitsu R&D Center | +86-10-59691000 | yisu@cn.fujitsu.com
Ryuichi Matsukura | Fujitsu/Fujitsu Laboratory | +81-44-754-2667 | r.matsukura@jp.fujitsu.com
Notice: This document does not represent the agreed view of the OmniRAN EC SG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
This presentation gives an overview on measurement and management functions in IEEE 802.11, and concludes that these functions can be covered by OmniRAN specification. Moreover, an argument is made on how the network management system should take form in the network reference model.

## Slide 2: Measurement and Management in IEEE 802.11 and More
2016-03-16
Hao Wang
Fujitsu R&D Center

## Slide 3: Background
Wi-Fi networks in home environments usually operates without any centralized control with individual stations controlling access to the medium, but for enterprise and WMAN deployments, radio resource measurement (802.11k) and wireless network management (802.11v) help optimize applications by managing radio network resources effectively.
  802.11k covers access point (AP) measurements and has been adopted quite widely by AP and device vendors
  802.11v allows AP measurements to be used in order to enable centralized remote configuration of client device parameters
These 802.11 extensions alone are not sufficient to create a managed network. A network management entity must sit above these interfaces and provide the control function.

## Slide 4: Layer Management Model
The layer management model of 802.11h provides a preliminary entity as ‘OAM client’ residing in ‘SME’.
  The model assumes that policy decisions, e.g. measurement and channel switching resides in the SME
  The protocol for measurement, switching timing, and the associated frame exchanges resides within the MLME
The model was adopted by 802.11k for use and actually are the foundation for providing the 802.11k measurements
MAC Timing
Measurement
Processing
Measurement
Policy
Channel Switch
Decision
Measurement
Frames
SME
MLME
Channel Switch
Timing
PLME
SME
MLME
MREQUEST
/MREPORT
Measurement
Frames
Measurement Policy
MEASURE
CHANNEL
SWITCH
MREQUEST
/MREPORT
‘OAM client’

## Slide 5: Management Interfaces
Primary interface to obtain real-time information through the request/response mechanisms of radio measurements (RM, 802.11k) and wireless network management (WNM, 802.11v)
Secondary interface provided to the management applications (NMS, EM) by performing MIB.get and MIB.set operations, e.g. SNMP GET and SET.
Primary Interface
Secondary Interface
e.g. SNMP GET and SET

## Slide 6: Comparing 802.3ah and 802.11k,v Capability Discovery
802.3ah | 802.11k,v | 
Information OAMPDU | Beacon Association Request/Reponse, Reassociation Request/Response, Probe Request/Response | 
OAM Configuration field | RM Enabled Capabilities Extended Capabilities Element | 
Variable Retrieval Link events OAM remote loopback support Unidirectional support OAM mode (1 byte) | Link measurement Neighbor Report Parallel Measurements … (5 bytes) | Event Diagnostics Multicast Diagnostics Location Tracking … (40 bits)

## Slide 7: Comparing 802.3ah and 802.11k,v Remote Failure Indication
802.3ah | 802.11k,v
Information OAMPDU | disassociation, deauthentication, DELTS, DELBA, DLS teardown
Critical link event | Reason code field
Link fault (The PHY has determined a fault has occurred in the receive direction of the local DTE.) Dying gasp (An unrecoverable local failure condition has occurred.) Critical event (An unspecified critical event has occurred.)* * Definition is implementation specific | Previous authentication no longer valid Deauthenticated because sending STA is leaving (or has left) IBSS or ESS Disassociated due to inactivity Disassociated because AP is unable to handle all currently associated STAs … (2 bytes)
Regarding security, shared channel resource allocation, QoS, channel condition, etc

## Slide 8: Comparing 802.3ah and 802.11k,v Link Monitoring
802.3ah | 802.11k,v
Event Notification OAMPDU Variable Request OAMPDU Variable Response OAMPDU | Radio measurement request/report Link measurement request/report Neighbor report request/response Event request/report Collocated interference request/report
Link event (for errors) Variable Descriptors/Containers | Measurement report IE TPC (transmit power control) report IE Neighbor report IE Event report ID Collocated interference report ID
Errored Symbol Period Errored Frame Errored Frame Period Errored Frame Seconds Summary MIB variable | CCA report, RPI histogram report, channel load report, noise histogram report, beacon report, frame report, STA statistics report, LCI report, transmit stream/category measurement report, multicast diagnostics report, location civic report, location identifier report Transmit power, link margin Information of neighbor, including BSSID, AP reachability, security, PHY type, etc. Time, reason and results of Transition event; EAP method and RSNA results; channel number, Tx power, connection Time and status of P2P link event; WNM log event Interference level, interval, center frequency and bandwidth of the collocated interference

## Slide 9: Comparing 802.3ah and 802.11k,v Remote Test
802.3ah | 802.11k,v
Loopback Control OAMPDU | Diagnostic Request Diagnostic Report
Remote Loopback command | Diagnostic Request/Report IE
Enable Disable | Association Diagnostic IEEE 802.1X Authentication Diagnostic

## Slide 10: Measurement Procedure (11k) Example of STA Statistic
A sends measurement request for STA statistic
  Set report condition: dot11RMRqstSTAStatTrigSTAFrameDupeCntThresh
B accepts measurement request
  B processes measurement
  B stores measurement results in MIB
B sends measurement report of STA statistic
  Generates a report every time duplicate frame count has increased more than dot11RMRqstSTAStatTrigSTAFrameDupeCntThresh
STA A
Measurement request
Measurement report
Measurement report
Process Measurement
STA B
Report results to SME by primitive
Store results in MIB
Initiated by SME through primitive
…

## Slide 11: Diagnostic Procedure (11v) Example of Association Test
A sends Diagnostic Request for association test
  Indicate the target AP (STA C) for testing
B accepts request and processes association test
  De-association with A
  Association with C and store association results in MIB
  De-association with C
  Re-association with A
B sends Diagnostic report
  Including testing results
Diagnostic request
STA C
STA B
(type = association test)
De-association request
STA A
De-association reply
Association request
Association reply
De-association request
De-association reply
Re-association request
Re-association reply
Diagnostic report
Process Association Test
Initiated by SME
Report results to SME

## Slide 12: 802.11 Fits in a Common Structure
NMS
(SS)
Controller
Interface
OmniRAN
NMS
OAM client
MAC/PHY interface
NMS
Ex. SNMP agent
MAC/PHY interface
802.3ah
802.1ag
OAM client
MAC/PHY interface
Ex. SNMP agent
MAC/PHY interface
OAMPDU
CFM message
802.3 OAM service interface
Ex. SNMP interface
Layer management interface (LMI)
Element Manager (EM)
EM
Itf-N
Ex. SNMP manager/ agent
Ex. SNMP manager
Itf-N
NMS
RM/WNM MIB
MAC/PHY interface
802.11 k/v
RM/WNM MIB
MAC/PHY interface
Management/action frame
MLME/PLME
SAP
Element Manager (EM)
Itf-N
R2, R4,
R11
R5, R7
R1, R6,
R3

## Slide 13: NMS vs. ‘Management Function Set’
Differentiate management functions by ‘EM’ and ‘NM’ is common in WiMAX and 3GPP, benefits including but not limited to
  Vendor specific management provided as EM
  Operator, service provider management provided as NM
  EM focus on managing network element (i.e. interface), providing OAM support through N<>S interface, and forward alarms and events to NM
  NM focus on managing multi-vendor multi-domain network, providing OAM support through ItfN when EM functionality is insufficient, and providing human interface to administrator
  Expose ItfN to the vendors which provides possibility standardize higher level of management (even if it is informative)
  Make the model more easy to extend, e.g. considering BSS, OSS, etc
  Help to define management functions and management domains when NRM blocks are operated with different arrangement
NMS
(SS)
Controller
(EM)
Interface
(NE)
OmniRAN
R2, R4,
R11
R5, R7
N<>S
E<>W
Management plane
Network plane
ItfN
R1, R6,
R3

## Slide 14: NMS vs. ‘Management Function Set’ Deployment Case (I)
NMS
(SS)
Controller
(EM)
Interface
(NE)
OmniRAN
R2, R4,
R11
R5, R7
N<>S
E<>W
Management plane
Network plane
ItfN
NMS
EM
EM
EM
EM
EM
R1, R6,
R3

## Slide 15: NMS vs. ‘Management Function Set’ Deployment Case (II)
NMS
(SS)
Controller
(EM)
Interface
(NE)
OmniRAN
R2, R4,
R11
R5, R7
N<>S
E<>W
Management plane
Network plane
ItfN
NMS
EM
R1, R6,
R3

## Slide 16: NMS vs. ‘Management Function Set’ Deployment Case (III)
NMS
(SS)
Controller
(EM)
Interface
(NE)
OmniRAN
R2, R4,
R11
R5, R7
N<>S
E<>W
Management plane
Network plane
ItfN
NMS
EM
R1, R6,
R3

## Slide 17: NMS vs. ‘Management Function Set’
NM + EM = Management Function Set? The drawbacks including but not limited to
  Functions in the ‘set’ are too much different, ‘set’ becomes ‘sets’
  The ‘set’ will be vendor specific or operator specific?
    If vendor specific, controller should provide human interface?
    If operator specific, operator should manage network element directly?
  Impossible to describe ‘ItfN’ interface
  The ‘set’ will be implemented only on ANC?
    If yes, impossible to support multi-vendor management scenario
    If no, management functions will be redundant and unnecessary
  Difficult to describe OSS, BSS, etc in near future
    OSS & BSS is on different level in the netowrk from SS & CIS
  Difficult to address the management requirement when the network is software defined or virtualized
NMS
(SS)
Controller
(EM)
Interface
(NE)
OmniRAN
R2, R4,
R11
R5, R7
N<>S
E<>W
Management plane
Network plane
ItfN
R1, R6,
R3

## Slide 18: Annex: Management Functionality of WiMAX
 | Element Management | Network Management
Fault Management | Fault identification, mitigation, and recovery, including rerouting traffic through other network elements, and initiating diagnostics remotely to avoid truck-rolls Forwarding the events / alarms to NMS | Manage and provide repair or temporarily work-around for faults automatically detected by network elements, or manually reported by subscribers.
Performance Management | Collects performance data on the air interface, traffic load, resource utilization, etc. which are needed for WiMAX network performance monitoring. | Gather the performance data that can be used to monitor network performance, ensure the QoS as defined in the subscriber’s service level agreements are being met and plan for network evolution
Security Management | Define the policies for operator access to managed objects. Define the policies for operator access to EMS capabilities (read only, etc) Define the policies for EMS operator access. | Provide control and protect over network resources. Provide centralized AAA capability
  Source: WMF-T31-119-R016v01 "WiMAX Network Management: NMS to EMS Interface"

## Slide 19: Questions, Comments Thank YOU!