## Slide 1: Proposal for IEEE 802.1CQ-LAAP
Antonio de la Oliva (UC3M, IDCC)
aoliva@it.uc3m.es
Robert Gazda (IDCC)
robert.gazda@interdigital.com

## Slide 2: Background
IEEE 802.1CQ aims at defining mechanisms for mac address distribution and automatic configuration in the SAI space
Two mechanisms to be defined:
  MAC address self-assignment (Claimed)
  Server/Proxy based assignment
    This will require of synchronization mechanism between Server and Proxies
The aim of this contribution is to propose a general mechanism for address assignment, based on IPv6 SLAAC and DHCP
  Detailed in the contribution, messages and rules for sending them

## Slide 3: Aim of these slides
Reminder of previous discussion
Definition of a set of questions to be answered (informal Straw-Poll?)
  Multiple LAAP mechanisms?
    Can we define a basic one based on Self-Assignment + Server as baseline?
  Self-Assignment
    Pool of addresses to choose from
      Definition of a set
      Provided by the network
      A mix?
    Source address and destination of the Claiming message
      I really like the idea of a multicast group, like in IPv6 Solicited multicast
    Preferred encapsulation  Personally I like the idea of LLDP or new LLC/SNAP
  Server-based
    Discovery of the server address Message to multicast address (interceptable by Proxy)
    Advertisement options  IPv6 RS LLDP
    Encapsulation
      Source address?
  OverallMechanism to advertise the network is conformant to .1CQ

## Slide 4: Self-assignment of MAC addresses
Node self-assigns a MAC address
  From previously defined space:
    Good: Easy to configure
    Bad: Cannot follow a given MAC address assignment in the network, e.g., follow semantics in the network
  From pool advertised by the network
    Good: Can follow the structure of MAC addresses defined by the network
    Bad: Needs of extra messages to carry on this advertisement

## Slide 5: Claiming Address Space TLV
Aim: Advertise pool of addresses a station can use for self-assignment
A prefix in this message means a MAC address and a number of bits that must remain constant of the MAC address provided, e.g., MAC/24
Claiming Allowed bit indicates if claiming is allowed in the network
Number of prefixes means number of the next 3 fields provided
Length MAC address indicates if the address provided is 48 or 64 bits
Prefix indicates MAC to be used as basis
Prefix length indicates number of bits that must remain fixed in the claimed address

## Slide 6: Possible co-existance
Listen for Claiming Address Space TLV for a time
If not present, self-claim from pre-defined pool
  Who sets this pool?
If LAAP proxy sees a message claiming an address not valid, answer with error code

## Slide 7: Self-assignment: Duplicate Address Detection
  Procedure similar to IPv6 DAD, send a probe, wait for answer
  What is the destination address to use?:
    Use of broadcast address (ff:ff:ff:ff:ff:ff).
      Flood
    Unicast to the MAC address claimed.
      Flood if address does not exist
    Use of a multicast group, such as the one used for the solicited multicast in IPv6. When a station self-assigns a MAC address, then it joins a multicast group such as the 33:33:xx:xx:xx:xx, where the last 4 bytes correspond to the last 4 bytes of the self-assigned MAC address. This might lead to spanning tree problems if the address is duplicated
  In all cases the source MAC address will be set to the claimed unicast address or to the broadcast address (as recommended by IEEE RA for NULL addresses)already discussed and not a good option
Notes:     Use of broadcast address (ff:ff:ff:ff:ff:ff). This solution will cause the network to flood unnecessary messages, since all stations in the LAN will receive the message.
    Unicast to the MAC address claimed. A message is sent in unicast to the address to be claimed. In this case the stations receiving the message (with a duplicate address) will answer and the duplication will be detected.
    Use of a multicast group, such as the one used for the solicited multicast in IPv6. When a station self-assigns a MAC address, then it joins a multicast group such as the 33:33:xx:xx:xx:xx, where the last 4 bytes correspond to the last 4 bytes of the self-assigned MAC address.

## Slide 8: Self-assignment: Possible DAD message
Different possibilities for encapsulation
  LLDP
  LLC/SNAP
  DAD procedure is based on the sending of the DAD request, with the D bit set to 0 and wait for some time (to be defined) until a DAD request, with D bit set to 1, is received or the timer expires.
  In case multiple addresses are claimed, the station may choose between using 1 message per address sent in unicast or a bulk message sent to broadcast. Unicast answers are expected for each duplicated MAC address detected.

## Slide 9: Server based
  Two big questions
    How do we reach the server
    Do we support advertisement of the server/LAAP proxies?
  How do we encapsulate these messages

## Slide 10: Server based assignment
In order to request a pull of MAC addresses the station requires to know the address of the Server/Proxy to request the addresses
An advertisement message is required:
Encapsulation can be done through LLDP or SNAP/LLC

## Slide 11: Server based assignment: Procedure
Once the LAAP Server/Proxy has been identified the procedure shown is followed:
  Solicit: A client sends a Solicit message to locate servers.
  Advertise: A server sends an Advertise message to indicate that it is available for LAAP service, in response to a Solicit message received from a client.
  Request: A client sends a Request message to request MAC address assignment.
  Confirm: A client sends a Confirm message to any available server to determine whether the addresses it was assigned are still appropriate to the link to which the client is connected.
We should follow DHCP guidelines, that are proven and well tested

## Slide 12: Server based assignment: Procedure
We should think on adding the following functionality to the LAAP server
  Renew: A client sends a Renew message to the server that originally provided the client's addresses and configuration parameters to extend the lifetimes on the addresses assigned to the client.
  Rebind: A client sends a Rebind message to any available server to extend the lifetimes on the addresses assigned to the client; this message is sent after a client receives no response to a Renew message.
  Reply: A server sends a Reply message containing assigned addresses and configuration parameters in response to a Solicit, Request, Renew, Rebind message received from a client. A server sends a Reply message in response to a Confirm message confirming or denying that the addresses assigned to the client are appropriate to the link to which the client is connected. A server sends a Reply message to acknowledge receipt of a Release or Decline message.
  Release: A client sends a Release message to the server that assigned addresses to the client to indicate that the client will no longer use one or more of the assigned addresses.
  Decline: A client sends a Decline message to a server to indicate that the client has determined that one or more addresses assigned by the server are already in use on the link to which the client is connected.
  Reconfigure: A server sends a Reconfigure message to a client to inform the client that the server has new or updated configuration parameters, and that the client is to initiate a Renew/Reply transaction with the server in order to receive the updated information.

## Slide 13: Server based assignment: Addressing
For all messages exchanged with the Server, the following rules should apply:
  Destination address must be chosen between the one received in a Server/Proxy LLDP TLV or a well known address defined in the standard. This well-known address can be, for example, the address 33:33:00:00:01:02, which corresponds to the multicast MAC address mapping of the IPv6 address ff02::1:2 (all DHCPv6 agents). In this way, a LAAP server can be collocated with a DHCPv6 server.
  Source Address: The station must use a randomised address following the policy as defined with the Claiming Address Space TLV.
Messages can be encapsulated following:
  Extend LLDP TLVs to provide the functionality. This has the drawback that standard LLDP is not forwarded by bridges, hence we will need to use any of the extensions defined that support this.
  Definition of new LLC/SNAP protocol.
  Use of Edge Control Protocol (ECP), as defined in IEEE 802.1Q.

## Slide 14: Advertisement of IEEE 802.1CQ use in the network
The network should advertise it is using LAAP
This can be done extending LLDP System Capabilities TLV (802.1AB)
12 | IEEE 802.1CQ enabled network | IEEE 802.1CQ