## Slide 1
WiFi Privacy network experiment at IEEE meeting @ Berlin |  |  | 
Date: [2015-03-08] |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Carlos Jesús Bernardos | UC3M |  | cjbc@it.uc3m.es
Fabio Giust | UC3M |  | fgiust@it.uc3m.es
Antonio de la Oliva | UC3M |  | aoliva@it.uc3m.es
Juan Carlos Zúñiga | InterDigital |  | JuanCarlos.Zuniga@InterDigital.com
Notice: This document does not represent the agreed view of the IEEE 802 EC Privacy Recommendation SG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
The present document describes the MAC Privacy trial
to be performed at IEEE plenary meeting @ Berlin
privecsg-15-0007-01-0000

## Slide 2: MAC Add Privacy Trial
As part of the Internet Privacy efforts in coordination between IETF (IAB/IESG) and IEEE 802 (Privacy EC SG), we are performing a trial to randomize the MAC address of some user's Wi-Fi devices
Instructions on how to participate in this trial are described here:
  http://goo.gl/eFUM9h
We need your help to make this a successful experiment
  Please participate!

## Slide 3: Experiment goals
Carry out a Wi-Fi MAC randomization trial/experiment at IEEE meeting @ Berlin
  Evaluating support of different OSes (Mac OS X, Linux, Windows and Android)
  Analyzing the impact of L2 address randomization on the user experience and the network infrastructure
    Specially in case of L2 address collision
  Keep learning from these experiences (building on top of initial trial at IETF 91 meeting in Honolulu, HI)

## Slide 4: Network setup
A specific SSID (ieee802_privacy_trial) deployed for the trial
  Deployed on all IEEE physical APs, as an additional virtual AP
  WPA2 PSK security, to avoid non participants to accidentally connect to our trial WLAN
  DHCP server specific configuration for the trial
    A different (shorter) lease time for trial participants
      30 minutes (instead of the 24-hour default lease)
      Participants are identified by a MAC addresses with 0x06 as first octet
      Different DHCP pool and VLANs

## Slide 5: Trial setup
Participants: please notify your participation to privacy_trial@inv.it.uc3m.es
WLAN address randomization tools developed and/or tested for 4 different OSes. Generate a local MAC address with 0x06 as first octet
  Apple Mac OS X (tested on v10.10, alias Yosemite)
  GNU Linux (tested on Debian testing/unstable, Ubuntu 13.10, and Fedora 20)
  Microsoft Windows (tested on Windows 7)
  Android (tested on Nexus 4 and Jelly Bean 4.2.2)
Use of DHCP client identifier for debugging
More info available at the trial Wiki page: http://goo.gl/eFUM9h
Notes: Note that we have tested the scripts in a limited

## Slide 6: Apple Mac OS X*
Command-based. Run on a terminal every time you want to connect to a WiFi Network:
Some parameters have to be properly filled in
  <WLANIFACE> name of wireless interface (e.g., en0)
  <ESSID> ieee802_privacy_trial
  <WiFi KEY> ieeeieee
  <PATH_TO_LOGFILE> path to a log file used to save the randomized MAC addresses used during the trial
*Tested on Mac OSX version 10.10 (MacBook 2014)
** Update: Working on OSX10.7.5 MacBook Air (2008) + Broadcom BMC43XX 1.0 WiFi and OSX10.9.5 MacBook Pro (2010) + Broadcom BMC43XX 1.0 WiFi. Not Working on OSX10.7.5 MacBook (2006) + Atheros 5416 WiFi and OSX10.7.5 MacBook Air (2008) + Broadcom BMC43XX 1.0 WiFi
MAC_ADDR=06:`openssl rand -hex 5 | sed 's/\(..\)/:\1/g;s/^.\(.\)[0-3]/\12/;s/^.\(.\)[4-7]/\16/; s/^.\(.\)[89ab]/\1a/;s/^.\(.\)[cdef]/\1e/'`; sudo ifconfig <WLANIFACE> ether $MAC_ADDR; networksetup -setairportnetwork <WLANIFACE> <ESSID> <WiFi KEY>; echo $MAC_ADDR >> <PATH_TO_LOGFILE>
More info available at the trial Wiki page: http://goo.gl/eFUM9h
Notes: OSX10.7.5 MacBook (2006) + Atheros 5416 WiFi: FAIL
Whilst the ifconfig command succeeds the new MAC address is only apparent in ifconfig - it does not change the actual WiFI MAC address used on the air. Furthermore the machine is unable to connect to any WiFI networks after the change - the networksetup command generates an error -3905 - normal operation is only resumed when the original MAC address is reassigned. A monitor mode Wireshark running on another machine confirms the fact that MAC address has not changed.
OSX10.7.5 MacBook Air (2008) + Broadcom BMC43XX 1.0 WiFi: FAIL
Whilst the ifconfig command apparently succeeds the new MAC address is not assigned to the interface neither as far as the ifconfig command shows nor from external Wireshark machine. There is no error indication as the ifconfig command quietly fails to change the MAC address.
OSX10.9.5 MacBook Pro (2010) + Broadcom BMC43XX 1.0 WiFi: SUCCESS
The script operates correctly and a monitor mode Wireshark running on another machine confirms the fact that MAC address has successfully changed.

## Slide 7: Linux**
Config file-based. Make Linux’s Network Manager automatically use a random local MAC address with any new WLAN connection
Makes use of the macchanger tool
Download provided script and copy it to /etc/NetworkManager/dispatcher.d/random_wlan_mac_06
  Some parameters have to be properly filled in
    <WLANIFACE> name of wireless interface (e.g., en0)
    <MACCHANGER> path to the macchanger tool
    <LOGFILE> path to file where logs will be saved
Additional script provided for periodic random address randomization while not connected and scanning
**Tested on Debian testing/unstable, Ubuntu 13.10*, Fedora 20 and Ubuntu 14.04.2 LTS.
More info available at the trial Wiki page: http://goo.gl/eFUM9h
Notes: Ubuntu 14.04.2 LTS: SUCCESS
The scripts operates fine - this machine runs without a GUI and network manager so it's less usual. Anyway a monitor mode Wireshark running on another machine confirms the fact that MAC address has successfully changed.

## Slide 8: Windows***
Script-based. Download New-MACaddress.ps1 script. Run on a console every time you want to configure a new local MAC address on a NIC
If there are multiple network interfaces (NIC) you will get a prompt asking for which card to change the MAC address
***Tested on Windows 7 (and PowerShell 2.0)
More info available at the trial Wiki page: http://goo.gl/eFUM9h
C:\TEMP> .\New-MACaddress.ps1 -Wireless

## Slide 9: Android****
Support is very much HW and Android version specific
The device has to be rooted
Makes use of the MAC Spoofer (changer) app
  Need to introduce the MAC address (use 0x06 as first octet)
****Tested on the following devices
  Nexus 4 (Jelly Bean 4.2.2): works OK
  Nexus 5 (CyanoGen12 Android 5.0.2)
    With open non-protected networks the user may need to re-connect manually after the spoof.
    With protected networks:
      De-activate WiFi.
      Use the spoofer to change MAC. The app will complain that the interface is down. Move on.
      Activate WiFi and connect.
      The interface uses the new MAC even if the interface settings may not display it.
More info available at the trial Wiki page: http://goo.gl/eFUM9h

## Slide 10: Next Steps
Run similar setup at IETF 92 meeting in Dallas, TX (March 22-27, 2015)
Compile data and draft a report
Publish/communicate results at both IEEE 802 and IETF committees
More info available at the trial Wiki page: http://goo.gl/eFUM9h